| Input Contribution |
| --- |
| Meeting ID* | ARC19 |
| Title:* | TR-0021 Referencing schema |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-08-29 |
| Document(s) Impacted* | TR-0021 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the texts into the TR if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 5.2	Referencing architecture

# Figure 5.2-1: Referencing Architecture

Step 1: The change of the Subject Resource matches the predefined filter conditions that an operation is triggering to be sent to the Object Resource to change the state of the Object Resource.

Step 2: Before the performing of operation, it is also needed to check if all the Dependency Conditions are met.

Step 3: If the Dependencies are met, as a part of the operation, the operation could need input parameters. The input parameter can be read from the Input Resource.

Step 4: Send the Operation to the Object Resource. The Operation could be Create, Retrieve, Update, Delete or Notify.

Step 5: After the performing of the operation, the state of the Object Resource is to be changed which could result in the switching of some device. In this case, the effect of the operation can be read from the Output Resource.

# Text boxes

Subject Resource

Object Resource

①

Input Resource

Dependencies

Output Resource

operation(CRUDN)

②

③

④

⑤