| Input Contribution |
| --- |
| Meeting ID* | ARC19 |
| Title:* | TR-0021 Major Compostion |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., yinjiaxin@huawei.com |
| Uploaded Date:* | 2015-08-29 |
| Document(s) Impacted* | TR-0021 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the texts into the TR if agreed. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6	Major composition parts to trigger an action

## 6.1	Subject Resource

## Subject Resource is the resource that is to be monitored. Action is to be triggered based on the change of the state of the Subject Resource. For example the temperature information that is created by the temperature sensor in the room.

## 6.2	Filter Condition

## When Subject Resource changes, Filter Condition need to be checked to see if the operation needs to be performed. Filter Condition is the policy defining if the change of the Subject Resource match the defined condition. For example, the Filter Condition is whether or not the temperature in the room is above 30 degrees. The Filter Condition could be semantic descriptions.

## 6.3	Object resource

## The Objective Resource is the resource to be changed by the action triggered pertaining to the change of the Subject Resource. Object Resouce is the target of the operation. For example the air-condition in the room. If the temperature rise above 30, the air-condition needs to be truned on.

## 6.4	Input Resource

## Before sending operation request to the Object Resource, the operation could need input parameter. The Input Resource is the resource where the input parameter is kept. For example, by turning on the air-condition, the temperature of the air-condition needs to be set to 25 degrees. In this case, the Input Resource would be 25 degrees.

## 6.5	Dependent Conditions

## Dependent Condition is the characteristic of the operation that when the operation needs to be performed, the dependent conditions has always need to be checked. The difference between Filter Condition and Dependent Condition is that Filter Condition applys to the Subject Resource but Dependent Condition applies to some external state. For example, when air-condition needs to be turned on and start to cooling the room, it is needed to check if all the room windows and doors are shut.

## 6.6	Definition of operation

## Operation is the action to be performed on the Object Resource. It could be the creation, update, retrieve, deletion or notify of the resource. For example, air-condition can be turned on by sending Create request.

## 6.7	Output Resource

## Output resource is the resource that can be used to check if the operation has been performed successfully. The resource is the output of the operation. For example, by turn on the air-condition, the output of the operation would be cooling of the room. As a result, the output can be checked through the monitoring of the temperature of the room.