| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19 |
| Source:* | InterDigital, NEC |
| Date:* | 2015-08-28 |
| Contact:* | Catalina Mladin, InterDigital, Catalina.Mladin@InterDigital.com Joerg Swetina, NEC, Joerg.Swetina@neclab.eu Qing Li, InterDigital, Qing.Li@InterDigital.com |
| Reason for Change/s:* | Introduce resource for operation modelling |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.3.0 |
| Clauses/Sub Clauses* | New 9.x.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This document presents two options:

- Option A organizes the inputs, outputs and state information in sub-resources

- Option B keeps everything at top level. This means that both inputs, outputs and state information is given via attributes

Hybrid options can also be envisioned

Remaining questions:

- Using <operation> for now, could be changed to a different term. The  problem with “operation” is that it is the term used in TS-0001 for CRUD

- Not sure if the repetition mode functionality enabled in mgmtCmd by attributes execMode, execFrequency, execDelay, execNumber is also desired for generic operations.

- What are the assumptions on allowed parent: AE only, or????

- What are the best levels to provide SemanticDescriptor, ontologyRef at? Some proposals are included.

- What types are needed for the containers/attributes capturing the state information? Same as for input/output, or can the types be restricted?

### -----------------------Start of change 1( option A) -------------------------------------------

### 9.x.x.	Resource Type operation

- The <operation> resource represents a method to model complex operations involving multiple CRUD requests and which may be used to trigger execution of commands with multiple inputs and outputs

- Figure: Structure of <operation> resource

- The execution of the command represented by <operation> shall be triggered using the UPDATE method to its attribute opEnable.

- For multiple requests of the same <operation> command, a child-resource (i.e. <operationInstance>) may be used to contain all execution instances.

- The <operation> resource shall contain the child resources specified in table

- Table: Child resources of <operation> resource

| Child Resources of <operation> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..1 |  |
| [variable] | <subscription> | 0..n |  |
| [variable] | <operationInstance> | 0..n |  |

- The <operation> resource shall contain the attributes specified in table.

- Table: Attributes of <operation> resource

| Attributes of <operation> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| description | 0..1 | RW | The text-format description of this resource. |
| processingType | 1 | WO | Type of processing to be applied when multiple instantiations of the operation are initiated, e.g. blocking (one instantiation pending at a time), non-blocking (multiple instantiations allowed) |
| maxNofInstantiations | 0..1 | WO | Maximum number of instantiations permitted to be enabled in parallel, for non-blocking operations |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that describes the operation |

### 9.x.x.	Resource Type operationInstance

- The <operationInstance> resource represents a successful instance of <operation> execution request, which had been triggered using the UPDATE method to the attribute opEnable of <operation> resource.

- Figure: Structure of <operationInstance> resource

- The <operationInstance> resource shall contain the child resources specified in table.

- Table: Child resources of <operationInstance> resource

| Child Resources of <operationInstance > | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..1 |  |
| [variable] | <subscription> | 0..n |  |
| [variable] | <opInstanceInputTarget> | 0..1 |  |
| [variable] | <opInstanceOutputTarget> | 0..1 |  |
| [variable] | <opInstanceStateTarget> | 0..1 |  |

- The <operationInstance> resource shall contain the attributes specified in table

- Table: Attributes of <operationInstance> resource

| Attributes of <operationInstance> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| execStatus | 1 | RO | The status of <operationInstance>. It can be Initiated, Started, Finished, Cancelled. |
| opEnableDisable | 1 | RW | The attribute is used to initiate or cancel the execution of <operationInstance> using UPDATE method. |

### 9.x.x.	Resource Type opInstanceInputTarget

- The <opInstanceInputTarget> resource provides links to all the necessary resources providing inputs for the execution of an operation instance.

- Figure: Structure of <opInstanceInputTarget > resource

- The <opInstanceInputTarget> resource shall contain the child resources specified in table.

- Table: Child resources of <opInstanceInputTarget> resource

| Child Resources of <operationInstance > | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..1 |  |
| [variable] | <subscription> | 0..n |  |

- The <opInstanceInputTarget> resource shall contain the attributes specified in table

- Table: Attributes of <opInstanceInputTarget> resource

| Attributes of <opInstanceInputTarget> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| nofInputs | 1 | RW | Number of resources with input information for the operation |
| inputContentInfo | 0..n | WO | This attribute specifies if inputContent is an URI to a resource providing the input, or if the input data is contained in inputContent attributes. If not specifying an URI, this attribute may provide additional information about the inputContent content type. In this case the attribute may be a composite attribute. It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content. Both elements of information are separated by a separator defined in oneM2M TS-0004 [i.2]. |
| inputContentSize | 0..n | RO | Size in bytes of the inputContent attribute. |
| inputContent | 0..n | RW | Depending on the inputContentInfo, this attribute may be: An URI of the target resource (container, contentInstance) with inputs for the execution of this operation instance. OR Actual input content, which may be opaque data or may be described and become understandable using contentInfo. |

### 9.x.x.	Resource Type opInstanceOutputTarget

- The <opInstanceOutputTarget> resource provides links to all the necessary resources for storing the outputs resulting from the execution of an operation instance.

- Figure: Structure of < opInstanceOutputTarget > resource

- Table: Child resources of <opInstanceOutputTarget> resource

| Child Resources of <operationInstance > | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..1 |  |
| [variable] | <subscription> | 0..n |  |

- The < opInstanceOutputTarget > resource shall contain the attributes specified in table

- Table: Attributes of <opInstanceOutputTarget> resource

| Attributes of <opInstanceOutputTarget> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| nofOutputs | 1 | RW | Number of resources with output information from the command |
| outputContentInfo | 0..n | WO | This attribute specifies if outputContent is an URI to a resource containing the operation output, or if the output data is contained in outputContent attributes If not specifying an URI, this attribute may provide additional information about the outputContent content type. In this case the attribute may be a composite attribute. It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content. Both elements of information are separated by a separator defined in oneM2M TS-0004 [i.2]. |
| outputContentSize | 0..n | RO | Size in bytes of the outputContent attribute. |
| outputContent | 0..n | RW | Depending on the outputContentInfo, this attribute may be: An URI of the target resource (container, contentInstance) with outputs resulting from the execution of this operation instance. OR Actual output content, which may be opaque data or may be described and become understandable using contentInfo. |

### 9.x.x.	Resource Type opInstanceStateTarget

- The <opInstanceStateTarget> resource provides links to all the necessary resources to store the state information associated with the execution of an operation instance.

- Figure: Structure of < opInstanceStateTarget > resource

- Table: Child resources of <opInstanceStateTarget> resource

| Child Resources of <operationInstance > | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..1 |  |
| [variable] | <subscription> | 0..n |  |

- The < opInstanceStateTarget > resource shall contain the attributes specified in table

- Table: Attributes of < opInstanceStateTarget> resource

| Attributes of <opInstanceStateTarget> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| nofStateAttributes | 1 | RW | Number of resources or attributes containing state information for the command |
| stateContentInfo | 0..n | WO | This attribute specifies if stateContent is an URI to a resource containing operation state information, or if the state information is contained in stateContent attributes |
| stateContentSize | 0..n | RO | Size in bytes of the stateContent attribute. |
| stateContent | 0..n | RW | Depending on the stateContentInfo, this attribute may be: An URI of the target resource (container, contentInstance) with state information of this operation instance. OR Actual state information, which may be opaque or may be described and become understandable using stateContentInfo. |

### -----------------------End of change 1 (option A) -------------------------------------------

### -----------------------Start of change 1( option B) -------------------------------------------

### 9.x.x.	Resource Type operation

- The <operation> resource represents a method to model complex operations involving multiple CRUD requests and which may be used to trigger execution of commands with multiple inputs and outputs

- Figure: Structure of <operation> resource

- The execution of the command represented by <operation> shall be triggered using the UPDATE method to its attribute opEnable.

- For multiple requests of the same <operation> command, a child-resource (i.e. <operationInstance>) may be used to contain all execution instances.

- The <operation> resource shall contain the child resources specified in table

- Table: Child resources of <operation> resource

| Child Resources of <operation> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..1 |  |
| [variable] | <subscription> | 0..n |  |
| [variable] | <operationInstance> | 0..n |  |

- The <operation> resource shall contain the attributes specified in table.

- Table: Attributes of <operation> resource

| Attributes of <operation> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| description | 0..1 | RW | The text-format description of this resource. |
| processingType | 1 | WO | Type of processing to be applied when multiple instantiations of the operation are initiated, e.g. blocking (one instantiation pending at a time), non-blocking (multiple instantiations allowed) |
| maxNofInstantiations | 0..1 | WO | Maximum number of instantiations permitted to be enabled in parallel, for non-blocking operations |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that describes the operation |

### 9.x.x.	Resource Type operationInstance

- The <operationInstance> resource represents a successful instance of <operation> execution request, which had been triggered using the UPDATE method to the attribute opEnable of <operation> resource.

- Figure: Structure of <operationInstance> resource

- The <operationInstance> resource shall contain the child resources specified in table.

- Table: Child resources of <operationInstance> resource

| Child Resources of <operationInstance > | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  |
| [variable] | <semanticDescriptor> | 0..1 |  |

- The <operationInstance> resource shall contain the attributes specified in table

- Table: Attributes of <operationInstance> resource

| Attributes of <operationInstance> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| execStatus | 1 | RO | The status of <operationInstance>. It can be Initiated, Started, Finished, Cancelled. |
| opEnableDisable | 0..1 | RW | The attribute is used to trigger or cancel execution of the <operationInstance> using UPDATE method. |
| nofInputs | 1 | RW | Number of resources with input information for the operation |
| inputContentInfo | 0..n | WO | This attribute specifies if inputContent is an URI to a resource providing the input, or if the input data is contained in inputContent attributes. If not specifying an URI, this attribute may provide additional information about the inputContent content type. In this case the attribute may be a composite attribute. It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content. Both elements of information are separated by a separator defined in oneM2M TS-0004 [i.2]. |
| inputContentSize | 0..n | RO | Size in bytes of the inputContent attribute. |
| inputContent | 0..n | RW | Depending on the inputContentInfo, this attribute may be: An URI of the target resource (container, contentInstance) with inputs for the execution of this operation instance. OR Actual input content, which may be opaque data or may be described and become understandable using contentInfo. |
| nofOutputs | 1 | RW | Number of resources with output information from the command |
| outputContentInfo | 0..n | WO | This attribute specifies if outputContent is an URI to a resource containing the operation output, or if the output data is contained in outputContent attributes If not specifying an URI, this attribute may provide additional information about the outputContent content type. In this case the attribute may be a composite attribute. It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content. Both elements of information are separated by a separator defined in oneM2M TS-0004 [i.2]. |
| outputContentSize | 0..n | RO | Size in bytes of the outputContent attribute. |
| outputContent | 0..n | RW | Depending on the outputContentInfo, this attribute may be: An URI of the target resource (container, contentInstance) with outputs resulting from the execution of this operation instance. OR Actual output content, which may be opaque data or may be described and become understandable using contentInfo. |
| nofStateAttributes | 1 | RW | Number of resources or attributes containing state information for the command |
| stateContentInfo | 0..n | WO | This attribute specifies if stateContent is an URI to a resource containing the operation output, or if the output data is contained in outputContent attributes If not specifying an URI, this attribute may provide additional information about the stateContent data type. |
| stateContentSize | 0..n | RO | Size in bytes of the stateContent attribute. |
| stateContent | 0..n | RW | Depending on the stateContentInfo, this attribute may be: An URI of the target resource (container, contentInstance) with outputs resulting from the execution of this operation instance. OR Actual state information, which may be opaque data or may be described and become understandable using stateContentInfo. |

### -----------------------End of change 1 (option B) -------------------------------------------