## Slide 1: Fuctional Architecture for oiC interworking
Group Name: Architecture WG
Source: Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com
Jieun Keum, Samsung Electronics, je.keum@samsung.com
Sung Chan Choi, KETI, csc@keti.re.kr
Seonhyang Kim, DT&C, shkim@dtnc.net
Bahareh Sadeghi, Intel, bahareh.sadeghi@intel.com
Lionel Florit, Cisco, lflorit@cisco.com
Meeting Date: <2015-09-07>
Agenda Item: <WI 44: oneM2M-OIC interworking >
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Basic Sketch
IPE in between
  which plays the role of both oneM2M & OIC entities.
Separation of OIC & oneM2M operation
  The intermediary interact with OIC (& oneM2M) devices with OIC (& oneM2M) procedures respectively.
oneM2M device
(controller)
① oneM2M REQ
OIC device
(sensor & actuator)
IPE
② OIC REQ
③ OIC RES
④ oneM2M RES
(virtual)
oneM2M device
(virtual)
OIC device
oneM2M & OIC resource translation

## Slide 3: Functional Architecture
Interworking with IPE
  IPE, as an intermediary, facilitates oneM2M & OIC interworking by translating oneM2M and OIC data/information model via oneM2M Mca and OIC interface.
Functional Entities
  IPE: a specialized AE, characterized by the support of a non-oneM2M reference point, and by the capability of remapping the related data model to the oneM2M resources exposed via the Mca reference point
  oneM2M CSE: oneM2M common service entity (CSE)
  OIC device: a logical entity which plays either OIC client or OIC server roles or both. OIC server hosts OIC resources and expose those for IoT service. OIC client accesses OIC server to manipulate OIC resources, i.e. monitoring & controlling
OIC device
oneM2M CSE
IPE
oneM2M AE
virtual OIC device
Mca
Reference Point
OIC
Interface

## Slide 4: oneM2M interworking with OIC via IPE
MN-CSE
OIC device
IPE
Gateway
IN-CSE
IN-AE
ASN-AE
ASN-CSE
ADN-AE
OIC
Interface
Mca
Mcc
Mca
Mcc
Mca
Mca
Deployment model based on Functional Architecture
  Main entities and their interworking via reference points.

## Slide 5: Interworking with IPE in detail
virtual OIC devices in IPE
  Replicating virtual OIC device in IPE with OIC procedures.
  Binding two devices such that they are synchronized, i.e. the same resource representations
virtual oneM2M devices in IPE
  Mirroring virtual OIC device to virtual oneM2M device by resource mapping.
  oneM2M service by manipulating virtual oneM2M device, which will reflected in the virtual & original OIC devices.
IPE
vOIC device
/oic/res
/oic/d
/lightSwitch
CSE
/oic/res
/oic/d
/myLight
/lightSwitch
Mirroring oneM2M & OIC devices
OIC device
/oic/res
/oic/d
/lightSwitch
Sync OIC devices via OIC interfaces
oneM2M services with oneM2M interfaces
CSE (AE)
/oic/res
/oic/d
/myLight
/lightSwitch

## Slide 6: Operation procedures
(virtual) OIC device replication
  replicating OIC device in IPE as (virtual) OIC device
    With synchronization binding by OIC discovery procedures.
(virtual) oneM2M device translation
  mirroring OIC device into (virtual) oneM2M device.
    With proxying & translating
oneM2M registration & discovery
  registering (virtual) oneM2M device to suitable CSE for discovery
oneM2M monitoring & controlling
  oneM2M controller interacts with (virtual) oneM2M devices
oneM2M & OIC resource translation
  Translating oneM2M & OIC resources to synchronize virtual devices state
OIC synchronization
  Synchronizing virtual OIC device & OIC device
    With OIC Request & response via synchronization binding.
Initial preparation
Actual monitoring & controlling

## Slide 7: Appendix- (virtual) OIC device replication
Overview
  replicating OIC device in IPE as (virtual) OIC device, (IPE as OIC server (?) )
  ensuring two OIC devices to be synchronized, i.e. having the same resource representation
Procedures
  Using OIC discovery to acquire the OIC device information
    GET to /oic/res (from IPE)
    POST to /factoryResource (from OIC device)
  Establishing the relationship between two OIC devices .
    Link with “binding” relationship
OIC device
IPE
/oic/res
/oic/d
/lightSwitch
GET /oic/res
Response
OIC Client
GET /oic/d
Response
GET /lightSwitch
Response
vOIC device
/oic/res
/oic/d
/lightSwitch
Bind
Bind
Bind
Bind
Bind
Bind