| Input Contribution |
| --- |
| Meeting ID* | ARC #19 |
| Title:* | Functional Architecture for oneM2M – OIC interworking |
| Source:* | Jinhyeock Choi,Samsung Electronics, jinchoe@samsung.com Jieun Keum, Samsung Electronics, je.keum@samsung.com Sung Chan Choi, KETI, csc@keti.re.kr Seonhyang Kim, DT&C, shkim@dtnc.net Bahareh Sadeghi, Intel, bahareh.sadeghi@intel.com Lionel Florit, Cisco, lflorit@cisco.com |
| Uploaded Date:* | 2015-08-31 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This input contribution propose an architecture scheme for oneM2M- OIC interworking

================ Start or Text Proposal 1 ======================

# 3	Definitions, symbols and abbreviations

OIC device : a logical entity which plays either OIC client or OIC server roles or both. OIC server hosts OIC resources and expose those for IoT service. OIC client accesses OIC server to manipulate OIC resources, i.e. monitoring & controlling

virtual OIC device : A representation of OIC device on IPE.

================ Start or Text Proposal2=======================

# 7.	Possible Solutions for oneM2M and OIC Interworking

This section presents tentative solutions for oneM2M and OIC interworking and provides 1) Functional architecture and 2) Operation procedures. The first presents the interworking principle with main entities. The second describes the operation procedures, i.e. interaction between main entities. This functional architecture can address all scenarios from clause 6 where OIC devices are controlled by the oneM2M system.

## 7.1.	Functional Architecture for Interworking

OIC interworking scheme is based on Interworking Proxy Entity (IPE), which, as an intermediary, facilitates oneM2M & OIC interworking by translating oneM2M and OIC resources. IPE interacts with OIC devices and expose those as virtual oneM2M devices, i.e. oneM2M resources. oneM2M CSE accesses IPE via oneM2M interface to manipulate virtual oneM2M devices, then the resulting representation change is reflected to the corresponding OIC devices via OIC interface.

Figure 7-1 Functional Architecture with IPE

The main entities and their characteristics are as below.

- IPE : a specialized AE, characterized by the support of a non-oneM2M reference point, and by the capability of remapping the related data model to the oneM2M resources exposed via the Mca reference point

- oneM2M CSE :  oneM2M common service entity (CSE)

- OIC device : a logical entity which plays either OIC client or OIC server roles or both. OIC server hosts OIC resources and expose those for IoT service. OIC client accesses OIC server to manipulate OIC resources, i.e. monitoring & controlling.

The figure 7-2 demonstrates a possible deployment model which describes the main entities and their Main entities and their interworking via reference points.

Figure 7-2	Deployment model based on functional architecture

## 7.2.	Interworking with IPE

Conceptually IPE performs 3 functions. First IPE interacts with OIC devices to retrieve the OIC resource. Second IPE translates OIC resources to oneM2M resources and vice versa. Third IPE exposes those  a virtual OIC device   into oneM2M system We summarize those functions as below.

- virtual OIC device in IPE: IPE performs OIC procedures (e.g. discovery or registration) to replicate (virtual) OIC device in itselt. The original and the virtual OIC device are bound such that they are synchronized, i.e. they have the same resource representation. A change in representation in one device is reflected in the other and vice versa.

- oneM2M AE in IPE: IPE mirrors the virtual OIC device into a virtual oneM2M AE by resource mapping.

- oneM2M service with oneM2M AE : IPE exposes  oneM2M AEs for IoT services via Mca  interfaces. oneM2M application access a oneM2M AE through the connected CSE in between and manipulate its resources (e.g. controlling & monitoring). The resulting representation change is reflected to the virtual OIC device via intra IPE translation, then the original device is synchronized by binding.

Figure 7-3	IPE functions with resource translation

================ End or Text Proposal 1 =====================