| Input Contribution |
| --- |
| Meeting ID* | ARC19.0 |
| Title:* | Introduction to OIC Technology |
| Source:* | Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com Jieun Keum, Samsung Electronics, je.keum@samsung.com |
| Uploaded Date:* | 2015-09-10 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# ================ Start of Text Proposal 1 =======================

## 2.2	Informative references

[i.2] 	OIC Core Framework (http://openinterconnect.org/developer-resources/specs/)

[i.3]	OIC Remote Access (http://openinterconnect.org/developer-resources/specs/)

================ End of Text Proposal 1 =====================

# ================ Start of Text Proposal 2 =======================

## 3.3	Abbreviations

## RAE – Remote Access Endpoint

## For further list of abbreviations refer the OIC specifications [i.2] and [i.3]

================ End of Text Proposal 2 =====================

# ================ Start of Text Proposal 3 =======================

## 5.1	Introduction to OIC technology

This section describes the introduction to OIC as basic information for comparision between oneM2M and OIC. More details of OIC is described in [i.2]

### 5.1.1 Design Principle

The main objective of OIC is to create an interoperable framework for interaction between devices within local network and remote network. In OIC architecture, entities in physical world for e.g. bulb are represented as resources with their unique URIs and supported interfaces that enable RESTful operations on these resources. OIC defines the notion of a roles for devices. A device having Client role initiates a RESTful operation with a device having Server role which responds to the operation. The interaction between OIC Client and Server are depicted as in the figure 1.

Figure 1: OIC Architectural Interaction

### 5.1.2 System Architecture

#### 5.1.2.1 Network Architecture

OIC System is a network of devices connected peer to peer or via an infrastructure device. Devices in an OIC network can play the role of an OIC Client or an OIC Server or both. Figure 2 represents an OIC network with peer to peer connected devices.

Figure 2: OIC Network

#### 5.1.2.2 Device Architecture (Functional Block Diagram)

OIC Device architecture encompasses the functionality required for OIC operations. Figure 3 below depicts the same. L2 connectivity includes various connectivity like Wi-Fi, BT etc. Network could be either IPv4 or IPv6 based. Transport uses either UDP or TCP. OIC framework provides the core functions needed by an OIC device for e.g. discovery etc. The application profiles are specific to a domain of operation for e.g. Smart Home.

Figure 3: Functional Block Diagram

### 5.1.3 OIC Remote Access

#### 5.1.3.1 Philosophy

OIC Remote Access is accomplished using XMPP and ICE standards. XMPP Clients in an OIC network interact with XMPP server hosted in the cloud. XMPP clients are configured with an address and account of the XMPP server. XMPP server maintains account information and account policies. The XMPP stanzas (messages) exchanged between XMPP server and XMPP Client includes OIC CoAP messages in its payload. The receiving end decodes it and retrieves the message. For Peer to Peer communication ICE standard is proposed which will be fully specified in later releases.

#### 5.1.3.2 Architecture

Figure below shows the OIC Remote Access Architecture with one XMPP server.

Figure 4: OIC Remote Access Architecture

RAE Server is an OIC Server with XMPP client functionality. RAE client is also an XMPP client. Both RAE Server and RAE client are configured with the details of XMPP server. OIC devices are associated with a full JID using which they login to the XMPP server and get authenticated. After this they can know the presence status of other devices and can connect with each other and exchange XMPP stanzas (messages).

More details of OIC Remote Access are described in [i.3]

Sleeping devices are handled using Resource Directory. For details please refer [i.2]

Editors Note: OIC Security details to be submitted in a separate contribution

================ End of Text Proposal 3 =====================