| Input Contribution |
| --- |
| Meeting ID* | ARC19.0 |
| Title:* | Technical comparison of oneM2M and OIC in Clause5.2 |
| Source:* | Sung-Chan Choi, Jaeho Kim, Minu Ryu KETI (TTA), csc@keti.re.kr Jieun Keum, Samsung Electronics, je.keum@samsung.com Seonhyang Kim, DT&C, shkim@dtnc.net Bahareh Sadeghi, Intel, bahareh.sadeghi@intel.com Lionel Florit, Cisco, lflorit@cisco.com |
| Uploaded Date:* | 2015-09-07 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is based on ARC-2015-2138-oneM2M-OIC_Interworking_Technical_Comparison. The proposed text will be included in Clause5.2 in TR0024 for the technical comparison between oneM2M and OIC from the perspective of Resource representation and Communication model.

================ Start or Text Proposal 1 =======================

# 5	Technical Comparison of oneM2M and OIC

This clause will include the introduction of OIC technology and  the comparison between oneM2M and OIC technology.

## 5.2        Technical Comparison

This clause describes the technical comparison of oneM2M and OIC. Both oneM2M and OIC adopt ROA(Resource Oriented Architecture) design principles which expose their functionalities by means of  resoruces and manipulated with RESTful APIs. However, There are some points of comparison between oneM2M and OIC from the perspective of resource representation and communication model.

### 5.2.1	Resource Representation

The table 5.2.1-1 demonstrates the comparison between oneM2M and OIC with respect to resource representation.

Table 5.2.1-1	The Comparison of Resource Representation of oneM2M and OIC System

|  | oneM2M | OIC |
| --- | --- | --- |
| Functionality exposed by Resources | oneM2M defines common M2M services which can be used for any vertical application service domains. oneM2M common services are exposed via oneM2M defined resource types which comprises of <container>, <group>, <locationPolicy>, <subscription>, <request>, <delivery> etc. Based on the device capability, oneM2M entity can be represented as CSE or AE. oneM2M resource model provides common service layer level interoperability. | OIC represents an entity of the physical world as a OIC device (e.g. temperature, an electric light or a home applicance) using resource model. OIC device includes the base/core functionality and device specific functionality which is represented by OIC defined resource types. OIC resource model provides application profile level interoperability among OIC Devices. |
| Resource Structure | Hierarchical resource structure <CSEBase> represents the oneM2M CSE and is the the root for all the resources. oneM2M resources have a parent-child relationships. Each resource in oneM2M entity can be accessed via both structured (hierarchical) URI as well as un-structured (flat) URI. | Flat resource structure OIC device consists of core resource and device specific resource. Core resource has pre-defined resource name which can be accessed via fixed URI Device specific resource has variable resource name and represents device specific functionality (e.g. binary switch, brightness etc.) |

Assuming a light bulb shall be modelled as oneM2M device or OIC device in each domain, the table 5.2.1-2 and 5.2.1-3 show examples about oneM2M and OIC resource representation respectively.

Table 5.2.1-2 oneM2M <AE> resource (XSD example)

<xs:schema xmlns=http://www.w3.org/2001/XMLSchema targetNamespace="http://www.onem2m.org/xml/protocols" xmlns:m2m=http://www.onem2m.org/xml/protocols xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema"> <xs:element name="AE"> <xs:complexType> <xs:complexContent> <!-- Inherit common attributes for announceable Resources --> <xs:extension base="m2m:announceableResource"> <xs:sequence> <!-- Resource Specific Attributes --> <xs:element name="appName" type="xs:string" minOccurs="0" /> <xs:element name="App-ID" type="xs:string" /> <xs:element name="AE-ID" type="m2m:ID" /> <xs:element name="pointOfAccess" type="m2m:poaList" minOccurs="0" /> <xs:element name="ontologyRef" type="xs:anyURI" minOccurs="0" /> <xs:element name="nodeLink" type="xs:anyURI" minOccurs="0" /> <xs:element name="requestReachability" type="xs:boolean" /> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" /> <xs:choice minOccurs="1" maxOccurs="unbounded"> <xs:element ref="m2m:container" /> <xs:element ref="m2m:group" /> <xs:element ref="m2m:accessControlPolicy" /> <xs:element ref="m2m:subscription" /> <xs:element ref="m2m:pollingChannel" /> <xs:element ref="m2m:schedule" /> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> </xs:schema>

Table 5.2.1-3	OIC light device resource (JSON example)

[{ "di": "example_device_id", "links": [ { "href": "/oic/d", "rt": "oic.d.light", "if": "oic.if.r", "rel": "hosts"}, { "href": "/myLightSwitch", "rt": "oic.r.switch.binary", "if": "oic.if.a", "rel": "hosts"}, { "href": "/myLightBrigtness", "rt": "oic.r.light.brightness", "if": "oic.if.a", "rel": "hosts"} ] }] { "n": "myRoomLightDevice", "rt": “oic.d.light", "if": "oic.if.r", “di": "example_device_id“, "icv": "oic.1.5" } { "n": MyRoomLightSwitch", "rt": "oic.r.switch.binary", "if": "oic.if.a", "id": "b.switch_TF38_3", "value": "true" } { "n": MyRoomLightBrightness", "rt": "oic.r.light.brightness", "if": "oic.if.a", "id": “light_brightenss_TF38_3", "value": 30 }

### 5.2.2	Communication Model

The table 5.2.1-1 demonstrates the comparison between oneM2M and OIC with respect to communication model.

Table 5.2.2-1 The Comparison of Communication Model of oneM2M and OIC System

|  | oneM2M | OIC |
| --- | --- | --- |
| Communication Model | Request-Response communication model (Originator-Receiver) In order to use M2M services, each entity in oneM2M shall perform registration procedure which establishes a relationship between CSEs/AE allowing them to exchange information. Request message flow occurs from the Originator CSE to the Hosting CSE which generates Hop-by-Hop data delivery. Registree-Registrar relationship produces routing path when transferring messages. Blocking vs. non-Blocking supported | Peer-to-Peer communication model (Server-Client) OIC client accesses a resource provided by an OIC server. OIC client is the initiator of request. OIC server exposes resources to OIC client. OIC server is the recipient of the requests and is responsible for processing and responding to the request. OIC client and OIC server directly communicate without involvement of any other OIC entity. OIC supports remote access from WAN to LAN via connection broker server. |

The figure 5.2.2-1 and figure 5.2.2-2 illustrate message delivery in each oneM2M and OIC system and show comparison between oneM2M and OIC system communication model.

Figure 5.2.2-1	oneM2M Reqeust-Response communication model (Multi-Hop)

Figure 5.2.2-2 OIC Peer-to-Peer communication model

================ End or Text Proposal 1 =====================