## Slide 1: OIC INTERWORKING Operational Procedure (addressing and Discovery)
Group Name: Architecture WG
Source: Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com
Jieun Keum, Samsung Electronics, je.keum@samsung.com
Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com
Sungchan Choi, KETI, sungchan.keti@gmail.com
SeonHyang Kim, DT&C, shkim@dtnc.net
Meeting Date: <2015-10-20>
Agenda Item: <WI 44: oneM2M-OIC interworking >
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
This presentation introduces possible initialization setup of different entities for oneM2M OIC Interworking
Also details of how oneM2M device can discover OIC entities is depicted. There can be 2 alternatives
  Request-response Mode
  Notification Mode
Also how entities are addressed is described

## Slide 3: Initialization of Entities
The IN supports a CSE. An AE (Smartphone) is registered to the IN CSE
Similarly MN supports a CSE. IN CSE also registers with MN CSE
Intermediary Device is installed with an IPE based on an out of band mechanism
  Triggered by a user action e.g. user subscribing to some service or
  Based on business logic of service provider

## Slide 4: Discovery (Request-response Mode)
The IPE AE discovers OIC devices using its OIC Client functionality as soon as it is installed on MN. It uses OIC mechanisms for the discovery
After the discovery, IPE AE uses its IWK (Interworking) function to map the discovered OIC devices and resources into oneM2M resources and creates them on MN
For each discovered OIC Device an OIC AE is created and registered with MN CSE
(4.0/ 4.1) After that an AE through an IN CSE can anytime discover OIC AE resources by sending a RETRIEVE REQ with appropriate filter criteria to the MN CSE where they are registered
(5.0/5.1) The MN CSE sends a RETRIEVE RES to IN CSE with the OIC AE’s information which in turn is sent to the AE

## Slide 5: Discovery (Notification Mode)
(1.0/1.1) AE subscribes to IN CSE for any changes in registered AE’s on MN CSE. This request is forwarded to MN CSE
The IPE AE discovers OIC devices using its OIC Client functionality as soon as it is installed on MN. It uses OIC mechanisms for the discovery
After the discovery, IPE AE uses its IWK (Interworking) function to map the discovered OIC devices and resources into oneM2M resources and creates them on MN
For each discovered OIC Device an OIC AE is created and registered with MN CSE
(5.0/5.1) IN CSE and In-Turn AE is notified of the newly registered AE’s based on the earlier subscription

## Slide 6: Addressing
The “To” parameter in a request/ notification is used as a target for the request/ notification
Resource-ID: The originator of the request is recommended to use “Absolute” or “SP-relative” format of addressing when sending requests. This is just to ensure that the MN-CSE hosting OIC AE resources receives the request
Request Target
  Requests are targeted to AEs but via CSE which hosts them
  The MN CSE-PoA is used by IN to reach the CSE which is hosting the OIC AE resource
  Specific AE under the MN CSE is addressed using the AE-ID attribute of the <AE>
Notification Target
  Notifications are usually targeted to AEs
  A hosting CSE which receives notification request, can retarget the request to AE-PoA