| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19.3 |
| Source:* | Samsung Electronics |
| Date:* | 2015-10-20 |
| Contact:* | Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com Jieun Keum, Samsung Electronics, je.keum@samsung.com Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com Sungchan Choi, KETI, sungchan.keti@gmail.com SeonHyang Kim, DT&C, shkim@dtnc.net |
| Reason for Change/s:* | This introduces the OIC interworking procedure for subscription and notification. |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <WI-0044> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0023 v0.1.0 |
| Clauses/Sub Clauses* | 7 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contirubtion includes possible interworking procedure of Subscription and Notification for oneM2M OIC Interworking. This consists of three inteworkin procedure such as susbscription, notification and cancel of subscription.

### -----------------------Start of change 1-------------------------------------------

## 7.4.x  Subscription & Notification interworking Procedure

oneM2M Subscription and Notification function can be mapped to OIC oberve mechanism which utilizes the RETRIEVE operation to require the OIC Device for updates in case of OIC Resource state changes[i.2]. The privilege checking process for subscription and observation should be done at oneM2M side as well as OIC side.

## 7.4.x.1 Interworking Procedure for Subscription

This clause describes the interworking procedure when IN-CES Requests to get notification on the change of the OIC corresponding resources.

- IN-CSE send CREATE Request of  <subscription> target to a <container> corresponds to OIC Device.

- Map <subscription> to OIC  observe RETRIEVE Request message with observe indication

- URI of the <container> can be mapped to to parameter of OIC RETRIEVE Request message

- OIC client URI in Gateway can be mapped to  fr parameter of OIC RETRIVE Request message

- Resource ID in <subscription> can be mapped to ri parameter of OIC RETRIVE Request message

- OIC Client send OIC RETRIEVE Request message to OIC Device

- OIC Device send OIC RETRIEVE Response message to OIC Client

- IPE Transform to oneM2M  CREATE Response message

- cn of OIC RETRIEVE message  can be mapped to content parameter of oneM2M CREATE Response message

- MN-CSE send CREATE Response message to IN-CSE

## 7.4.x.2 Interworking Procedure for Notification

This clause describes the interworking procedure when OIC resource change notify to oneM2M subscriber(ex, IN-CES) of the subscription.

- OIC Device send OIC RETRIEVE Response message to OIC Client with the modified resource representation

- IPE Transform to oneM2M NOTIFY  Request message

  - cn of OIC RETRIEVE message  can be mapped to content parameter of oneM2M NOTIFY Request message

- MN- CSE send oneM2M NOTIFY Request message

- IN- CSE send oneM2M NOTIFY Response message

## 7.4.x.3 Interworking Procedure for cancel of Subscription

This clause describes the interworking procedure when IN-CES Requests to cancel the subscription.

- IN-CSE send DELETE Request of <subscription> resource.

- IPE transform to OIC RETRIEVE Request message without observe indication

- OIC Client send OIC RETRIEVE Request message without observation indication to OIC Device

- OIC Device send OIC RETRIEVE Response message

- IPE transform to DELETE Response message.

- MN-CSE send DELETE Response message

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?