| Input Contribution |
| --- |
| Meeting ID* | ARC19.3 |
| Title:* | OIC Interworking procedure for subscription and notification |
| Source:* | Jieun Keum, Samsung Electronics, je.keum@samsung.com Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com Sungchan Choi, KETI, sungchan.keti@gmail.com SeonHyang Kim, DT&C, shkim@dtnc.net |
| Uploaded Date:* | 2015-10-20 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.1.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution includes possible interworking procedure of Subscription and Notification for oneM2M OIC Interworking. This consists of three inteworking procedures such as susbscription, notification and cancel of subscription.

================ Start of Text Proposal 1 =====================

## 7.4.x  Subscription & Notification Interworking Procedure

oneM2M Subscription and Notification function can be mapped to OIC oberve mechanism which utilizes the RETRIEVE operation to require the OIC Device for updates in case of OIC Resource state changes[i.2]. The privilege checking process for subscription and observation should be done at oneM2M side as well as OIC side.

## 7.4.x.1 Interworking Procedure for Subscription

This clause describes the interworking procedure when IN-CES Requests to get notification on the change of the OIC corresponding resources.

- Assume that IPE already subscribe to <container> resource  at CES for notifying of creating request of <subscription>

- IN-CSE CREATE Request of  <subscription> resource targeting to the <container> resource under OIC AE

- MN-CSE send CREATE Response message to IN CSE

- CSE send Notify message to IPE of creating <subscription>

- OIC Client send OIC Retrieve Request message to OIC Device

- OIC Device send OIC Retrieve Response message to OIC Client

## 7.4.x.2 Interworking Procedure for Notification

This clause describes the interworking procedure when OIC resource change notify to oneM2M subscriber(ex, IN-CES) of the subscription.

- OIC Device send OIC Retrieve Response message to OIC Client with the modified resource representation

- IPE send oneM2M UPDATE message to MN-CSE

- MN- CSE send oneM2M NOTIFY request message

- IN- CSE send oneM2M NOTIFY response message

## 7.4.x.3 Interworking Procedure for Canceling the Subscription

This clause describes the interworking procedure when IN-CES Requests to cancel the subscription.

- Assume that IPE already subscribe to container resource hosted at CES for notifying of DELETE request of <subscription>

- IN-CSE send DELETE request of <subscription> resource.

- MN-CSE send DELETE response message

- CES notify to IPE the DELETE of <subscription>

- OIC Client send OIC Retrieve request message without observation indication to OIC Device

- OIC Device send OIC Retrieve response message

================ End of Text Proposal 1 =====================