## Slide 1: OIC Interworking Operation Procedure for Subscription & Notification
Group Name: Architecture WG
Source: Jieun Keum, Samsung Electronics, je.keum@samsung.com
Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com
Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com
Sungchan Choi, KETI, sungchan.keti@gmail.com
SeonHyang Kim, DT&C, shkim@dtnc.net
Meeting Date: <2015-10-20>
Agenda Item: <WI 44: oneM2M-OIC interworking >
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
This presentation introduces possible interworking procedure of Subscription and Notification for oneM2M OIC Interworking

## Slide 3: General principle
oneM2M Subscription and Notification function can be mapped to OIC observe scheme.
In observe mechanism the OIC Client utilizes the RETRIEVE operation to require the OIC Server for updates in case of OIC Resource state changes
<OIC operation for observe mechanism>

## Slide 4: Subscription
Create <subscription> targeting <container> under OIC AE
Map <subscription> to OIC observe Retrieve request message with observe indication
  Corresponding URI of the <container> can be mapped to to parameter of OIC RETRIVE message
  OIC client URI in Intermediary can be mapped to fr parameter of OIC RETRIVE message
  Resource ID in <subscription> can be mapped to ri parameter of OIC RETRIVE message
OIC Client send OIC Retrieve Request message to OIC Device
OIC Device send OIC Retrieve Response message to OIC Client
Transform to oneM2M Create RESPONSE message
  cn of OIC retrieve message can be mapped to content parameter of oneM2M CREATE RESPONSE message
MN CSE send Create RESPONSE message to IN CSE

## Slide 5: Notification
OIC Device send OIC Retrieve Response message to OIC Client with modified resource representation
Transform to oneM2M NOTIFY Request message
  cn of OIC retrieve message can be mapped to content parameter of oneM2M NOTIFY request message
MN- CSE Send oneM2M NOTIFY request message
IN- CSE send oneM2M NOTIFY response message

## Slide 6: Cancel of Subscription
IN-CSE send Delete request of <subscription> resource.
IPE transform to OIC Retrieve request message without observe indication
OIC Client send OIC Retrieve request message without observation indication to OIC Device
OIC Device send OIC Retrieve response message
IPE transform to DELETE response message.
MN-CSE send DELETE response message