| Input Contribution |
| --- |
| Meeting ID* | ARC#19.4 |
| Title:* | oneM2M-AllJoyn interworking clause 5 – architecture model |
| Source:* | LG Electronics, SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Uploaded Date:* | 2015-10-27 |
| Document(s) Impacted* | TS-0021 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## ----------------------- Start of text 1 -----------------------

# 5	Architecture Model

## 5.1	Reference model

The architecture model followed in the present document is based on the architecture model in Annex F of TS-0001 [1] that describes how interworking between oneM2M CSEs and non-oneM2M systems using specialized Interworking Proxy application Entities (IPE). The present document descibes the AllJoyn IPE that supports the following reference model:

Figure 5.1-1 AllJoyn interworking reference model

This reference model describes how the oneM2M AEs can interwork with AllJoyn services provided by AllJoyn provider applications. By the IPE, AllJoyn services are exposed as oneM2M resources and stored in MN-CSE. AEs access exposed AllJoyn service resources by oneM2M APIs.

Note that this figure does not exclude the interworking scenario via Mcc’ reference point.

Editor’s Note: interworking over Mcc’ reference point is FFS.

## 5.2	Composition of the IPE

The AllJoyn IPE mainly consists of MN-AE and AllJoyn consumer application. IPE, optionally, can have AllJoyn router and this is implementation specific. IPE is registered to MN-CSE to interwork in oneM2M systems and communicate with other AllJoyn applications using AllJoyn protocols. IPE registration is mandatory which is not defined in AllJoyn system. Discovery and session establishment is needed for IPE to communicate with other AllJoyn applications.

## ----------------------- End of text 1 -----------------------

# Text boxes

MN-CSE

AllJoyn protocol

IPE (AllJoyn consumer Application)

Mca

IN-AE / ADN-AE

Mca

IN-CSE

Mcc

AllJoyn Producer Application

AllJoyn Provider Application

Mcc

ASN-CSE

ADN-AE

ASN-AE

Mca

Mca