| Input Contribution |
| --- |
| Meeting ID* | ARC#19.4 |
| Title:* | oneM2M-AllJoyn interworking clause 5 – architecture model |
| Source:* | LG Electronics, SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Uploaded Date:* | 2015-10-27 |
| Document(s) Impacted* | TS-0021 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## ----------------------- Start of text 1 -----------------------

# 5	Architecture Model

## 5.1	Reference model

The architecture model followed in the present document is based on the architecture model in Annex F of TS-0001 [1] that describes how interworking between oneM2M CSEs and non-oneM2M systems using specialized Interworking Proxy application Entities (IPE). The present document descibes the AllJoyn IPE that supports the following reference model:

Figure 5.1-1 AllJoyn interworking reference model

This reference model describes how the oneM2M AEs can interwork with AllJoyn  applications. By the IPE, AllJoyn services are exposed as oneM2M resources and stored in MN-CSE. AEs access the exposed AllJoyn service resources by the oneM2M APIs.

Note that this figure does not exclude the interworking scenario via Mcc’ reference point.

Editor’s Note: interworking over Mcc’ reference point is FFS.

## 5.2	Composition of the IPE

The AllJoyn IPE mainly consists of MN-AE and AllJoyn application. To provide the interworking functions to other oneM2M entities, the IPE registers to MN-CSE and communicate with other AllJoyn applications using AllJoyn protocols. The IPE registration is mandatory in oneM2M systems which is not defined in AllJoyn system. AllJoyn discovery and session establishment are needed for the IPE to communicate with other AllJoyn applications.

## ----------------------- End of text 1 -----------------------

# Text boxes

MN-CSE

AllJoyn protocol

IPE (AllJoyn Application)

Mca

IN-AE / ADN-AE

Mca

IN-CSE

Mcc

AllJoyn Producer Application

AllJoyn Application

Mcc

ASN-CSE

ADN-AE

ASN-AE

Mca

Mca