| Input Contribution |
| --- |
| Meeting ID* | ARC 19.4 |
| Title:* | OIC Interworking procedure for device management |
| Source:* | Sungchan Choi, KETI, csc@keti.re.kr Jieun Keum, Samsung Electronics, je.keum@samsung.com Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com SeonHyang Kim, DT&C, shkim@dtnc.net |
| Uploaded Date:* | 2015-11-02 |
| Document(s) Impacted* | WI-0044 OIC-Interworking TR-0023 v0.1.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed text into TR-0023 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution includes possible interworking procedure for OIC device management with oneM2M OIC Interworking. This consists of  introduction of OIC device management and oneM2M interworking procedure with OIC for device management.

================ Start of Text Proposal 1 =====================

## 7.5.x  OIC Device Management Interworking Procedure

The OIC Device Management includes the following functions: Monitoring, Diagnostics and maintenance  [i.2].

Monitoring in OIC is used for monitoring the current state of the OIC devices, to check their functionality state and to ensure the OIC device is operating as expected. The feature supported by the OIC core resource ‘oic/mon’ as follows:

- Availability: Indicate if the device is available or not

- Lasted Acted Time: Indicate the elapsed time in seconds after the device acted upon

- Device Statistics: Contain information about number of received packets and sent packets etc.

Diagnostics and Maintenance in OIC is used by the administrators to resolve issue encountered with the OIC devices while operating in the field. This feature is supported by using the OIC core resource ‘oic/mnt’. The following commands can be executed for the diagnostics and maintenance for the OIC devices.

- Factory reset: Updates the device configuration to its original state

- Reboot: Triggers a soft reboot of an OIC device

- Statisics collection: Triggers collection and logging information for diagnostic purposes

For interworking between OIC and oneM2M, the OIC device management resources regarding ‘oic/mon’ and ‘oic/mnt’can be mapped to oneM2M <container> and <contentInstance>. OIC device management resources can be exposed via <container> and <contentInstance> oneM2M resource and then oneM2M AE can access these resources for triggering OIC device management from oneM2M side.

NOTE: Mapping principles of the OIC Device management information into oneM2M resource and Procedure will be more specified in the OIC interworking TS.

## 7.5.x.1 Interworking Procedure for OIC monitoring

This clause describes the interworking procedure for reteiving OIC monitoring resource which are already mapped to oneM2M <container> and <contentInstance> resources in MN-CSE.

In order to synchronize ‘oic/mon’ resource in OIC device with the <conainter>, <contentInstance> in MN-CSE via IPE function, we assume these steps are performed.

- OIC client in IPE sends “RETRIEVE Request” message to the OIC device in Legacy OIC domain.

- OIC device responds to the request message with the “/oic/mon” resource.

- Based on the response message, IPE sends oneM2M resource CREATE request to the MN-CSE (conainer, contentInstance)

- MN-CSE sends oneM2M resource CREATE response to the IPE

For OIC device monitoring from oneM2M AE, we follow these steps.

- IN-AE sends <contentInstance> RETRIVE request to the MN-CSE via IN-CSE

- MN-CSE sends <contentInstance> RETRIVE response to the IN-AE via IN-CSE

## 7.5.x.2 Interworking Procedure for OIC diagnostics and maintenance

This clause describes the interworking procedure for triggering OIC diagnostics and maintenance from oneM2M IN-AE.

Precondition:  ‘oic/mnt’ resource in OIC device was synchronized with <container>, <contentInstance> in MN-CSE and based on following procecure, we assume IPE creates subscription resource under the <container> reouce in MN-CSE with setting its IPE address as notificationURI.

- IPE sends <subscription> CREATE request to the MN-CSE in order to receive notification message  (Related eventType is a direct child resource creation)

- MN-CSE sends <subscription> CREATE response to the IPE

For triggering OIC device diagnostics and maintenance from oneM2M AE, we follow these steps.

- IN-AE sends <contentInstance> CREATE request to the MN-CSE via IN-CSE

- MN-CSE sends CREATE response to the IN-AE via IN-CSE

- <contentInstance> creation triggers notification message delivering to the IPE

- Based on notification message, OIC client sends ‘oic/mnt’ UPDATE request to the OIC Device in Legacy OIC domain

- OIC Device sends UPDATE response to the OIC client in IPE

================ End of Text Proposal 1 =====================