| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#20.0 |
| Source:* | ZTE Corporation (CCSA) |
| Date:* | 2015-10-29 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | Add reference architecture for 3GPP IWK |
| CR against: Release* | Rel-2.0 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.0.1 |
| Clauses/Sub Clauses* | 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add reference architecture for 3GPP IWK.

### -----------------------Start of change 1-------------------------------------------

# 6	Reference architecture

Figure 6-1 Interworking architecture

There are three architecture options for oneM2M Platform interworking with 3GPP Release 13 MTC specifications.

The first option of oneM2M interworking architecture is that the oneM2M platform hosts SCEF. The oneM2M service provider is a trusted business partner of 3GPP MNO (3GPP MNO can be the oneM2M service provider also). NSSE in IN-CSE provides SCEF functionality and interfaces directly with the 3GPP network entities via 3GPP exposed interfaces. The oneM2M platform is equivalent to SCEF in 3GPP architecture. SCEF southbound exposed interfaces (e.g. S6*, Rx, T4 etc.) are mapped to Mcn reference point. Details on SCEF northbound interfaces are to be defined and possibility of SCEF-SCS interface is not considered to expose. Refer to the following figure 6-2.

Figure 6.2 Architecture option 1

The second option of oneM2M interworking architecture is that the SCEF is in an independent functional entity. There is standalone SCEF, SCEF is in 3GPP trust domain, 3GPP MNO can be SCEF provider as well. The assumption is that OMA will specify the SCEF. The oneM2M platform is equivalent to Service Capability Server (SCS) in 3GPP architecture, SCEF northbound interface is the OMA specified APIs that are mapped to Mcn. SCEF communicates with 3GPP network entities over 3GPP exposed interfaces (e.g. S6*, Rx, T4 etc.). Refer to the following figure 6.3.

Figure 6.3 Architecture option 2

The third option of oneM2M interworking architecture is that Mcn supports other APIs. There is a standalone ‘Other Exposure Function’, this other ‘Exposure Function’ is in 3GPP network trust domain, the 3GPP MNO provides this ‘Other Exposure Function’ as well. The specification of this ‘Other Exposure Function’ is to be defined. For oneM2M supported other APIs, the oneM2M platform is equivalent to SCS in 3GPP architecture. For other APIs which are not supported by oneM2M, the Application Server (AS in 3GPP architecture) communicates with the ‘Other Exposure Function’ directly. ‘Other Exposure Function’ northbound interface is the Other APIs. ‘Other Exposure Function’ communicates with 3GPP network entities over 3GPP exposed interfaces (e.g. S6*, Rx, T4 etc.). Refer to the following figure 6.4.

Figure 6.4 Architecture option 3

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?