| Input Contribution |
| --- |
| Meeting ID* | ARC 20 |
| Title:* | TS-0014-LWM2M_Object_Transport and Interworking |
| Source:* | Thierry GARNIER, Gemalto N.V, Thierry.garnier@gemalto.com |
| Uploaded Date:* | 2015-10-29 |
| Document(s) Impacted* | TS-0014 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add to next TS-0014 Baseline |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 6.4  LWM2M Object Transport and Interworking

### 6.4.1	Introduction

The LWM2M Client uses the Device Management & Service Enablement interface to  provide the capabilities for the LWM2M Server of the IPE (Interworking Proxy Entity)  to access LWM2M Objects, Objects Instances and Resources available from the LWM2M Client.

An Hosting CSE maintains a representation of the LWM2M Data Model in dedicating a container to each LWM2M Object and Object Instance  registered during the Discovery Phase, in order to allow data exchanges between the LWM2M  Client and the oneM2M Service Layer . It is the <contentInstance> resource of  the  dedicated <container> resource which will actually hold the Object Instance and its LWM2M Resource values.

In reference to clause 6.3, at the end of the registration phase all declared LWM2M Object Instances and  LWM2M Objects are associated  to a <container>  resource created with  the resourceName attribute set accordingly to the proper LWM2M Object Instance path (e.g. /9/1) or to the LWM2M Object  path (e.g /9).

When a oneM2M CRUD request is addressed from a registar CSE to an  hosting CSE containing the represention of  an  LWM2M Endpoint, the answer to the Originator is returned in cooperation with the IPE for ensuring up-to-date information as well as a full respect of the LWM2M access control policy.

### 6.4.2	LWM2M Interworking mechanisms

A proper Interworking between LWM2M Application and the oneM2M Hosting CSE, requires of having efficient  mechanisms to maintain Data synchronization and  to respect  Access Control Policy when exchanging information accross these 2 contexts.

- Data synchronization is relying on both oneM2M Subscription/Notification and LWM2M Observation/Notification mechanisms. A fine granularity for Automatic Data synchronization shall  be achieved .

- Access Control Policy check is achieved through a close collaboration between oneM2M and LWM2M Access Control mechanisms

LWM2M and oneM2M  mechanisms  used to achieve Data Synchronisation and Access Control Policy check  are specified in more details in the two following clauses 6.5 and  6.6. In particular, for supporting LWM2M Interworking and in order to trigger the appropriate notification to the IPE,  the <container> resource’ subscribtion shall have eventNotificationCritera attribute with Condition tag  eventType  ‘B’ ,‘C’ and ’E’ set (clause 6.4.2.2, 6.4.2.3, 6.4.2.4) ;  in specific case,  eventType ‘F’ shall be set instead , when the <container> resource is just a placeholder for the object  instanciation (see clause 6.4.2.1)

| eventType | 0..n | B. Deletion of the subscribed-to resource , C. Creation of a direct child of the subscribed-to resource Retrieval of obsolete information for the subscribed-to resource Retrieval of an unassigned accessControlPolicyIDs |
| --- | --- | --- |

The current sub-clause aims at specifying how the usage of such mechanisms can  provide to the LWM2M Interworked context, an efficient answer to a oneM2M CRUD request.

Following sub-clauses specify the sequences of operations involved for each particular CRUD request related to  Interworking Process; these CRUD requests shall follow the general procedures specified  in clause 10 (CREATE, RETRIEVE, UPDATE, DELETE).

Figure 6.4-1:

6.4.2.1  oneM2M CREATE Procedure

Such a request aims at creating a new oneM2M Resource which will result of requesting a new Object Instantiation in the LWM2M Client.

Figure 6.4-2: Procedure for CREATEing a Resource (TS-0001 Clause 10)

Specific  steps of the Receiver Processing according to the LWM2M Interworking process are detailed  below :

Step 001:  Find the targeted <container> resource : its resourceName contains the ID of the Object to instanciate.

This <container> resource has no value for the accessControPolicyIDs attribute.

The final <container> resource representing the Object Instance doesn’t exist yet  (it is the goal of that request to create that resource).

Step 002 : Check  Access Control Policy for being able to create a new Resource

- As no accessControlPolicyIDs exists for the targeted <container> resource, a notification  is triggered  from the CSE to the IPE (TS-0001 clause 9.6.1.3.2  eventType ‘F’ set)

- The IPE according to the NOTIFY request information (step above),  checks  the validity of creating a new Object Instance into the LWM2M Client .

  - On successful validation, the following transaction  is performed but is stopped and operations are  reversed to the stage just before the transaction  if any error occurs

    - a CREATE Command regarding the targeted Object is provided by the IPE  to the LWM2M Client

    - on LWM2M CREATE success

      - The new Object Instance is available into the LWM2M Client

      - A LWM2M  Update Registration is performed on the IPE related to the new Object Instance.

      - After above registrationtheIPE will create via the Mca reference point, a new <container> resource in the hosting CSE along with a resourceName referring to the new Object Instance ID  and an accessControlPolicyIDs.

- NOTIFICATION response, is sent back on Mca Reference point and  the CSE Access Control Policy system can finalize its process. .

Step 003  :  The Hosting CSE sends the appropriate  answer  back to the Originator (Acknowlegment, Errors, Data) as specified in TS-001 clause 8.1.3

6.4.2.2  oneM2M RETRIEVE Procedure

A RETRIEVE  request on  information related to a resource representing a data of the  LWM2M Client registered to the target CSE, will be treated in conformance with the Basic RETRIEVE Procedure specified in TS-0001 clause 10.1.2.

The Receiver performs local processing to verify the existence of requested Resource and checks privileges for retrieving the information related to the resource. After successful verification, the Receiver shall return the requested information according to the procedures for the type of interworking (e.g Transparent, Semantic) as described in clause 7 and 8, otherwise an error indication shall be returned.

Figure 6.4-3: Procedure for RETRIEVing a Resource (TS-0001 Clause 10)

Specific  steps of the Receiver Processing according to the LWM2M Interworking process are detailed  as follows:

Step 001:  Find the targeted <container> resource  : its resourceName is the path of the Object  Instance Path

Step 002 : Check  Access Control Policy for retrieving information related to the resource

Step 003  On successful validation  of  Access Control Policy, the obsolescence of the targeted Resource is checked

Step 003.1 : When the resource Information is obsolete ( <contentInstance> resource is not available) an event for Information Retrieval  (eventType ‘E’) is triggered to the IPE

- In case of  “Not Blocking” trigger Policy of the notification set in the subscription, the step 004 is processed with an acknowledgement sent back to the Originator

Step 003.2 : On receiving the event  ‘Retrieval of obsolete information (eventType ‘E’) the IPE performs a READ request to the LWM2M Client through the IPE Server side in posting an LWM2M Observation on the targeted Object Instance.

Step 003.3 : Once the Object Instance related  to the Request is available  on the IPE Server, the IPE via the Mca creates  and populates a <contentInstance> resource in the  requested  <container>  resource.

Step 004 :   The appropriate answer is sent back to the Originator (Acknowlegment, Errors, Data)

NB : as an OBSERVATION has been set up on the targeted LWM2M Object Instance, the automatic synchronisation between this Object Instance and its representation in the hosting CSE is performed. Further oneM2M accesses to these data should be simplified in minimizing  Step003 impact (up-to-date data already present in the CSE).

General Exceptions:

- The targeted resource/attribute in To parameter does not exist. The Receiver responds with an error.

- The Originator does not have privileges to retrieve information stored in the resource on the Receiver. The Receiver responds with an error.

6.4.2.3  oneM2M UPDATE Procedure

An UPDATE request on information related to a resource representing a data of the  LWM2M Client registered to the target CSE will be treated in conformance with the Basic UPDATE Procedure specified in TS-0001 clause 10.1.2.

Figure 6.4-4: Procedure for UPDATing a Resource (TS-0001 Clause 10)

Specific  steps of the Receiver Processing according to the LWM2M Interworking process are detailed  as follows:

Step 001:  Find the targeted <container> resource

Step 002 : Check  Access Control Policy for updating  the information related to the resource

Step 003 : On successful validation  of  Access Control Policy,

Step 003.1 : <contentInstance>  resource of the targeted <container> resource is created (firstly deleted  if already present) and filled up with the informations provided in the request. Information  is ready  to be transferred to the LWM2M Client.

Step 003.2 : according to the <subscribed>-to resource parameters notification  (eventType ‘C’  direct Child Creation),  a notification  (from previous step) is sent from the CSE to the IPE in order to advise IPE that  new information  has to be reported to the LWM2M Client.

At that stage, Step 4, may already be engaged

Step 003.3 : The IPE processes the request, retrieves the data from the  <contentInstance>  resource via Mca Interface and address a LWM2M Update Request to the LWM2M Client.

Step 004 :   The appropriate answer is sent back to the Originator (Acknowlegment, Errors)

General Exceptions:

- The targeted resource in To parameter does not exist. The Receiver responds with an error.

- The Originator does not have the privilege to modify the resource, create attributes or delete attributes on the Receiver. The Receiver responds with error.

- The provided information in the Content is not accepted by the Receiver. The Receiver responds with error.

6.4.2.4  oneM2M DELETE Procedure

The DELETE operation shall be used by an Originator CSE or AE to delete a resource at a Receiver CSE.  A DELETE  request on  information related to a resource representing a data of the  LWM2M Client registered to the target CSE, will be treated in conformance with the Basic DELETE Procedure specified in TS-0001 clause 10.1.2.

For such operation, the DELETE procedure shall consist of the deletion of all related information of the target resource, which will result - due to the LWM2M interworking context -  of requesting the deletion of an  Object Instance to the LWM2M Client.

Figure 6.4-5: Procedure for DELETING a Resource (TS-0001 Clause 10)

Specific  steps of the Receiver Processing according to the LWM2M Interworking process are detailed  as follows:

Step 001:  Verify and find  the targeted  <container> resource  : its resourceName is the path of  the Object  Instance to delete (e.g. /5/0).

Step 002 : Check  Access Control Policy for being able to delete the targeted  Resource  in using the CSE Authorization System

Step 003 : On successful validation  of  Access Control Policy :

Step 003.1:  the subscribed-to <container> resource and associated resource are deleted.

Step 003.2:  from step above and according to the <subscribed>-to resource parameters  notification  (eventType ‘B’  Deletion of the subscribed-to resource),  a notification  is sent from the CSE to the IPE in order to advise IPE a new informations have to be reported to the LWM2M Client.

    - The Object Instance is deleted in the LWM2M Client

    - A LWM2M  Update Registration is performed on the IPE

Step 004 :   The appropriate answer is sent back to the Originator (Acknowlegment, Errors) as specified in TS-0001 clause 8.1.3.

General Exceptions:

- The targeted resource in To information does not exist. The Receiver responds with an error.

- The Originator does not have the privileges to delete the resource on the Receiver. The Receiver responds with an error.

### 6.4.3  oneM2M Resource Operation Responses

| LWM2M Errors Client Device Management & Service Enablement interface | oneM2M Resource Operation Response |
| --- | --- |
| Create 2.01 Created: 4.00 Bad Request 4.01 Unauthorized 4.04 Not Found | 2001 Created 4000 4103 4004 |
| Read 2.05 Content: 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2000 OK 4103 4004 4005 |
| Write 2.04 Changed 4.00 Bad Request 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2004 Changed 4000 4103 4004 4005 4102 |
| Delete 2.02 Deleted 4.00 Bad Request 4.01 Unauthorized 4.04 Not Found 4.05 Method Not Allowed | 2002 deleted 4103 4103 4004 4005 |