| CHANGE REQUEST |
| --- |
| Meeting:* | WG2 Architecture - ARC 20 |
| Source:* | Ericsson |
| Date:* | 2015-10-20 |
| Contact:* | George Foti |
| Reason for Change/s:* | WI-0037 New text to be included in TR-0024 |
| CR against: Release* |  |
| CR against: WI* | Active WI-0037 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024-V-0.0.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### -----------------------Start of change 1-------------------------------------------

# 8         Potential solutions for interworking with oneM2M

## 8.1 Generic Interworking Architecture

Figore 8.1-1 below depicts a generic interworking architecture between oneM2M and any underlying network including a 3GPP network

Figure 8.1-1: oneM2M Generic Interworking Model with any underlying network.

This architecture supports the following interworking modes:

- The NSSE exclusively invokes services of a 3GPP underlying network using OMA API.

- The NSSE invokes exclusively services of any underlying network using third party APIs.

- The NSSE invokes services of the underlying network directly via the reference points of the applicable nodes within the underlying network. This model is applicable to the case where the oneM2M service provider and the underlying network provider is the same or there is trust relation between both service providers if they are different.

- Any combination of the above, where some services are invoked using an API (OMA or third party depending on the underlying network) while other services are invoked directly with the underlying network using the applicable reference point.

It is clear that the functionality supported by the NSSE is different depending on the interworking mode.

## 8.2  Interworking Architecture with a 3GPP underlying network

The following three architectural models can be supported

### 8.2.1 Exclusive Support through OMA API

Figure 8.2-1 depicts this architectural model. In this case 3GPP services capabilities are exclusively invoked via the OMA API. Hence, the SCEF is fully implemented outside the oneM2M environment

Figure 8.2-1: oneM2M interworking with a 3GPP underlying network via OMA API

### 8.2.1 Exclusive Support through 3GPP Reference Points

Figure 8.2-2 depicts this architectural model.

In this case 3GPP services capabilities are exclusively invoked via the 3GPP reference points for the applicable 3GPP node

In this case, the SCEF is fully implemented within the oneM2M environment

Figure 8.2-2: oneM2M interworking with a 3GPP underlying network via 3GPP Reference Points

### 8.2.3 Hybrid Mode

Figure 8.2-3 depicts this architectural model.

In this case 3GPP services capabilities are invoked on a per service basis which can include OMA API for some service, proprietary APIs for others and finally some services can be invoked directly using the 3GPP reference points.

Figure 8.2-3: oneM2M interworking with a 3GPP underlying network in a hybrid mode

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?