| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 20 |
| Source:* | Huawei Technologies |
| Date:* | 2015-11-01 |
| Contact:* | Qi Yu, yuqi@huawei.com Mitch Tseng, mitch@T-infoserv.com |
| Reason for Change/s:* | This contribution intends to introduce new resources defined for Time Series Data as discussed in . R01: <flexContainer> can be used to support Time Series Data afer offline discussion. R02: solution comparison New resource type TimeSeries and timeSeriesInstance made by flexcontainer are used for Time Series Data. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active WI-0033 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v2.3.0 |
| Clauses/Sub Clauses* | 9.6 and 10.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution intends to introduce the new resources defined for Time Series Data. The related discussion contribution is ARC-2015-2235-Solution_discussion_of_Time_Series_Data.

A new resource type  <flexContainer> was defined in ARC-2015-2248R02-Custom_Container. The structure of the <flexContainer> is as follows.

When an instance of <flexContainer> is a child of a <flexContainer> resource, some of  attributes can be optional. Their presence is determined by the respective definition referred to by the containerDefinition attribute.

Through  the above description, we can know that this resource can be used for Time Series Data since the data redundancy can be reduced if some madantory common attributes become optional.

The comparison of five solutions are as follows

- container and contentInstancet

In this case ,the container is used to store meta information of the Time Series Data .And the contentInstnace is created for every Time Series Data.It will lead to a lots of  data redundancy because  the common attributes have to be repeated when a new contentInstance is created.

- Container and timeSeriesInstance made by flexcontainer

In this case ,the container is used to store meta information of the Time Series Data .And the flexcontainer is used to define TimeSeriesInstance. It will lead to container complicated and heavy because the container need some special attributes for Time Series Data and the CSE has to handle the contentInstance and TimeSeriesInstance.

- TimeSeries and timeSeriesInstance made by flexcontainer

In this case the flexcontainer is used to make TimeSeries and TimeSeriesInstance. TimeSeries is used to store meta information of Time Series Data . The CSE need to detect when the data is missing ,therefore the TimeSeries made by flexcontainer does not work.

- New resource type TimeSeries and timeSeriesInstance made by flexcontainer

The flexcontainer is used to define TimeSeriesInstance. A new resource type timeSeries is used to store meta information of Time Series Data and detects the missing data when it happens.

Based on the above discussion ,the Option 4 is good choice.In order to make some progress on Time Series Data , how to detect the missing data will be discussed later. And for option4, the “containerDefinition”attribute in the < flexcontainer> shall be optional.

### -----------------------Start of change 1-------------------------------------------

### 9.6.x	Resource Type timeSeries

The <timeSeries> resource represents a container for Time Series Data instances. It is used to share information with other entities and potentially to track, detect and report the missing data in Time Series. A <timeSeries> resource has no associated content. It has only attributes and child resources.

Figure 9.6.x-1: Structure of <timeSeries> resource

Table 9.6.x-1:Child resources of <timeSeries> resource

| Child Resources of <timeSeries> | Child Resource Type | Multiplicity | Description | <timeSeriesAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <timeSeriesInstance> | 0..n | See clause 9.6,y | <timeSeriesInstance>, <timeSeriesInstanceAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |

The <timeSeries> resource shall contain the attributes specified in table 9.6.x-2.

Table 9.6.x-2: Attributes of <timeSeries> resource

| Attributes of <timeSeries> | Multiplicity | RW/ RO/ WO | Description | <timeSeriesAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. | NA |
| maxNrOfInstances | 0..1 | RW | Maximum number of direct child <timeSeriesInstance> resources in the <timeSeries> resource. | OA |
| maxByteSize | 0..1 | RW | Maximum size in bytes of data that is allocated for the <timeSeriesInstance> resource for all direct child<timeSeriesInstance> resources in the <timeSeries> resource. | OA |
| maxInstanceAge | 0..1 | RW | Maximum age of a direct child <timeSeriesInstance> resource in the <timeSeries> resource. The value is expressed in seconds. | OA |
| currentNrOfnstances | 1 | RO | Current number of direct child <timeSeriesInstance> resource in the <timeSeries> resource. It is limited by the maxNrOfInstances. | OA |
| currentByteSize | 1 | RO | Current size in bytes of data stored in all direct child <timeSeriesInstance> resources of a <timeSeries> resource. It is limited by the maxByteSize. | OA |
| period | 0..1 | WO | The period of Time Series Data. | OA |
| allowedDuplication | 1 | RW | The attribute indicates whether the different <timeSeriesInstance> with the same dataTime attribute is permitted. If no, the Receiver shall not create the <timeSeriesInstance> with the dulication of dataTime attribute. | OA |
| missingDataDetect | 0..1 | WO | Indicates whether the Receiver shall detect the missing Time Series Data if it is periodic. | NA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the child <tsdInstance> resources of the present <timeSeriesData> resource (see note). | OA |
| NOTE: The access to this URI is out of scope of oneM2M. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start  of change 2-------------------------------------------

### 9.6.y	Resource [timeSeriesInstance]

The [timeSeriesInstance] resource represents a data instance in the <timeSeries> resource. The  [timeSeriesInstance] resource is a specialization of the <flexcontainer>resource.

The  [timeSeriesInstance] resource shall not be modified once created. An AE shall be able to delete a  [timeSeriesInstance] resource explicitly or it may be deleted by the platform based on policies. If the platform has policies for  [timeSeriesInstance] retention, these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge attributes in the [timeSeries] resource. If multiple policies are in effect, the strictest policy shall apply.The [timeSeriesInstance] resource inherits the same common attributes from its parent [timeSeriesData] resource.

Figure 9.6.y-1: Structure of [timeSeriesInstance] resource

The < timeSeriesInstance> resource shall contain the attributes specified in table 9.6.y-1.

# Table 9.6.y-1: Attributes of [timeSeriesInstance ]resource

| Attributes of <timeSeriesInstance> | Multiplicity | RW/ RO/ WO | Description | <tsdInstanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| dataTime | 1 | WO | This attribute contains the time when the data was generated by the M2M Node, | OA |
| content | 1 | WO | This attribute contains the data generated by the M2M Node. | OA |
| sequenceNr | 0..1 | WO | This attribute contains the data sequence number generated by the M2M Node | OA |

### -----------------------End of change 2-------------------------------------------

### ------------------------Start of change 3-------------------------------------------

#### 10.2.x	<timeSeries> Resource Procedures

#### 10.2.x.1	 Create <timeSeries>

This procedure shall be used for creating a < timeSeries> resource.

# Table 10.2.x.1-1: < timeSeries> CREATE

| <timeSeries> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.x |
| Processing at Originator before sending Request | According to clause 10.1.1.1. |
| Processing at Receiver | According to clause 10.1.1.1. Upon successful validation of the provided attributes, the Hosting CSE creates the <timeSeries> resource in the Hosting CSE. Conditionally, in the case that the period and missingDataDetect are set, the Hosting CSE shall monitor the Time Series Data based on its period. If the allowedDuplication is set, the Hosting CSE may create the <timeSeriesInstance> resource with the same dataTime. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <timeSeries> resource, according to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.x.2	Retrieve <timeSeries>

This procedure shall be used for retrieving the attributes of a <timeSeries> resource.

# Table 10.2.x.2-1: <timeSeries> RETRIEVE

| <timeSeries> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <timeSeries> resource as defined in clause 9.6.x |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.x.3	Update <timeSeries>

This procedure shall be used for updating the attributes  in  a <timeSeries> resource.

# Table 10.2.x.3-1: <timeSeries> UPDATE

| < timeSeries > UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: attributes of the <timeSeries> resource as defined in clause 9.6.x which need be updated. |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.x.4	Delete <timeSeries>

This procedure shall be used for deleting a <timeSeries> resource residing under a <timeSeries> resource.

# Table 10.2.x.4-1: <timeSeries> DELETE

| <timeSeries> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.4.1. |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | Once the <timeSeries> resource is deleted, the Receiver shall delete the associated resources (i.e. <timeSeriesInstance> resources) |
| Exceptions | According to clause 10.1.4.1 |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?