| Input Contribution |
| --- |
| Meeting ID* | ARC 20 |
| Title:* | TS-0014-LWM2M_Object_Security |
| Source:* | Thierry GARNIER, Gemalto N.V, Thierry.garnier@gemalto.com |
| Uploaded Date:* | 2015-11-4 |
| Document(s) Impacted* | TS-0014 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add to next TS-0014 Baseline |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 6.6  LWM2M Interworking Object Security  Policy

6.6.1	Introduction

OMA-LWM2M and oneM2M Access Control Policies shall collaborate in order of assuring to the Interworked resources to follow the oneM2M Authorisation Procedure specified in clause 11.3.4 of oneM2M TS-0001 and clause 7 of oneM2M TS-0003

As a LWM2M Client MAY support one or more LWM2M Servers, there is a need to determine which operation on a given Object Instance is authorized for which LWM2M Server: the LWM2M Access Control Object is designed for supporting that capability.

The LWM2M Interworking Proxy Entity (IPE) is viewed as one of the LWM2M Server of the Interworked LWM2M Client.

The Access Control Policy between oneM2M and  OMA LWM2M cannot be a simple re-mapping  from one context to the other one, so adaptation  has to be preferably supported at the IPE level in order to minimize impact on the standard CSE.

### 6.6.2 Object Security  Policy

A brief reminder of  the Access Control mecanisms in LWM2M and in oneM2M is given first, then is specified how the Interworking Proxy Entity allows both systems to collaborate

#### 6.6.2.1  LWM2M  Object Security Policy

In OMA LWM2M there is the notion of Object Instance owner which is a LWM2M Server which has full access rights regarding the Object Instance it was authorized to create.

LWM2M Security Object Security Policy can be addressed at three different levels

- the Ownership Object Policy : to define which Server is authorized to Instantiate which Object :  the LWM2M Bootstrap Server only can manage this.

- the Object Instance Access Control Policy : to assign Object Instance Access Rights (Read, Write, Execute, Delete) to a given Server; only the Server which is the Object Instance owner can manage this.

- the Resource Access Control Policy :  LWM2M Object Specification determins which operation a given resource is likely to support (Read, Write, Execute).

The Ownership Object is out of the scope of the  Interworking context; the LWM2M IPE will be only able to interact with the Objects and Object Instances appearing during the LWM2M registration phase

#### 6.6.2.2  OneM2M resource Security Policy

Access Control Mechanisms for oneM2M are described in clause 7 of oneM2M TS-0003 and are using  <accessControlPolicy> resource  described in clause 9.6.2 of oneM2M TS-0001

Figure 6.6.2.2-1    : Structure of <accessControlPolicy> resource

With the description for privileges and selfPrivileges  attributes given below :

| privileges | 1 | RW | A set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| --- | --- | --- | --- | --- |
| selfPrivileges | 1 | RW | A set of access control rules that apply to the <accessControlPolicy> resource itself. | MA |

Figure 6.6.2.2-2        extract from  <accessControlPolicy> resource  attributes description (oneM2M TS-0001)

The set of access control rules represented in privileges and selfPrivileges attributes are composed of 3-tuples (accessControlOriginators, accessControlContexts, accessControlOperations) with parameters described in clause 9.6.2.1 , 9.6.2.2, 9.6.2.3 in oneM2M TS-0001. The accessControlOriginators determines the CSE / AE originator and the accessControlOperations determine the set of operations the protected resource can support from the originator.

If privileges attribute contains no 3-tuples then this represents an empty set of the access control rules.

The selfPrivileges attribute shall contain at least one 3-tuples.

The protected resource contains an accessControlPolicyIDs attribute  which is a list of Access Control Policy resources (Figure below extracted from clause 7 of oneM2M TS-0003) against which the originator request is checked by the CSE Access Control   mecanisms in order to validate or to refuse the access to this resource .

Figure 6.6.2.2-3      extract from TS-0001 Relation between Resources Instances and Access Control Policies

##### 6.6.2.3  LWM2M Interworking Access Control Policy 6.6.2.3.1  LWM2M Interworking ACP assignation

In the hosting CSE,  the Access Control mechanisms  (see Figure 6.6.2.3.1-1 and oneM2M TS-0003)  are responsible to check and deliver the Access Right Validation when a resource is targeted by a oneM2M request .

The LWM2M Client itself, has no way to control the  accesses to itself based on oneM2M entities identifier,  also the hosting CSE shall have full authority for checking the validity of a oneM2M request regarding  LWM2M Interworked resource,

- consequently : The hosting CSE shall be provisioned with the proper  <accessControlPolicy>  (ACPs) resources, prior to the phase (clause 6.3 LWM2M Object Delivery) where the IPE-registered Objects and Object Instances are translated to <container> resources of this CSE.

Note : In the current release the  “selfPrivileges” attributes shall be configured in such a way the <accessControlPolicy>  resources cannot be modified after provisioning.

- Each <container> resource  representing a LWM2M Object Instance in the hosting CSE shall have an assigned accessControlPolicyIds attribute. These associated accessControlPolicyIDs are provisioned in the LWM2M IPE and this process may be part of the Clause 6.8 of this document (IPE Administration)

This assignation shall takes place :

- along the processus of allocating <container> resources of the hosting CSE from the IPE-registered Object Instances (clause 6.3 LWM2M Object Delivery)

- and after a oneM2M CREATE request leading to the successful instanciation of an Object  in the LWM2M Client and the allocation of its <container> resource representation in the hosting CSE.

- 6.6.2.3.1 LWM2M Interworking ACP  mechanismThe ACP mechanisms for a oneM2M CREATE request and the Nominal ACP Mechanisms for the other oneM2Mrequests,  can be distinguished.(see Figure 6.6.2.3.1 -1)

Figure  6.6.2.3.1 -1 LWM2M  Interworking messages flow

Note : <Description to add>

###### 6.6.2.3.2.1  Nominal ACP mechanisms

###### These ACP mechanisms are used for all the oneM2M requests except the CREATE one.

In such a nominal process  each oneM2M resource in the hosting CSE representing a LWM2M Object Instance has an assigned accessControlPolicyIDs attribute referring a list of  valid <accessControlPolicy> resources. As a consequence Access Control for LWM2M interworking resources are performed  as specified in clause 7 of oneM2M TS-0003.

6.6.2.3.2.2  CREATE request and ACP mechanisms

The oneM2M CREATE request  applies to a resource for which  the CSE Access Control  mechanisms is not able to determin an accessControlPolicyIDs since this LWM2M Interworked resource doesnot exist yet.

As specified  in Clause 6.4.2.1, for a oneM2M CREATE request,  the targeted <container> resource is representing a LWM2M Object; in that context the accessControlPolicyIDs attribute of that  targeted resource is unassigned.  In the LWM2M Interworking context, for such a resource representing a LWM2M Object and for which a <subscription> resource has been assigned with the eventType ‘F’ set (Retrieval of unassigned accessControlPolicyIDs)in its notification policy (eventNotificationCritera) attribute , a notification shall be triggered to the IPE in order to start the CREATE Resource/ LWM2M Object Instantiation processes described  in clause 6.4.2.1 of this document.

Along with the notification answer coming back from IPE to the hosting CSE, the full material regarding <container> resource and  the assignment of the accessControlPolicyIDs shall be transferred  allowing the Access Control mechanisms to complete thevalidation process as specified  in clause 7 of the oneM2M TS-0003.

# Text boxes

Resource_2

...

ACP_1

ACP_2

ACP_3

ACP_4

Instances of

accessControlPolicy

resources (ACP)

Example:

ACP set = (ACP_1, ACP_2)

assigned to Resource_1

Each ACP includes one privileges and one selfPrivileges attribute.

privileges and selfPrivileges attributes include a set of access control rules (defined in Section 7.3)

List of IDs in accessControlPolicyIDs

attribute of Resource_1

Resource_1

Resource_3

Resource_N