| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#20.4 (joint with SEC) |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-01-06 |
| Contact:* | As above |
| Reason for Change/s:* | Support for End-to-End Security. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 and v2.5.0 |
| Clauses/Sub Clauses* | Clause 9.6 “Resource Types”, 10.2 “Resource Type-Specific Procedures”, Clause 11 “Trust Enabling Architecture” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

See contributions

- ARC-2016-0001 “E2E Attribute and Parameter Security”

- ARC-2016-0002 “E2E Primitive Security”

- ARC-2016-0003 “e2EKey Resource”. The CR proposes changes for where the Terminating End-Point from ARC-2016-0003 is a CSE; the CR currently does not propose changes for where the Terminating End-Point from ARC-2016-0003 is an AE.

Yellow highlighting has been used indicate references and cross references whose values are not yet finalized and which are to be assigned by the rapporteur, e.g. “[i.RFC7516]” or “clause 9.6.y”.

The following table identifies the necessary tasks for supporting E2E Security in TS-0001, and notes an unofficial status for those tasks (not yet proposed, proposed, agreed in principle). This table is for tracking purposes only; it will be deleted in the final version of the CR to be agreed, and has no official standing.

| Tasks ID | Task | Status within CR |
| --- | --- | --- |
| 1 | Change Table 9.6.1.1-1 Resource Types by adding <e2EKeyCSE> and <e2ESecurityPromitiveExchange> | Proposed |
| 2 | Change Table 9.6.1.3.2-1: Common Attributes by adding certificate and e2ESecurityCapabilities attributes | Proposed |
| 3 | Update 9.6.3 Resource Type CSEBase: add child resources<e2EKeyCSE> and <e2ESecurityPromitiveExchange> and certificate and e2ESecurityCapabilities | Proposed |
| 4 | Update 9.6.4 Resource Type remoteCSE: add attribute lastE2ERand | Proposed |
| 5 | Update 9.6.5 Resource Type AE: add attributes certificate and e2ESecurityCapabilities | Proposed |
| 6 | Add 9.6.x Resource Type e2EKeyCSE for e2EKey with CSE as terminating End Point | Proposed |
| 7 | Add 9.6.y Resource Type e2ESecurityPrimitiveExchange for transporting security primitives | Proposed |
| 8 | Add 10.2.x <e2EKeyCSE> Resource Procedures | Proposed |
| 9 | Add 10.2.y <e2ESecurityPrimitiveExchange> Resource Procedures | Proposed |
| 10 | Add overview of end-to-end security procedures in clause 11 | Proposed |
| 11 | Add references | Proposed |
| 12 | Update sub-clauses of clause 10.1 “Basic Procedures” to explain interaction with E2E Security for Primitives. | Not yet proposed |
| 12 | Add definition of resource type (possibly specialization of <mgmtObj>) for containing the policy for E2E Security of Primitives (either “all” or a list of specific end-points and/or groups) | Not yet proposed |
| 14 | Explain use of the policy for E2E Security of Primitives | Not yet proposed |
| 15 | Add 9.6.x Resource Type e2EKeyAE for e2EKey with AE as terminating End Point | Not yet proposed |
| 16 | Add 10.2.x <e2EKeyAE> Resource Procedures | Not yet proposed |

### Apply changes to Table 9.6.1.1-1 Resource Types – trailing rows are not shown

### -----------------------Start of change 1-------------------------------------------

Table 9.6.1.1-1 Resource Types

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the Hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing resources | subscription | AE, AEAnnc, remoteCSE, remoteCSEAnnc, CSEBase | 9.6.2 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the Registrar CSE | subscription, container, group, accessControlPolicy, schedule, pollingChannel，semanticDescriptor | remoteCSE, remoteCSEAnnc, CSEBase | 9.6.5 |
| container | Shares data instances among entities. Used as a mediator that buffers data exchanged between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule | container, flexContainer, contentInstance, subscription, latest, oldest，semanticDescriptor | AE, AEAnnc, container, containerAnnc, remoteCSE, remoteCESAnnc, CSEBase, flexContainer, flexContainerAnnc | 9.6.6 |
| contentInstance | Represents a data instance in the <container> resource | semanticDescriptor | Container, containerAnnc | 9.6.7 |
| flexContainer | A template which allows to define specialized (customizable) versions of containers with a flexible and lightweight structure | container, flexContainer, subscription, semanticDescriptor, | AE, AEAnnc, container, containerAnnc, flexContainer, flexContainerAnnc, remoteCSE, remoteCESAnnc, CSEBase | 9.6.35 |
| CSEBase | The structural root for all the resources that are residing on a CSE. Stores information about the CSE itself | remoteCSE, remoteCSEAnnc, node, AE, container, group, accessControlPolicy, subscription,, mgmtCmd, locationPolicy, statsConfig, statsCollect, request, delivery, schedule, notificationTargetPolicy, flexContainer, e2EKeyCSE, e2ESecurityPrimitiveExchange | None specified | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | CSEBase | 9.6.11 |
| e2EKeyCSE | Represents a key establishment handshake between the creator of the resource the CSE represented by the parent resource | None specified | CSEBase | 9.6.x |
| e2ESecurityPrimitiveExchange | Represents an end-to-end security primitive exchange between the Originator and the CSE represented by the parent resource | None specified | CSEBase | 9.6.y |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.24 |

### -----------------------End of change 1-------------------------------------------

### Apply changes to Table 9.6.1.3.2-1: Common Attributes – trailing rows are not shown

### -----------------------Start of change 2-------------------------------------------

Table 9.6.1.3.2-1: Common Attributes

| Attribute Name | Description |
| --- | --- |
| accessControlPolicyIDs | The attribute contains a list of identifiers of an <accessControlPolicy> resource. The privileges defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyIDs attribute definition, then the accessControlPolicyIDs for that resource is governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyIDs attribute definition, or the privileges for access are fixed by the system. Refer to the corresponding resource type definitions and procedures to see how access control is handled in such cases. If a resource type does have an accessControlPolicyIDs attribute definition, but the (optional) accessControlPolicyIDs attribute is not set, or it is set to a value that does not correspond to a valid, existing <accessControlPolicy> resource, or it refers to an <accessControlPolicy> resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access privileges shall apply. All resources are accessible if and only if the privileges (i.e., shored as privileges or selfPrivileges attribute of <accessControlPolicy> resource) allow it, therefore all resources shall have an associated AccessControlPolicyIDs attribute, either explicitly (setting the attribute in the resource itself) or implicitly (either by using the parent privileges or the system default policies). Which means that the system shall provide a default access privileges in case that the Originator does not provide a specific accessControlPolicyIDs during the creation of the resource. To update this attribute, a Hosting CSE shall check whether an Originator has Update permission in any selfPrivileges of the <accessControlPolicy> resources which this attribute originally indicates. |
| stateTag | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource (see notes 1 and 2). The modification also includes direct child resource creation and deletion. |
| announceTo | This attribute may be included in a CREATE or UPDATE Request in which case it contains a list of addresses/CSE-IDs where the resource is to be announced. For the case that CSE-IDs are provided, the announced-to CSE shall decide the location of the announced resources based on the rules described in clause 9.6.26. For the original resource, this attribute shall only be present if it has been successfully announced to other CSEs. This attribute maintains the list of the resource addresses to the successfully announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. If announceTo attribute includes resource address(s), the present document does not provide any means for validating these address(s) for announcement purposes. It is the responsibility of the Hosting-CSE referenced by the resource address(s) to validate the access privileges of the originator of the Request that triggers the announcement. |
| announcedAttribute | This attributes shall only be present at the original resource if some Optional Announced (OA) type attributes have been announced to other CSEs. This attribute maintains the list of the announced Optional Attributes (OA type attributes) in the original resource. Updates to this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |
| labels | Tokens used as keys for discovering resources. This attribute is optional and if not present it means that the resource cannot be found by means of discovery procedure which uses labels as key parameter of the discovery. |
| certificate | Present in a resource representing an AE or CSE, and contains a certificate of the AE or CSE |
| e2ESecurityCapabilities | Present in a resource representing an AE or CSE. Lists the end-to-end security capabilities supported by the AE or CSE. A high level description of the supported protocols are provided clause 11.4, with details in TS-0003 [2]. |
| NOTE 1: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. NOTE 2: This attribute has the scope to allow identifying changes in resources within a time interval that is lower than the one supported by the attribute lastModifiedTime (e.g. less than a second or millisecond). This attribute can also be used to avoid race conditions in case of competing modifications. |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. The <CSEBase> resource shall be the root for all resources that are residing in the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource

Figure 9.6.3-1 does not show the child announce resource types defined in table 9.6.3-2.

Editor’s Note: Annex E should be updated to include provisioning of the notification deletion policy.

The <CSEBase> resource shall contain the child resources specified in table 9.6.3-1.

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resources of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See clause 9.6.4 |
| [variable] | <node> | 0..n | See clause 9.6.18 |
| [variable] | <AE> | 0..n | See clause 9.6.5 |
| [variable] | <container> | 0..n | See clause 9.6.6 |
| [variable] | <group> | 0..n | See clause 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <mgmtCmd> | 0..n | See clause 9.6.16 |
| [variable] | <locationPolicy> | 0..n | See clause 9.6.10 |
| [variable] | <statsConfig> | 0..n | See clause 9.6.23 |
| [variable] | <statsCollect> | 0..n | See clause 9.6.25 |
| [variable] | <request> | 0..n | See clause 9.6.12 |
| [variable] | <delivery> | 0..n | See clause 9.6.11 |
| [variable] | <schedule> | 0..1 | This resource defines the reachability schedule information of the entity. The absence of this resource implies the entity is always reachable. See clause 9.6.9 |
| [variable] | <m2mServiceSubscriptionProfile> | 0..n | See clause 9.6.19 |
| [variable] | <serviceSubscribedAppRule> | 0..n | See clause 9.6.29 |
| [variable] | < notificationTargetPolicy > | 0..n | See clause 9.6.32 |
| [variable] | <e2EKeyCSE> | 0..n | See clause 9.6.x |
| e2ESecurityPrimitiveExchange | <e2ESecurityPrimitiveExchange> | 0..n | See clause 9.6.y |

Table 9.6.3-2: Child announced resources of <CSEBase> resource

| Child Announced Resources of <CSEBase> | Child Announced Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | Refer Table 9.6.26.1-1 Announced Resource Types | 0..n |  |

The child announced resources of <CSEBase> resource defined in table 9.6.3-2 should be created when an Originator CSE (i.e. original resource Hosting CSE) and a Hosting CSE (i.e. announced resource Hosting CSE) have no registration relationship (e.g. the Originator CSE has not created <remoteCSE> resource on the Hosting CSE).

The <CSEBase> resource shall contain the attributes specified in table 9.6.3-3.

Table 9.6.3-3: Attributes of <CSEBase> resource

| Attributes of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 . |
| resourceID | 1 | RO | See clause 9.6.1.3 . |
| resourceName | 1 | RO | See clause 9.6.1.3 . |
| creationTime | 1 | RO | See clause 9.6.1.3 . |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 . |
| accessControlPolicyIDs | 0..1 (L) | RO | See clause 9.6.1.3 . |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 . |
| cseType | 0..1 | RO | Indicates the type of CSE represented by the created resource. Mandatory for an IN-CSE, hence multiplicity (1). Its presence is subject to SP configuration in case of an ASN-CSE or a MN-CSE. |
| CSE-ID | 1 | RO | The CSE identifier in SP-relative CSE-ID format (clause 7.2). |
| supportedResourceType | 1 (L) | RO | List of the resource types which are supported in the CSE. This attribute contains subset of resource types listed in clause 9.2. This also includes the supported optional attributes for each supported resource type. |
| pointOfAccess | 1 (L) | RO | Represents the list of physical addresses to be used by remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is exposed to its Registree. |
| nodeLink | 0..1 | RO | The resourceID of a <node> resource that represents the node specific information. |
| notificationCongestionPolicy | 0..1 | RO | This attribute applies to CSEs generating subscription notifications. It specifies the rule which is applied when the storage of notifications for each subscriber (an AE or CSE) reaches the maximum storage limit for notifications for that subscriber. E.g. Delete stored notifications of lower notificationStoragePriority to make space for new notifications of higher notificationStoragePriority, or delete stored notifications of older creationTime to make space for new notifications when all notifications are of the same notificationStoragePriority. |
| certificate | 0..1 | RO | See clause 9.6.1.3. |
| e2ESecurityCapabilities | 0..1 (L) | RO | See clause 9.6.1.3. |
| NOTE: All the attributes of this resource type can be changed by an offline configuration mechanism, but not over the reference points (all attributes are "RO"). |

### 9.6.4	Resource Type remoteCSE

A <remoteCSE> resource shall represent a Registree CSE that is registered to the Registrar CSE. <remoteCSE> resources shall be located directly under the <CSEBase> resource of Registrar CSE.

Similarly <remoteCSE> resource shall also represent a Registrar CSE. <remoteCSE> resource shall be located directly under the <CSEBase> resource of Registree CSE.

For example, when CSE1 (Registree CSE) registers with CSE2 (Registrar CSE), there will be two <remoteCSE> resources created: one in CSE1: <CSEBase1>/<remoteCSE2> and one in CSE2: <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> does not mean CSE2 registered with CSE1 in the example above.

Figure 9.6.4-1: Structure of <remoteCSE> resource

The <remoteCSE> resource shall contain the child resources specified in table 9.6.4-1. The <remoteCSE> resource may contain <remoteCSEAnnc> child resources.

Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resources of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <pollingChannel> | 0..1 | See clause 9.6.21. If requestReachability is FALSE, the CSE that created this <remoteCSE> resource should create a <pollingChannel> resource and perform long polling. The <pollingChannel> shall be utilized by the the parent resource. | None |
| [variable] | <schedule> | 0..1 | This resource defines the reachability schedule information of the node. See clause 9.6.9 for <schedule>. | <scheduleAnnc> |
| [variable] | <nodeAnnc> | 0..n | This resource is the <nodeAnnc> resource representing the node where the CSE represented by this <remoteCSE> resource resides. | <nodeAnnc> |

Table 9.6.4-2: Child announced resources of <remoteCSE> resource

| Child Announced Resources of <remoteCSE> | Child Announced Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | Refer to table 9.6.26.1-1 Announced Resource Types | 0..n |  |

The <remoteCSE> resource shall contain the attributes specified in table 9.6.4-3.

Table 9.6.4-3: Attributes of <remoteCSE> resource

| Attributes of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 . | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 . | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 . | NA |
| parentID | 1 | RO | See clause 9.6.1.3 . | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 . | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 . | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 . | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 . | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 . | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 . | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 . | NA |
| cseType | 0..1 | WO | Indicates the type of CSE represented by the created resource. Mandatory for an IN-CSE, hence multiplicity (1). Its presence is subject to SP configuration in case of an ASN-CSE or a MN-CSE. | OA |
| pointOfAccess | 0..1 (L) | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. If this information is not provided, the CSE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the CSE without using the PoA. | OA |
| CSEBase | 1 | WO | The address of the CSEBase resource represented by this <remoteCSE> resource. | OA |
| CSE-ID | 1 | WO | The CSE identifier in SP-relative CSE-ID format (clause 7.2). | OA |
| M2M-Ext-ID | 0..1 | RW | Supported when Registrar is IN-CSE. See clause 7.1.8 where this attribute is described. This attribute is used only for the case of dynamic association of M2M-Ext-ID and CSE-ID. | NA |
| Trigger-Recipient-ID | 0..1 | RW | Supported when Registrar is IN-CSE. See clause 7.1.10 where this attribute is described. This attribute is used only for the case of dynamic association of M2M-Ext-ID and CSE-ID. | NA |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> resource can receive a request from other AE/CSE(s), this attribute is set to "TRUE" otherwise "FALSE" (see note) | OA |
| nodeLink | 0..1 | RW | The resourceID of a <node> resource that hosts the CSE represented by the <remoteCSE> resource. | OA |
| latestE2ERand | 0..1 | RW | An e2ERand which is frequently updated by the CSE associated with this resource. The structure and use of this attribute is described in TS-0001 [2]. The e2ERand is used to establish session keys used in End-to-End Security for Primitives. | MA |
| NOTE: Even if this attribute is set to "FALSE", it does not mean it AE/CSE is always unreachable by all entities. E.g. the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. |

### 9.6.5	Resource Type AE

An <AE> resource shall represent information about an Application Entity registered to a CSE.

Figure 9.6.5-1: Structure of <AE> resource

The <AE> resource shall contain the child resources specified in table 9.6.5-1.

Table 9.6.5-1: Child resources of <AE> resource

| Child Resources of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <schedule> | 0..1 | See clause 9.6.9 | <scheduleAnnc> |
| [variable] | <pollingChannel> | 0..1 | See clause 9.6.21. When the AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. The <pollingChannel> shall be utilized by the the parent resource. | None |

The <AE> resource shall contain the attributes specified in table 9.6.5-2.

Table 9.6.5-2: Attributes of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. Contains the AE-ID-Stem of the AE (see clause 7.2 on identifier formats and clause 10.1.1.2.2 for AE registration procedure). | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| appName | 0..1 | RW | The name of the application, as declared by the application developer(e.g. "HeatingMonitoring"). Several sibling resources may share the appName. | OA |
| App-ID | 1 | WO | The identifier of the Application (see clause 7.1.2). | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..1 (L) | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g. IP address, FQDN, URI). This attribute shall be accessible only by the AE and the Hosting CSE. If this information is not provided, the AE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the AE without using the PoA. | OA |
| ontologyRef | 0..1 | RW | A URI of the ontology used to represent the information that is managed and understood by the AE. | OA |
| requestReachability | 1 | RW | If the AE that created this <AE> resource can receive a request, this attribute is set to "TRUE" otherwise "FALSE" | OA |
| nodeLink | 0..1 | RO | The resourceID of a <node> resource that stores the node specific information where the AE resides. | OA |
| contentSerialization | 0..1 (L) | RW | The list of supported serializations of the Content primitive parameter for receiving a request from its registrar CSE. (e.g. XML, JSON). The list shall be ordered so that the most preferred format comes first. | OA |
| certificate | 0..1 | RO | See clause 9.6.1.3. | OA |
| e2ESecurityCapabilities | 0..1 (L) | RO | See clause 9.6.1.3. | MA |

### -----------------------End of change 3-------------------------------------------

### Add the following new sub-clauses of clause 9.6

### -----------------------Start of change 4-------------------------------------------

### 9.6.x Resource Types e2EKeyCSE

The <e2EKeyCSE> resource is a virtual resource because it does not have a representation. It is the child resource of a <CSEBase> resource.

The <e2EKeyCSE> resource is used for the 4-way exchange of TLS handshake messages for the purposes of establishing a pairwiseE2EKey between the CSE or AE which created the resource and the CSE associated with the parent resource. A high level description is provided clause 11.4, with normative details in TS-0003 [2].

The <e2EKeyCSE> resource supports only the CREATE and UPDATE operations. Permission to create the <e2EKeyCSE> resource is dictated by the access control policies of the parent resource. Permission to update the <e2EKeyCSE> resource is limited to the CSE or AE which created the resource

### 9.6.y Resource Type e2ESecurityPrimitiveExchange

The <e2ESecurityPrimitiveExchange> resource is a virtual resource because it does not have a representation. It is the child resource of a <CSEBase> resource.

The <e2ESecurityPrimitiveExchange> resource is used for end-to-end security of primitives. A high level description is provided clause 11.4, with normative details in TS-0003 [2].

### -----------------------End of change 4---------------------------------------------

### Add the following new sub-clauses of clause 10.2

### -----------------------Start of change 5 -------------------------------------------

### 10.2.x	<e2EKeyCSE> Resource Procedures

#### 10.2.x.1	Create <e2EKeyCSE>

This procedure shall be used for creating a <e2EKeyCSE> resource.

Table 10.2.x.1-1: <e2EKeyCSE> CREATE

| <e2EKeyCSE> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: According to clause 8.1.2. To: The address of the <CSEBase> resource associated with the CSE with which the Originator wishes to establish a pairwiseE2EKey. Operation: Create (C) Request Identifier: According to clause 8.1.2. Content: this parameter shall be the base64 encoding of the first TLS handshake message. Resource Type: indicating <e2EKeyCSE> resource type. The following parameters shall not be present: Role, Result Content, Result Persistence, Group Request Identifier, Filter Criteria, and Discovery Result Type. Other optional parameters listed in clause 8.1.2 may be present if the parameters are allowed for the Create operation. |
| Processing at Originator before sending Request | The Originator forms a first TLS handshake message is described in TS-0003 [2]. |
| Processing at Receiver | The Receiver shall perform the following steps: The Receiver shall check if the Originator has the appropriate privileges for performing the request. Privileges are part of the attribute accessControlPolicyIDs of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyIDs of the parent resource. This lookup of accessControlPolicyIDs attribute in case of non-existence shall be performed recursively until a parent with such an attribute is found. The Receiver shall assign a Resource-ID to the resource to be created. The Receiver shall record, internally, the identifier of the Originator as the creator of the resource. Access to the resource shall be limited to this CSE or AE. The Receiver shall apply base64 decoding to the Content parameter, producing the first TLS handshake message. The Receiver shall process the first TLS handshake message as described in TS-0003 [2], resulting in the second handshake message. The Receiver shall apply base64 encoding to the second TLS handshake. |
| Information in Response message | Response Status Code: According to clause 8.1.3. Request Identifier: According to clause 8.1.3. Content: this parameter shall contain the resource-ID assigned to the created resource, and the base64 encoding of the second TLS handshake message. Other optional parameters listed in clause 8.1.3 may be present if the parameters are allowed for the Create operation. |
| Processing at Originator after receiving Response | The Originator shall perform the following steps: The Originator shall process the extract the Content parameter to extract The Resource-ID of the created resource, and The base64 encoding of the second TLS handshake message. The Originator shall apply base64 decoding to this encoding to producing the second TLS handshake message. The Originator shall process the second TLS handshake message as described in TS-0003 [2], resulting in the third TLS handshake message. The Originator shall apply base64 encoding to the third TLS handshake. The Originator shall initiate the Update <e2EKeyCSE> procedure using the extracted Resource-ID, as described in clause 10.2.x.3. |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.x.2	Retrieve <e2EKeyCSE>

The Retrieve procedure shall not apply to the <e2EKeyCSE> resource.

#### 10.2.x.3	Update <e2EKeyCSE>

This procedure shall be used for updating the attributes and the actual data of a <e2EKeyCSE> resource.

Table 10.2.x.3-1: <e2EKeyCSE> UPDATE

| <e2EKeyCSE> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: According to clause 8.1.2 To: The address corresponding to the Resource-ID received in the corresponding Create procedure (see Clause 10.2.x.1). Operation: Update (U) Request Identifier: According to clause 8.1.2. Content: this parameter shall be the base64 encoding of the third TLS handshake message. The following parameters shall not be present: Role, Result Content, Result Persistence, Group Request Identifier, Filter Criteria, and Discovery Result Type. Other optional parameters listed in clause 8.1.2 may be present if the parameters are allowed for the Update operation. |
| Processing at Originator before sending Request | See “Processing at Originator after receiving Response” in Clause 10.2.x.1. |
| Processing at Receiver | The Receiver shall perform the following steps: The Receiver shall allow access only if the Originator is the creator of the virtual resource. The Receiver shall apply base64 decoding to the Content parameter, producing the third TLS handshake message. The Receiver shall process the third TLS handshake message as described in TS-0003 [2], resulting in the fourth TLS handshake message and generation of the pairwiseE2EKey for use in end-to-end security protocols with the Originator. The Receiver shall apply base64 encoding to the fourth TLS handshake. |
| Information in Response message | Response Status Code: According to clause 8.1.3. Request Identifier: According to clause 8.1.3. Content: this parameter shall be the base64 encoding of the fourth TLS handshake message. Other optional parameters listed in clause 8.1.3 may be present if the parameters are allowed for the Update operation. |
| Processing at Originator after receiving Response | The Originator shall perform the following steps: The Originator shall apply base64 decoding to the Content parameter, producing the fourth TLS handshake message. The Originator shall process the fourth TLS handshake message as described in TS-0003 [2], resulting in generation of the pairwiseE2EKey for use in end-to-end security protocols with the Receiver. |
| Exceptions | According to clause 10.1.3 |

#### 10.2.x.4	Delete <e2EKeyCSE>

The Delete procedure shall not apply to the <e2EKeyCSE> resource.

The <e2EKeyCSE> resource is not accessed after the TLS handshake is either successfully completed or is abandoned. The <e2EKeyCSE> resource can be deleted via management operations not defined in this version of the specification.

### 10.2.y	<e2ESecurityPrimitiveExchange> Resource Procedures

#### 10.2.y.1	Create <e2ESecurityPrimitiveExchange>

The Create procedure shall not apply to the <e2ESecurityPrimitiveExchange> resource. The <e2ESecurityPrimitiveExchange> resource is created when its parent <CSEBase> resource is created.

#### 10.2.y.2	Retrieve <e2ESecurityPrimitiveExchange>

The Retrieve procedure shall not apply to the <e2ESecurityPrimitiveExchange> resource.

#### 10.2.y.3	Update <e2ESecurityPrimitiveExchange>

This procedure enables the transport of secured oneM2M primitives so CSEs which are not the Originator or Receiver do not need to be trusted with the confidentiality and integrity of the primitive.  The primitive to be secured is called the inner primitive, and the primitive which is used to transport a secured inner primitive is called the outer primitive.

Table 10.2.y.3-1: <e2ESecurityPrimitiveExchange> UPDATE

| <e2ESecurityPrimitiveExchange>UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | From: According to clause 8.1.2 To: The address corresponding to the Resource-ID received in the corresponding Create procedure (see Clause 10.2.x.1). Operation: Update (U) Request Identifier: According to clause 8.1.2. Content: See “Processing at Originator before sending Request” The following parameters shall not be present: Role, Result Content, Result Persistence, Group Request Identifier, Filter Criteria, and Discovery Result Type. Other optional parameters listed in clause 8.1.2 may be present if the parameters are allowed for the Update operation. |
| Processing at Originator before sending Request | The Originator shall perform the following steps: The Originator and Registrar may interact to establish an E2E Security for Primitives (ESPrim) session key as described in TS-0003 [2]. Once established, an ESPrim session key can be used for multiple exchanges of inner requests and response primitives. The Originator shall compose the inner request primitive (the request to be secured) according to the present specification. The Originator shall apply JSON Web Encryption (JWE) [i.RFC7516] or XML Encryption [i.XMLENC] to the inner request primitive, using the ESPrim session key, as described in TS-0003 [2]. The resulting serialization is placed in the Content parameter of the request. |
| Processing at Receiver | The Receiver shall perform the following steps: The Receiver shall check if the Originator has the appropriate privileges for performing the request. Privileges are part of the attribute accessControlPolicyIDs of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyIDs of the parent resource. This lookup of accessControlPolicyIDs attribute in case of non-existence shall be performed recursively until a parent with such an attribute is found. The Receiver shall apply JWE or XML-Encryption (as appropriate) to the Content primitive parameter, using the ESPrim session key, as described in TS-0003 [2]. This produces the inner request primitive. The Receiver shall process the inner request primitive according to the present specification, and produces a corresponding inner response primitive. The Receiver shall apply JWE or XML Encryption to the inner response primitive, using the ESPrim session key, as described in TS-0003 [2]. The resulting serialization is placed in the Content parameter o the request. The Receiver shall apply the security protocol (JWE or XML Encryption) used in the corresponding request. |
| Information in Response message | Response Status Code: According to clause 8.1.3. Request Identifier: According to clause 8.1.3. Content: See “Processing at Receiver” Other optional parameters listed in clause 8.1.3 may be present if the parameters are allowed for the Update operation. |
| Processing at Originator after receiving Response | The Originator shall perform the following steps: The Originator shall apply JWE or XML-Encryption (as appropriate) to the Content primitive parameter, using the ESPrim session key, as described in TS-0003 [2]. This produces the inner response primitive. The Originator shall process the inner response primitive according to the present specification. |
| Exceptions | According to clause 10.1.3 |

#### 10.2.y.4	Delete <e2ESecurityPrimitiveExchange>

The Delete procedure shall not apply to the <e2ESecurityPrimitiveExchange> resource. The <e2ESecurityPrimitiveExchange> resource is deleted when its parent <CSEBase> resource is deleted.

### -----------------------End of change 5---------------------------------------------

### Add new clause 11.4 “End-to-End Security”

### -----------------------Start of change 6-------------------------------------------

## 11.4	Overview of End-to-End Security Procedures

This clause introduces the high level procedures following for end-to-end security, for securing data and/or oneM2M primitives so CSEs do not need to be trusted with the confidentiality and integrity of the data and/or oneM2M primitives. These procedures shall be implemented as specified in the oneM2M security specification [2]. The following end-to-end security frameworks are provided:

- End-to-End Security for Data (ESData) provides an interoperable framework for protecting data that ends up transported using oneM2M reference points, in order that so transited CSEs do not need to be trusted with that data. The data could typically compose all or part of an attribute value (e.g. content attribute value of a <contentInstance> resource) or a primitive parameter (e.g. a signed, self-contained access token communicated in a request primitive to obtain dynamic authorization).

- End-to-End Security for Primitives (ESPrim) provides an interoperable framework for securing oneM2M primitives so CSEs do not need to be trusted with the confidentiality and integrity of the primitive.  ESPrim provides mutual authentication, confidentiality, integrity protection and a freshness guarantee (bounding the age of secured primitives). ESPrim uses the Update <e2ESecurityPrimitiveExchange> procedure for transporting the secured request primitive and corresponding secured response primitive.

- End-to-End Security Key Establishment (ESKey) provides a mechanism for two end-points to use certificates for establishing a pairwiseE2EKey. This mechanism is similar to certificate-based remote security provisioning, but removes the participation of an M2M Enrolment Function. The pairwiseE2EKey may then be used to derive keys for ESData or ESPrim. ESKey uses the <e2EKeyCSE> resource to establish a pairwiseE2EKey with a CSE.

### -----------------------End of change 6 ---------------------------------------------

### Add the following references to clause 2.2 “Informative References”

### -------------Start of Changes to Clause 2.2 “Informative References”----------

[i.RFC7516]	IETF RFC 7516: “JSON Web Encryption (JWE)”, 2015

[i.XMLENC]	W3C Recommendation “XML Encryption Syntax and Processing v1.1”, 2013, http://www.w3.org/TR/xmlenc-core1/

### -------------End of Changes to Clause 2.2 “Informative References”----------