| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 21 |
| Source:* | Datang, China Mobile, ZTE, China Unicom, CATR |
| Date:* | 2016-01-18 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Min Zuo, China Mobile, zuomin@chinamobile.com Hao Wu, ZTE, wu.hao18@zte.com.cn Peng Wang, China Unicom, wangpeng@chinaunicom.cn Song Luo, CATR, luosong@catr.cn |
| Reason for Change/s:* | New defined resource type and procedures for supporting role based access control |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.5.0 |
| Clauses/Sub Clauses* | Clause 9.6.5 Resource Type AE Clause 9.6.x Resource Type role Clause 10.2.y <role> Resource Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes new <role> resource and corresponding procedures for supporting the Role Based Access Control.

### -----------------------Start of change 1---------------------------------------------

### 9.6.5	Resource Type AE

An <AE> resource shall represent information about an Application Entity registered to a CSE.

Figure 9.6.5-1: Structure of <AE> resource

The <AE> resource shall contain the child resources specified in table 9.6.5-1.

Table 9.6.5-1: Child resources of <AE> resource

| Child Resources of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <schedule> | 0..1 | See clause 9.6.9 | <scheduleAnnc> |
| [variable] | <pollingChannel> | 0..1 | See clause 9.6.21. When the AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. The <pollingChannel> shall be utilized by the the parent resource. | None |
| [variable] | <role> | 0..1 | See clause 9.6.x. | <roleAnnc> |

The <AE> resource shall contain the attributes specified in table 9.6.5-2.

Table 9.6.5-2: Attributes of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. Contains the AE-ID-Stem of the AE (see clause 7.2 on identifier formats and clause 10.1.1.2.2 for AE registration procedure). | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| appName | 0..1 | RW | The name of the application, as declared by the application developer(e.g. "HeatingMonitoring"). Several sibling resources may share the appName. | OA |
| App-ID | 1 | WO | The identifier of the Application (see clause 7.1.2). | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..1 (L) | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g. IP address, FQDN, URI). This attribute shall be accessible only by the AE and the Hosting CSE. If this information is not provided, the AE should use <pollingChannel> resource. Then the Hosting CSE can forward a request to the AE without using the PoA. | OA |
| ontologyRef | 0..1 | RW | A URI of the ontology used to represent the information that is managed and understood by the AE. | OA |
| requestReachability | 1 | RW | If the AE that created this <AE> resource can receive a request, this attribute is set to "TRUE" otherwise "FALSE" | OA |
| nodeLink | 0..1 | RO | The resourceID of a <node> resource that stores the node specific information where the AE resides. | OA |
| contentSerialization | 0..1 (L) | RW | The list of supported serializations of the Content primitive parameter for receiving a request from its registrar CSE. (e.g. XML, JSON). The list shall be ordered so that the most preferred format comes first. | OA |

### -----------------------End of change 1 ---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### 9.6.x	Resource Type role

The <role> resource is used to describe a role that is assigned to an AE or CSE. <role> resources shall be located directly under the <AE> or <remoteCSE> resource on the Registrar CSE. An <AE> resource or <remoteCES> resource could have zero or multiple <role> child resources.

<role> resources shall be created by a CSE which have the privilege of assigning roles to AEs or CSEs. Information about what roles are assigned to an AE or CSE can be obtained through retrieving <role> resources under its <AE> or <remoteCSE> resource.

A <role> resource shall not be modified once created. A role assignment update shall be done through deleting the old <role> resource and then creating a new <role> resource.

Figure 9.6.x-1: Structure of <role> resource

The <role> resource shall contain the child resources specified in table 9.6.x-1.

Table 9.6.x-1: Child resources of <role> resource

| Child Resources of <role> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

The <role> resource shall contain the attributes specified in table 9.6.x-2

Table 9.6.x-2: Attributes of <role> resource

| Attributes of <role> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| roleID | 1 | RO | The identifier of the role. |
| issuer | 1 | RO | The identifier of the CSE that is responsible for assigning roles to AEs and/or CSEs. |
| notBefore | 1 | RO | Start time of the role can be used for access control. |
| notAfter | 1 | RO | End time of the role can be used for access control. |
| roleName | 0..1 | RO | Human readable name of the <role>. |
| appIDs | 0..1 | RO | List of App-IDs that are used for determining this role should be used for access control in which M2M applications. The role holder or access control decision maker could use this information for selecting applicable roles in access control. |
| tokenLink | 0..1 | RO | This attribute contains a reference to a <token> resource in which a token containing this role is stored. |

### -----------------------End of change 2 ---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

### 10.2.y	<role> Resource Procedures

#### 10.2.y.1	Introduction

This clause describes the management procedures for the <role> resource. Since <role> resource is immutable once created, there is no procedure for updating it.

#### 10.2.y.2	Create <role>

This procedure shall be used for creating a <role> resource.

Table 10.2.y.2-1: <role> CREATE

| <role> CREATE |
| --- |
| Associated Reference Point | Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: From: Identifier of the CSE that initiates the request To: Address of <AE> or <remoteCSE> resource where the <role> resource is intended to be created in the Registrar CSE of the AE or CSE. Content: The resource content shall provide the information as defined in clause 9.6.x |
| Processing at Originator before sending Request | According to clause 10.1.1.1 with the following additions: The Originator shall be a CSE. The Request shall address a <AE> or <remoteCSE> resource of a Hosting CSE which is the Registrar CSE of the AE or CSE to which the role is assigned. |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <role> resource, according to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.y.3	Retrieve <role>

This procedure shall be used for retrieving the attributes of a <role> resource.

Table 10.2.y.2-1: <role> RETRIEVE

| <role> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <role> resource as defined in clause 9.6.x |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.y.4	Update <role>

The Update operation shall not apply to <role> resource.

#### 10.2.y.5	Delete <role>

This procedure shall be used for deleting an existing <role> resource.

Table 10.2.y.5-1: <role> DELETE

| <role> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### -----------------------End of change 3 ---------------------------------------------