| Input Contribution |
| --- |
| Meeting ID* | ARC#21 |
| Title:* | AllJoyn interface mapping |
| Source:* | LG Electronics, SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Uploaded Date:* | 2016-01-11 |
| Document(s) Impacted* | TS-0021 oneM2M-AllJoyn interworking |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes three AllJoyn base service mapping in Annex B as supposed to be:

6.4.2 AllJoyn base service mapping The list of AllJoyn base services [i.2]: OnBoarding, Configuration, Notification, ControlPanel, Audio Streaming The present document specifies base services mapping for Configuration, Notification, ControlPanel. See Annex B AllJoyn base service mapping. Editor’s Note: Annex B is TBD. OnBoarding service is intended to support AllJoyn network onboarding (Wi-Fi connection support) for the device that does not have user interface. This is out of scope for oneM2M interworking. Audio Streaming is also out of scope since oneM2M system does not support in-bound streaming feature.

In R01: alignment with the AllJoyn generic mapping (contribution: ARC-2016-xxxx), in the resource tree figure, “xx” means fix name and italic means variable name.

In R02: added “callStatus” attribute to the methodCall flexContainers (containerDefinition = alljoynMethodCall)

## ----------------------- Start of text 1 -----------------------

Annex <B> (Normative) AllJoyn interface mapping to oneM2M resource structure

B.1	Notification service

B.1.1	Notification interface

AllJoyn Notification(org.alljoyn.Notification) interface and its members shall be mapped with the following structure.

Figure B.1.1-1: Structure of Notification interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.1.1-1: Attribute values of org.alljoyn.Notification resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn. Notification” | AllJoyn interface name |
| containerDefinition | “alljoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1”. |

Editor’s Note: enumeration value for flexContainer will be updated once it is set in Core Protocol TS. And this will affect the whole Annex B.

Table B.1.1-2: Attribute values of Notify resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “Notify” | “Notify” signal |

Table B.1.1-3: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | (variable) | Signal message |

B.1.2	Notification Producer interface

AllJoyn Notification Producer(org.alljoyn.Notification.Producer)  interface and its members shall be mapped with the following structure.

Figure B.1.2-1: Structure of Notification Producer interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.1.2-1: Attribute values of org.alljoyn.Notification.Producer resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.Notification.Producer” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1”. |

Table B.1.2-2: Attribute values of Dismiss resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Dismiss” | “Dismiss” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.1.2-3: Attribute values of call resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | key-value pair of “msgId” |
| callStatus | (variable) |  |

Editor’s Note: callStatus value should be an enumeration value as a definitive set, and this shall be determined in the Core Protocol TS. Once it is done in PRO WG, then the possible enumeration values would be specified in the “Description” column. This affects the rest part of this present specification for the “callStatus” attribute.

B.1.3	Dismisser interface

AllJoyn Dismisser(org.alljoyn.Notification.Dismisser)  interface and its members shall be mapped with the following structure.

Figure B.1.3-1: Structure of Dismisser interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.1.3-1: Attribute values of org.alljoyn.Notification.Dismisser resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.Notification.Dismisser” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1”. |

Table B.1.3-2: Attribute values of Dismiss resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “Dismiss” | “Dismiss” signal |

Table B.1.3-3: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | (variable) | Signal message |

B.2	Control Panel service

B.2.1	Container interface

AllJoyn Container(org.alljoyn.ControlPanel.Container)  interface and its members shall be mapped with the following structure.

Figure B.2.1-1: Structure of Container interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.1-1: Attribute values of org.alljoyn.ControlPanel.Container resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.ControlPanel.Container” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.1-2: Attribute values of States resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “OptParams” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only state “enabled” |

Table B.2.1-3: Attribute values of OptParams resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “OptParams” | “OptParams” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only “Container” widget metadata |

Table B.2.1-4: Attribute values of MetadataChange resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “MetadataChange” | “MetadataChange” signal |

Table B.2.1-5: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | “changed” | Notificiation that the metadata is changed |

B.2.2	Property interface

AllJoyn Property(org.alljoyn.ControlPanel.Property)  interface and its members shall be mapped with the following structure.

Figure B.2.2-1: Structure of Property interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.2-1: Attribute values of org.alljoyn.ControlPanel.Property resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “org.alljoyn.ControlPanel.Container” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.2-2: Attribute values of States resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only state “enabled” and “writable” |

Table B.2.2-3: Attribute values of OptParams resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “OptParams” | “OptParams” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only “OptParams” widget metadata |

Table B.2.2-4: Attribute values of Value resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Value” | “Value” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| requestedValue | (variable) | Suggested Property value |
| currentValue | (variable) | Current Property value |

Table B.2.2-5: Attribute values of ValueChanged resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “ValueChanged” | “ValueChanged” signal |

Table B.2.2-6: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | (variable) | Key-value pairs of property or metadata |

B.2.3	LabelProperty interface

AllJoyn LabelProperty(org.alljoyn.ControlPanel.LabelProperty)  interface and its members shall be mapped with the following structure.

Figure B.2.3-1: Structure of LabelProperty interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.3-1: Attribute values of org.alljoyn.ControlPanel.LabelProperty resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.ControlPanel.LabelProperty” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.3-2: Attribute values of States resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only state “enabled” |

Table B.2.3-3: Attribute values of Label resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Label” | “Label” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only label |

Table B.2.3-4: Attribute values of OptParams resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “pOptParams” | “OptParams” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only LabelProperty widget metadata |

Table B.2.3-5: Attribute values of MetadataChange resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “MetadataChange” | “MetadataChange” signal |

Table B.2.3-6: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | “changed” | Notificiation that the metadata is changed |

B.2.4	Action interface

AllJoyn Action(org.alljoyn.ControlPanel.Action)  interface and its members shall be mapped with the following structure.

Figure B.2.4-1: Structure of Action interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.4-1: Attribute values of org.alljoyn.ControlPanel.Action resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.ControlPanel.Container” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.4-2: Attribute values of States resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only state “enabled” |

Table B.2.4-3: Attribute values of OptParams resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “OptParams” | “OptParams” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only “Action” widget metadata |

Table B.2.4-4: Attribute values of Exec resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Exec” | “Exec” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.4-5: Attribute values of call resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.4-6: Attribute values of MetadataChange resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “MetadataChange” | “MetadataChange” signal |

Table B.2.4-7: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | “changed” | Notificiation that the metadata is changed |

B.2.5	NotificationAction interface

AllJoyn NotificationAction(org.alljoyn.ControlPanel.Container)  interface and its members shall be mapped with the following structure.

Figure B.2.5-1: Structure of NotificationAction interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.5-1: Attribute values of org.alljoyn.ControlPanel.NotificationAction resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.ControlPanel.NotificationAction” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.5-2: Attribute values of Dismiss resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “Dismiss” | “Dismiss” signal |

Table B.2.5-3: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | “dismiss” | Dismiss the notification panel |

B.2.6	Dialog interface

AllJoyn Dialog(org.alljoyn.ControlPanel.Dialog)  interface and its members shall be mapped with the following structure.

Figure B.2.6-1: Structure of Dialog interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.6-1: Attribute values of org.alljoyn.ControlPanel.Dialog resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “ControlPanel.Dialog” | org.alljoyn.ControlPanel.Dialog interface |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.6-2: Attribute values of States resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only state “enabled” |

Table B.2.6-3: Attribute values of OptParams resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “OptParams” | “OptParams” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only “Dialog” widget metadata |

Table B.2.4-4: Attribute values of Message resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only display message |

Table B.2.4-5: Attribute values of NumActions resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only number of actions |

Table B.2.6-6: Attribute values of Action1 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Action1” | “Action1” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.6-7: Attribute values of call1 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.6-8: Attribute values of Action2 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Action2” | “Action2” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.6-9: Attribute values of call2 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.6-10: Attribute values of Action3 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Action3” | “Action3” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.6-11: Attribute values of call3 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.6-12: Attribute values of MetadataChange resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “MetadataChange” | “MetadataChange” signal |

Table B.2.6-13: Attribute values of signal resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| resourceName | (variable) |  |
| content | “changed” | Notificiation that the metadata is changed |

B.2.7	ListProperty interface

AllJoyn ListProperty(org.alljoyn.ControlPanel.ListProperty)  interface and its members shall be mapped with the following structure.

Figure B.2.7-1: Structure of ListProperty interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.2.7-1: Attribute values of org.alljoyn.ControlPanel.ListProperty resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.ControlPanel.ListProperty” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.7-2: Attribute values of States resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “States” | “States” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only state “enabled” |

Table B.2.7-3: Attribute values of OptParams resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “OptParams” | “OptParams” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only “ListProperty” widget metadata |

Table B.2.7-4: Attribute values of Value resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Value” | “Value” property |
| containerDefinition | “alljoynProperty” | AllJoyn interface property |
| currentValue | (variable) | Read-only list of records |

Table B.2.7-5: Attribute values of Add resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Add” | “Add” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.7-6: Attribute values of call1 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.7-7: Attribute values of Delete resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Delete” | “Delete” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.7-8: Attribute values of call2 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | recordID |
| callStatus | (variable) |  |

Table B.2.7-9: Attribute values of View resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “View” | “View” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.7-10: Attribute values of call3 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | recordID |
| callStatus | (variable) |  |

Table B.2.7-11: Attribute values of Update resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Update” | “Update” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.7-12: Attribute values of call4 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | recordID |
| callStatus | (variable) |  |

Table B.2.7-13: Attribute values of Confirm resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Confirm” | “Confirm” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.7-14: Attribute values of call5 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.7-15: Attribute values of Cancel resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Cancel” | “Cancel” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.7-16: Attribute values of call6 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.7-17: Attribute values of ValueChanged resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “Changed” | “ValueChanged” signal |

Table B.2.7-18: Attribute values of signal1 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| content | “ValueChanged”” | Notificiation that the property value is changed |

Table B.2.7-19: Attribute values of MetadataChanged resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “3” | Enumeration value for the container resource type |
| resourceName | “Changed” | “MetadataChanged” signal |

Table B.2.7-20: Attribute values of signal2 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “4” | Enumeration value for the contentInstance resource type |
| content | “MetadataChanged” | Notificiation that the metadata is changed |

B.3	Configuration service

B.3.1	Config interface

AllJoyn Config(org.alljoyn.Config)  interface and its members shall be mapped with the following structure.

Figure B.3.1-1: Structure of Config interface mapping

Each resource in the figure above shall have the attribute values as follows.

Table B.3.1-1: Attribute values of Config resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “org.alljoyn.Config” | AllJoyn interface name |
| containerDefinition | “allJoynInterface” | AllJoyn interface |
| version | “1” | Version property value is “1” |

Table B.2.3-2: Attribute values of FactoryReset resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “FactoryReset” | “FactoryReset” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.3-3: Attribute values of call1 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.3-4: Attribute values of Restart resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “Restart” | “Restart” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.3-5: Attribute values of call2 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| callStatus | (variable) |  |

Table B.2.3-6: Attribute values of SetPasscode resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “SetPasscode” | “SetPasscode” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.3-7: Attribute values of call3 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | “daeonRealm” and “newPasscode” parameter |
| callStatus | (variable) |  |

Table B.2.3-8: Attribute values of GetConfigurations resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “GetConfigurations” | “GetConfigurations” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.3-9: Attribute values of call4 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | “languageTag” parameter |
| callStatus | (variable) |  |

Table B.2.3-10: Attribute values of UpdateConfigurations resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “UpdateConfigurations” | “UpdateConfigurations” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.3-11: Attribute values of call5 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | “languageTag” and “configMap” parameter |
| callStatus | (variable) |  |

Table B.2.3-12: Attribute values of ResetConfigurations resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | “ResetConfigurations” | “ResetConfigurations” method |
| containerDefinition | “alljoynMethod” | AllJoyn interface method |

Table B.2.3-13: Attribute values of call6 resource

| Attribute | Value | Description |
| --- | --- | --- |
| resourceType | “xx” | Enumeration value for the flexContainer resource type |
| resourceName | (variable) |  |
| containerDefinition | “alljoynMethodCall” | AllJoyn interface method call |
| input | (variable) | “languageTag” and “fieldList” parameter |
| callStatus | (variable) |  |

## ----------------------- End of text 1 -----------------------