²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP21 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-01-11 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | For improving Interworking efficiency, (see Input Contribution “ARC-2016-2064- IW - ARC improvement - LWM2M/IW Procedures” for the detailed rational)the <later> resource procedure should support minor modification |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.5.0 |
| Clauses/Sub Clauses* | Clause 10.2.22 <latest> Resource Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 ---------------------------------------------10.2.22	<latest> Resource Procedures

Only Retrieve and Delete operations shall be allowed for the <latest> resource.

#### 10.2.22.1	Retrieve <latest>

This procedure shall apply to the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If there is no <contentInstance> resource in the parent or existing ones are obsolete then 2 situations :

- if there is a subscription on the parent <container> resource with the eventType ‘E’ set (“Retrieval attempt of obsolete or non existing direct child resource for the subscribed-to resource”) , then the Receiver  shall delay the response until a <constantInstance> resource is available in the parent <container> resource  or until an implementation-dependent timeout has elapsed.

- If no notification occurred in a) or if an implementation-dependent timeout has elapsed, then the Receiver shall response with an error.

This procedure is the same as the procedures in clause 10.2.19.3 <contentInstance> RETRIEVE

-----------------------End of change 1 --------------------------------------------------