²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP21 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-01-11 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | Adding DELETE and CREATE Procedures Improving RETRIEVE procedure |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0014 V0.7 |
| Clauses/Sub Clauses* | Clause 6.4 LWM2M Object Transport and Interworking |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 -------------------------------------------------

### 6.4.2	LWM2M Interworking Mechanisms

#### 6.4.2.1	Introduction

.

These following sub-clauses specify the sequences of operations involved for each type of  supported oneM2M requests following the general procedures specified  in clause 10 (CREATE,RETRIEVE, DELETE) as used within the context of the interworking for this present document

### -----------------------End of change 1 --------------------------------------------------

### ---------------------- Start of change 2 --------------------------------------------------

#### 6.4.2.2	Relevant Interworked Resource Settings

A LWM2M Object Instance is represented in oneM2M as a <container> resource with 2 direct children resource types:  a <subscription> resource and a <contentInstance> resource.

For supporting the LWM2M interworking process, a few attributes for the <container> resource and the <notification> resource shall have a specified set of parameters

- Attributes of <container> resource

| Attributes of <container> resource | Value |
| --- | --- |
| accessControlPolicyIDs | ACP set (see Clause 6.6) |
| maxNrOfInstances | 1 |

Table 6.4.2.2-1 <container> resource – Relevant Interworked Attributes

- Child  resource types of <container> resource

Child resources of <container> resource

<contentInstance> resource

<subscription> resource

Table 6.4.2.2-2 <container> resource – Relevaent Child resource types

- Attributes of <subscription> resource

| Attributes of <subscription> resource | Description / Value |
| --- | --- |
| notificationURI | IPE URI |
| eventType | Deletion of the subscribed-to resource , Creation of a direct child of the subscribed-to resource , E. Attempted retrieval of an obsolete or non existing direct child of the subscribed-to resource when this retrieval is performed by a RETRIEVE request targeting the subscribed-to resource with the Result Content parameter set to either “child-resources” or “attributes+child-resources” |

Table 6.4.2.2-3 <subscription> resource – Relevant Interworked Attributes

### -----------------------End of change 2 --------------------------------------------------

#### 6.4.2.3	oneM2M RETRIEVE Procedure

This procedure describes the retrieval of a resource using the oneM2M RETRIEVE request. The information contained within the resource is related to the LWM2M Objects Instances that are interworked through the IPE. This clause shall be treated in conformance with the RETRIEVE Procedure specified in TS-0001 clause 10.1.2.

The Receiver performs local processing to verify the existence of requested Resource and checks privileges for retrieving the information related to the resource. After successful verification, the Receiver shall return the requested information according to the procedures for the type of interworking (e.g. Transparent, Semantically Enabled) as described in clause 7 and 8, otherwise an error response shall be returned to the Originator

Figure 6.4.2.3-1: Procedure for Retrieving a Resource (TS-0001 Clause 10)

The target of the request is a <container> resource, the ResultContent and FilterCriteria parameters of the request  (TS-0001 clause 8.1.2 ) specify the nature of the information to retrieve.

| Request parameter : ResultContent | Request parameter : FilterCriteria | Effect |
| --- | --- | --- |
| child-resources | resourceType = contentInstance | Retrieval of LWM2M Object Instance |
| attributes (default) | labels, attribute | Metadata retrieval of LWM2M Object Instance. |

Specific steps of the Receiver Processing according to the interworking process shall be as followed:

Step 001:  Find and verify the targeted <container> resource of the request : the resourceName corresponds to clause 6.3.2

Step 002: Using the Hosting CSE Access Control mechanisms, check for Access Control Policy attached to the <container> resource of the request

Step 003: On successful validation of the Access Control Policy, proceed to fetch the requested information:

- If   “ResultContent” is “attributes”, jump to Step 4

- If  “ResultContent” is “child-resources” and “FilterCriteria” is “contentInstance”, the associated <latest> resource of the targeted container is considered

Step 003.1: if  the <latest> resource is obsolete or not existing,  an event for Retrieval attempt (eventType ‘E’) is triggered to the Entity that subscribed to the event (i.e. IPE); as a Blocking Procedure, the Hosting CSE shall monitor the arrival of the new data or decide to report a timeout error in jumping to Step 004

Step 003.1.1: On receiving the event of type ‘E’  (eventType ‘E’) the IPE performs a LWM2M READ request on the Object Instance of the targeted LWM2M Client.

Step 003.1.2: Once the targeted Object Instance is available to IPE, the IPE creates and populates with that data       the  <latest> resource of the requested <container> resource.

Step 003.2: the up-to-date information is available in the <latest> resource

Step 004: The Hosting CSE returns the appropriate response back to the Originator (e.g. Acknowledgment, Errors, and Data)

Note: as an OBSERVATION has been set up on the targeted LWM2M Object Instance, the automatic synchronization between the Object Instance and its representation in the Hosting CSE is performed. Further oneM2M accesses to the resource should be simplified in minimizing impact of Step003 (up-to-date data already present from the Hosting CSE resources).

General Exceptions:

The targeted resource/attribute in To parameter does not exist. The Receiver responds with an error.

The Originator does not have privileges to retrieve information stored in the resource on the Receiver. The Receiver responds with an error.

### ----------------------- Start of change 2 -------------------------------------------------

##### 6.4.2.4	oneM2M CREATE Procedure

This procedure describes the update of a LWM2M Object Instance in a LWM2M Client using the oneM2M CREATE request The information contained in the request via the Content parameter (TS-0001 Clause 8.2.1) will be used to update an Object Instance in the LWM2M context. .

This clause shall be treated in conformance with the CREATE Procedure specified in TS-0001 clause 10.1.2 and 10.2.22.2.

Figure 6.4.2.3-2: Procedure for Creating a Resource (TS-0001 Clause 10)

The target of the request is a <container> resource, the ResourceType parameters of the request  (TS-0001 clause 8.1.2 ) specify the type of the resource to create.

| Request parameter :ResourceType | Effect |
| --- | --- |
| contentInstance | Replacement of the <latest> resource by a new one |

In LWM2M Interworking context, if there is already an existing <contentInstance> resource, creating a new one shall violates the policy defined in the parent <container> resource regarding the  maxNrOfInstances which shall be set to 1.Then the oldest <contentInstance> resources shall be removed from the <container> to enable the  creation of the new <contentInstance> resource.

In any case, a notification is sent to the IPE, which subscribed to the parent <container> resource with the eventType ‘C’ (Creation of a direct child of the subscribed-to resource ). The IPE shall use that notification to update the LWM2M resource model with the new data received (“Content” parameter of the request)

Specific steps of the Receiver Processing according to the interworking process shall be as followed:

Step 001:  Find and verify the <container> resource of the request : the resourceName corresponds to clause 6.3.2

Step 002: Using the Hosting CSE Access Control mechanisms, check for Access Control Policy attached to the <container> resource of the request

Step 003: On unsuccessful validation of the Access Control Policy, jump to step 4

Step 003.1: When according to the request, a  <contentInstance> resource is created, an event for  Child Creation (eventType ‘C’)   is triggered to the Entity that subscribed to that event (i.e. IPE).

Step 003.2: On receiving the event of type ‘C’ the IPE - via the Mca reference point – get the data from the created  <latest> resource and propagates the updated data to the related Object Instance in the LWM2M Client.

Step 004: The Hosting CSE returns the appropriate response back to the Originator (e.g. Acknowledgment, Errors)

General Exceptions:

- The Originator does not have the privileges to create a resource on the Receiver. The Receiver responds with an error.

- The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an error.

3 The provided information in Content is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an error.

### ---------------------- End of change 2 -------------------------------------------------

### ----------------------- Start of change 3 -------------------------------------------------

6.4.2.5	oneM2M DELETE ProcedureThis procedure describes the removal of a LWM2M Object Instance within a LWM2M Client using the oneM2M DELETE request .

This clause shall be treated in corformance with the DELETE Procedure specified in TS-0001 clause 10.1.4.

Figure 6.4.2.3-3 : Procedure for Deleting a resource (TS-0001 Clause 10)

Specific steps of the Receiver Processing according to the interworking process shall be  as followed:

Step 001:  Find and verify the <container> resource of the request : the resourceName corresponds to clause 6.3.2

Step 002: Using the Hosting CSE Access Control mechanisms, check for Access Control Policy attached to the <container> resource of the request

Step 003: On unsuccessful validation of the Access Control Policy, jump to step 4

Step 003.1: When the <container> resource is deleted  an event (eventType ‘B’: Deletion of subscribed-to resource)   is triggered to the Entity that subscribed to that event (i.e. IPE).

Step 003.2: On receiving the event type ‘B’, the IPE requests the LWM2M Client to delete the Object Instance related to  the <container> resource.

Step 003.2 : on Object Instance deletion, the LWM2M Client performs a De-Registration operation to the IPE.

Step 00.3.3 :  via the Mca reference point, the IPE communicates to the Hosting CSE the status of this De-Registration.

Step 004: The Hosting CSE returns the appropriate response back to the Originator (e.g. Success, Errors)

### ----------------------- End of change 3 -------------------------------------------------