| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#21 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Vinod Choyi, Interdigital, vinod.choyi@interdigital.com Dale Seed, Interdigital, dale.seed@InterDigital.com |
| Date:* | 2016-01-18 |
| Contact:* | As above |
| Reason for Change/s:* | Support for Dynamic Authorization. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 and v2.5.0 |
| Clauses/Sub Clauses* | Clause 8.1 “General Communication Flow Scheme on Mca and Mcc Reference Points”, 9.6 “Resource Types”, 10.2 “Resource Type-Specific Procedures”, Clause 11 “Trust Enabling Architecture” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Corresponding CRs for Security Solutions TS-0003 are in SEC-2016-0021-TS-0003_CR_Dynamic_Authorization_stage_2_text.

This CR refers to <dynamicAuthorizationConsultation> resource type; associated changes are found in:

- ARC-2016-0032-dynamic_authorization_consultation_resource_R2,

- ARC-2016-0033-dynamic_authorization_consultation_procedures_R2,

with associated TS-0003 changes in SEC-2016-0007-Consultation_based_Dynamic_Authorization_System.

Yellow highlighting has been used indicate references and cross references whose values are not yet finalized and which are to be assigned by the rapporteur, e.g. “[i.RFC7516]” or “clause 9.6.y”.

### Apply changes to clause 8.1.2

### -----------------------Start of change 1 -------------------------------------------

Discovery Result Type: Optional Discovery result format. This parameter applies to discovery related requests (see filterUsage in table 8.1.2-2 and clause 10.2.6) to indicate the preference of the Originator for the format of returned information in the result of the operation. This parameter shall take on one of the following values reflecting the options in clause 9.3.1:

Hierarchical  addressing method.

Non-hierarchical addressing method.

For example if Discovery Result Type is set to Non-hierarchical addressing method, then the request Originator indicates that the discovered resources should be in the form of Non-hierarchical address.

The absence of the parameter implies that the result shall be in the form of a  Hierarchical address.

Access Token Consultation Indicator: Optional parameter used to indicate that the Originator supports Access Token Consultation procedure (a Dynamic Authorization procedure), and the Originator may attempt the Access Token Consultation procedure if the Receiver provides an Access Token Consultation Initiation parameter in the response.

Access Tokens: Optional parameter used to transport Access Tokens applicable to the request for use in Dynamic Authorization.

### -----------------------End of change 1 -------------------------------------------

### Apply changes to table 8.1.2-3

### -----------------------Start of change 2-------------------------------------------

Table 8.1.2-3: Summary of Request Message Parameters

| Request message parameter | Operation |
| --- | --- |
|  | Create | Retrieve | Update | Delete | Notify |
| Mandatory | Operation - operation to be executed | M | M | M | M | M |
|  | To - the address of the target resource on the target CSE | M | M | M | M | M |
|  | From - the identifier of the message Originator | O See NOTE 1 | M | M | M | M |
|  | Request Identifier - uniquely identifies a Request message | M | M | M | M | M |
| Operation dependent | Content - to be transferred | M | O | M | N/A | M |
|  | Resource Type - of resource to be created | M | N/A | N/A | N/A | N/A |
| Optional | Originating Timestamp - when the message was built | O | O | O | O | O |
|  | Request Expiration Timestamp - when the request message expires | O | O | O | O | O |
|  | Result Expiration Timestamp - when the result message expires | O | O | O | O | O |
|  | Operational Execution Time - the time when the specified operation is to be executed by the target CSE | O | O | O | O | O |
|  | Response Type - type of response that shall be sent to the Originator | O | O | O | O | O |
|  | Result Persistence - the duration for which the reference containing the responses is to persist | O | O | O | O | N/A |
|  | Result Content - the expected components of the result | O | O | O | O | N/A |
|  | Event Category - indicates how and when the system should deliver the message | O | O | O | O | O |
|  | Delivery Aggregation - aggregation of requests to the same target CSE is to be used | O | O | O | O | O |
|  | Group Request Identifier - Identifier added to the group request that is to be fanned out to each member of the group | O | O | O | O | O |
|  | Filter Criteria - conditions for filtered retrieve operation | N/A | O | O | O | N/A |
|  | Discovery Result Type - format of information returned for Discovery operation | N/A | O | N/A | N/A | N/A |
|  | Access Token Consultation Indicator – indicating that the Originator shall attempt Access Token Consultation (for Dynamic Authorization) if initiating by the Receiver | O | O | O | O | O |
|  | Access Tokens – for use in dynamic authorization | O | O | O | O | O |
| NOTE 1: From parameter shall be optional in case of an AE CREATE request and mandatory for all other requests. |

### -----------------------End of change 2 -------------------------------------------

### Apply changes to clause 8.1.3

### -----------------------Start of change 3 -------------------------------------------

Event Category: event category: Indicates the event category that should be used to handle this response. The definition of event category is the same as in the case of requests in clause 8.1.2.

Example usage of "event category" set to specific value X: When the response is targeted to an entity that is different from the Transit CSE currently processing the response message and is not an AE registered with the Transit CSE that is currently processing the response message, the response may be stored in the Transit CSE that is currently processing the response on the way to the destination of the response message until it is allowed by provisioned policies for that event category X to use a communication link to reach the next CSE on a path to the destination of the response message or until the result expiration timestamp is expired.

Access Token Request Information: Optional parameter which may be used for requesting Access Tokens from Dynamic Authorization Systems.

Table 8.1.3-1 summarizes the parameters specified in this clause for the Response messages, showing any differences as applied to successful C, R, U, D or N operations, and unsuccessful operations. "M" indicates mandatory, "O" indicates optional, "N/A" indicates "not applicable".

Table 8.1.3-1: Summary of Response Message Parameters

| Response message parameter/success or not | Response Status Code |
| --- | --- |
|  | Ack | successful: Operation = Create | successful: Operation = Retrieve | successful. Operation = Update | successful. Operation = Delete | successful Operation = Notify | unsuccessful Operation = C,R,U,D or N |
| Response Status Code - successful, unsuccessful, ack | M | M | M | M | M | M | M |
| Request Identifier - uniquely identifies a Request message | M | M | M | M | M | M | M |
| Content - to be transferred | O (address of <request> resource if response is ACK of a non-blocking request) | O (The address and/or the content of the created resource) | M (the retrieved resource content or aggregated contents or an address list) | O (The content replaced in an existing resource. The content of the new attributes created. The name of the attributes deleted.) | O (The content actually deleted) | N/A | O (Additional error info) |
| To - the identifier of the Originator or the Transit CSE that sent the corresponding non-blocking request | O | O | O | O | O | O | O |
| From - the identifier of the Receiver | O | O | O | O | O | O | O |
| Originating Timestamp - when the message was built | O | O | O | O | O | O | O |
| Result Expiration Timestamp - when the message expires | O | O | O | O | O | N/A | O |
| Event Category - what event category shall be used for the response message | O | O | O | O | O | O | O |
| Content Status | N/A | N/A | M | N/A | N/A | N/A | N/A |
| Content Offset | N/A | N/A | M | N/A | N/A | N/A | N/A |
| Access Token Request Information | N/A | N/A | N/A | N/A | N/A | N/A | O |

### -----------------------End of change 3 -------------------------------------------

### Apply changes to clause 9.6.2 Resource Type accessControlPolicy

### -----------------------Start of change 4 -------------------------------------------

The set of access control rules represented in privileges and selfPrivileges attributes are comprised of 3-tuples (accessControlOriginators, accessControlDynamicAuthorizations, accessControlContexts, accessControlOperations) with parameters shown in table 9.6.2-3 which are further described in the following clauses.

If privileges attribute contains no 3-tuples then this represent an empty set of the access control rules.

The selPrivileges attribute shall contain at least one 3-tuples.

The CSE access granting mechanism shall follow the procedure described in oneM2M TS-0003 [2] in clause 7.1 (Access Control Mechanism).

Table 9.6.2-3: Parameters in access-control-rule-tuples

| Name | Mandatory/Optional | Description |
| --- | --- | --- |
| accessControlOriginators | Optional | One or both of these parameters shall be present | See clause 9.6.2.1 |
| accessControlDynamicAuthorizations | Optional |  | See clause 9.6.2.4 |
| accessControlContexts | Optional | See clause 9.6.2.2 |
| accessControlOperations | Mandatory | See clause 9.6.2.3 |

#### 9.6.2.1	accessControlOriginators

The set of Originators is described as a list of parameters, where the types of the parameter can vary within the list. Table 9.6.2.1-1 describes the supported types of parameters in accessControlOriginators. The following Originator privilege types shall be considered for access control policy check by the CSE.

Table 9.6.2.1-1: Types of Parameters in accessControlOriginators

| Name | Description |
| --- | --- |
| domain | A SP domain or SP sub-domain |
| originatorID | CSE-ID, AE-ID or the resource-ID of a <group> resource that contains the AE or CSE that represents the Originator. |
| all | Any Originators are allowed to access the resource within the accessControlOriginators constraints |

When the originatorID is the resource-ID of  a <group> resource which contains <AE> or <remoteCSE> as member, the Hosting CSE of the resource shall check if the originator of the request matches one of  the members in the memberIDs attribute of the <group> resource (e.g. by retrieving the <group> resource). If the <group> resource cannot be retrieved or doesn’t exist, the request shall be rejected.

#### 9.6.2.2	accessControlContexts

The accessControlContexts contains a list, where each element of the list, when present, represents a context that is permitted to use this access control rule. Each request context is described by a set of parameters, where the types of the parameters can vary within the set. Table 9.6.2.2-1 describes the supported types of parameters in accessControlContexts.

The following Originator accessControlContexts shall be considered for access control policy check by the CSE.

Table 9.6.2.2-1: Types of Parameters in accessControlContexts

| Name | Description |
| --- | --- |
| accessControlTimeWindow | Represents a time window constraint which is compared against the time that the request is received at the Hosting CSE. |
| accessControlLocationRegion | Represents a location region constraint which is compared against the location of the Originator of the request. |
| accessControlIpIPAddress | Represents an IP address constraint or IP address block constraint which is compared against the IP address of the Originator of the request. |

#### 9.6.2.3	accessControlOperations

The accessControlOperations represents the set of operations that are authorized using this access control rule. Table 9.6.2.3-1 describes the supported set of operations that are authorized by accessControlOperations.

### -----------------------End of change 4-------------------------------------------

### Add new clause 9.6.2.4	“accessControlDynAuthRoles” (New for R01)

### -----------------------Start of change 5-------------------------------------------

#### 9.6.2.4	accessControlDynAuthRoles

The accessControlDynAuthRoles represents the Dynamic Authorization Rules authorized for the access control rule. The accessControlDynamicAuthorizations is a list of accessControlDynAuthRoleInstruction parameters, where an accessControlDynAuthRoleInstruction parameter contains one or both of the following

- accessControlAbsDynAuthRole (Mandatory):  Absolute Dynamic Authorization Role which is authorized using this access control rule.

  - If this parameter is not present, then the Originator may be authorized if the Originator is associated with the Absolute Dynamic Authorization Role for the request. Further details are provided in clause 7.1.5 of TS-0003 [2].

- accessControlDASServerId (Optional): A URI or AE-ID of a DAS Server with which the Dynamic Authorization Consultation may be performed. The presence of this parameter indicates that Dynamic Authorization Consultation may be performed with the identified DAS Server for issuing DAO(s).

### -----------------------End of change 5-------------------------------------------

### Apply changes to 11.3.4 “M2M Authorization Procedure”

### -----------------------Start of change 6-------------------------------------------

### 11.3.4	M2M Authorization Procedure

The M2M authorization procedure controls access to resources and services by CSEs and AEs. This procedure requires that the Originator has been identified to an M2M Authentication Function and mutually authenticated and associated with an M2M Service Subscription. Authorization depends on:

The privileges set by the M2M Service Subscription associated with the Originator (e.g. service/role assigned to the Originator).

These privileges are set-up based on the access control policies associated with the accessed resource or service. They condition the allowed operations (e.g. CREATE) based on the Originator's privileges and other access control attributes (e.g. contextual attributes such as time or geographic location).

Dynamic Authorization Objects (DAOs) associated with the request, consisting of

  - All non-expired DAOs associated with the Originator and provided to the Hosting CSE via Direct Consultation.

  - All non-expired DAOs associated with the Originator and either present in the Access Tokens parameter of the request or identified in the Access Tokens parameter of the request, as specified in clause 7.x.2.4 of TS-0003 [2].

The authorization/access grant involves an Access Decision step to determine what the authenticated CSE or AE can actually access, by evaluating applicable access control policies based on the CSE or AE privileges. Access Decision is described in one M2M Security Solutions Technical Specification [2].

The following set of access control policy attributes shall be available for an Access Decision.

Access control attributes of Originator (e.g. Service Role, CSE_IDs, AE-IDs, etc.).

Access control attributes of Dynamic Authorization Roles.

Access control attributes of Environment/Context (e.g. time, day, IP address, etc.).

Access control attributes of Operations (e.g.  Create, Execute, etc.).

The M2M Service Provider/administrator and owner of resources are responsible to establish access control policies that determine by whom, in what context and what operations may be performed upon those resources. If the requesting entity satisfies the owner's access control policy, then the access to the resource is granted.

In the event that the request does not satisfy the any of the owner’s access control policies, a Hosting CSE shall first initiate Direct Consultation. Relevant details of Direct Consultation are provided clause 11.5.1. If Direct Consultation results in the requesting entity satisfying the owner's access control policy, then the access to the resource is granted.

In the event that the Direct Consultation does not result in granting access to the resource  and the Access Token Consultation Indicator s present in the request, then the Hosting CSE shall initiate Access Token Consultation as indicated in the applicable <accessControlPolicy> resources (linked to the resourced resource), which may result in Access Token Request Information parameter being included in the unsuccessful response to the Originator. The Access Token Request Information is used to request the Dynamic Authorization System to issue a Dynamic Authorization Object(s) and provide corresponding Access Token(s) to the Originator. The Originator then resends its request, this time adding any Access Tokens received from the Dynamic Authorization System. Relevant details of Access Token Consultation are provided clause 11.5.2.

The authorization procedure shall be implemented as specified in the oneM2M Security Solutions Technical Specification [2].

### -----------------------End of change 6-------------------------------------------

### Add new clause 11.5 “Functional Architecture Specifications for Dynamic Authorization”

### -----------------------Start of change 7-------------------------------------------

## 11.5	Functional Architecture Specifications for Dynamic Authorization Procedures

### 11.5.1	Functional Architecture Specifications for the Direct Consultation Procedure

The parameters exchanged for Direct Consultation, and the corresponding processing, are specified in clause 7.x.2.5, TS-0003 [2]. The present clause specifies the details for retrieval of parameters from resource, and transportation of parameter.  Further details for each step in the present clause can be obtained by examining the corresponding steps in clause 7.x.2.5, TS-0003 [2].

The message flow for the Direct Consultation Procedure is shown in Figure 11.5.1-1 “Message flow showing transport details of the Direct Consultation Procedure”, and described in the following text.

Figure 11.5.1-1: Message flow showing transport details for the Direct Consultation Procedure. The step numbers are aligned with the procedure in clause 7.x.2.5, TS-0003 [2]

  - The Hosting CSE examines the <accessControlPolicy> resources and <dynamicAuthorizationConsultation> resources to obtain the AE-IDs for a Dynamic Authorization Server (DAS) Server AEs with which to perform Direct Consultation. The Hosting CSE selects a DAS Server AE and forms a Direct Consultation Information parameter for the corresponding DAS Server.

4.	The Hosting CSE shall send a Notify request primitive to the DAS Server AE, with the following details specific to Direct Consultation

  - The Security Information parameter shall indicate that the Notify response primitive is for a Direct Consultation procedure.

  - The Content parameter shall contain the Direct Consultation Information parameter.

  - The DAS Server AE shall extract and parse the Direct Consultation Information parameter from the Content parameter of the received message. The DAS Server AE provides the resulting parameters to the DAS Server. The DAS Server may decide to one or more of the following

  - Change (static) access control information dictating the access control decision of the Hosting CSE.

  - Issue DAO(s) and form a DAO List parameter containing these DAO(s).

  - Generate dynamicACPInfo which will be used by the Hosting CSE to create a dynamic <accesscontrolPolicy> resource.

8.	The DAS Server shall send a Notify response primitive via the DAS Server AE to the HCSE, with the following details specific to Direct Consultation.

  - The Security Information parameter shall indicate that the Notify response primitive is for a Direct Consultation procedure.

  - If the previous steps resulted in DAO List parameter and/or dynamicACPInfo parameter, then these parameters shall be included in the Content parameter, otherwise the Content parameter shall not be present.

9.	The Hosting CSE shall processes the Content parameter (if present),

  - Generating DAO List parameter to extract and verify the DAO(s)

  - Creating a dynamic <accessControlPolicy> resource from dynamicACPInfo.

10.	The Hosting CSE repeats the access decision mechanism.

NOTE: The outcome of the access decision can have changed as a result of changes to access control information or a new DAO(s) received from the DAS Server.

### 11.5.2	Access Token Consultation Procedure Transport Specification

The parameters exchanged for Access Token Consultation, and the corresponding processing, are specified in clause 7.x.2.6, TS-0003 [2]. The present clause specifies the details for retrieval of parameters from resource, and transportation of parameter.  Further details for each step in the present clause can be obtained by examining the corresponding steps in clause 7.x.2.6, TS-0003 [2].

The message flow for the Access Token Consultation Procedure is shown in Figure 11.5.2-1 “Message flow for the Access Token Consultation Procedure”, and described in the following text.

Figure 11.5.2-1: Message flow for the Access Token Consultation Procedure

- The HCSE forms the Access Token Request Information primitive parameter.

- The HCSE shall send, to the Originator, an unsuccessful resource access response with the following details specific to the Access Token Consultation procedure:

  - The Response Status Code shall be set to “UNAUTHORIZED”.

  - The Access Token Request Information primitive parameter from step 1 shall be included.

  - The Assigned DAO Identifiers primitive parameter may present, as described in step 2, clause 7.x.2.4, TS-0003 [2].

- The Originator processes the Assigned DAO Identifiers primitive parameter (see Step 3, clause 7.x.2.4, TS-0003 [2]). The Originator provides the DAS Client with the Access Token Request Information primitive parameter and other information about the original resource access request.

4-10: The DAS Client, on behalf of the Originator, interacts with one or more DAS Servers to request the issuance of DAO(s) for the Originator. If successful, DAS Server provides the DAS Client with Initial Access Token(s).

11.	The DAS Client forwards the Initial Access Token(s) and associated metadata to the Originator.

12.	The Originator forms a new the resource access request, this time adding the Initial Access Token(s) to the Access Tokens primitive parameter.

### -----------------------End of change 7 ---------------------------------------------

# Comments

This doesn’t look right!