| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 21 |
| Source:* | Datang, China Unicom, CATR |
| Date:* | 2016-01-18 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Peng Wang, China Unicom, wangpeng@chinaunicom.cn Song Luo, CATR, luosong@catr.cn |
| Reason for Change/s:* | New defined resource types and procedures for supporting distributed authorization system |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.5.0 |
| Clauses/Sub Clauses* | 9.6.m Resource Type policyDecisionPoint 9.6.n Resource Type policyRetrievalPoint 9.6.o Resource Type policyInformationPoint 10.2.x <policyDecisionPoint> Resource Procedures 10.2.y <policyRetrievalPoint> Resource Procedures 10.2.z <policyInformationPoint> Resource Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The following figure shows how the proposed virtual resource types are used in distributed authorization scenario.

### -----------------------Start of change 1---------------------------------------------

### 9.6.m	Resource Type policyDecisionPoint

The <policyDecisionPoint> resource is a virtual resource that shall be located directly under the <CSEBase> resource. When a RETRIEVE Request addresses the <policyDecisionPoint> resource, a PDP process is triggered. The access control decision request should be included in the Content parameter of the Request, and the access control decision response should be included in the Content parameter of the Response.

The <policyDecisionPoint> resource inherits the access control policies applying to its parent <CSEBase> resource.

### 9.6.n	Resource Type policyRetrievalPoint

The <policyRetrievalPoint> resource is a virtual resource that shall be located directly under the <CSEBase> resource. When a RETRIEVE Request addresses the <policyRetrievalPoint> resource, a PRP process is triggered. The access control policy request should be included in the Content parameter of the Request, and the access control policy response should be included in the Content parameter of the Response.

The <policyRetrievalPoint> resource inherits the access control policies applying to its parent <CSEBase> resource.

### 9.6.o	Resource Type policyInformationPoint

The <policyInformationPoint> resource is a virtual resource that shall be located directly under the <CSEBase> resource. When a RETRIEVE Request addresses the <policyInformationPoint> resource, a PIP process is triggered. The access control attribute request should be included in the Content parameter of the Request,  and the access control attribute response should be included in the Content parameter of the Response.

The <policyInformationPoint> resource inherits the access control policies applying to its parent <CSEBase> resource.

### -----------------------End of change 1 ---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### 10.2.x  <policyDecisionPoint> Resource Procedures

#### 10.2.x.1  Create <policyDecisionPoint>

This procedure shall be used for creating a <policyDecisionPoint> resource.

Table 10.2.x.1-1: <policyDecisionPoint> CREATE

| <policyDecisionPoint> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | According to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.x.2  Retrieve <policyDecisionPoint>

This procedure is used to trigger a PDP process that is bound to a <policyDecisionPoint> virtual resource.

Originator: The Originator should request to obtain an access control decision by using RETRIEVE operation on a <policyDecisionPoint> virtual resource from the Receiver.

Receiver: The Receiver should check if the Originator has RETRIEVE permission on the <policyDecisionPoint> virtual resource. Upon successful validation, the Receiver should make an access control decision based on access control policies. If there is no process bound to the <policyDecisionPoint> virtual resource, the Receiver should respond with an error.

Table 10.2.x.2-1: <policyDecisionPoint> RETRIEVE

| <policyDecisionPoint > RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 with the following additions: From: Identifier of the AE or the CSE that initiates the Request To: Address of the <policyDecisionPoint> virtual resource Content: The representation of the decision request. The parameters contained in it are listed in table 10.2.x.2-2 |
| Processing at Originator before sending Request | The Originator should create a decision request according to an access request. The Originator should request to obtain a decision by using the RETRIEVE operation on a <policyDecisionPoint> virtual resource. The decision request shall be included in the Content parameter of the Request message. |
| Processing at Receiver | The Receiver should perform the following operations: Check if the Originator has RETRIEVE permission on the <policyDecisionPoint> virtual resource Check the validity of the provided parameters Check if the <policyDecisionPoint> virtual resource is bound to a PDP process. Upon successful validation, passing the decision request to the PDP process. The PDP process may contact a PRP to obtain applicable access control policies, and may also contact a PIP to obtain some access control attributes, and then make an access control decision. If the value of adviceIncluded parameter in the request is true, the PDP shall build a set of permitted attribute names and/or a set of permitted child resource types according to access control policies The Receiver should create a decision response according to the decision and respond to the Originator. The decision response should be included in the Content parameter of the Response message. |
| Information in Response message | According to clause 10.1.2 with the following additions: Content: The representation of the access control decision response. The parameters contained in it are listed in table 10.2.x.2-3 |
| Processing at Originator after receiving Response | The Originator should enforce the decision, i.e. either permit or deny the access to resource |
| Exceptions | According to clause 10.1.2 with the following: There is no PDP process bound to the <policyDecisionPoint> virtual resource The provided content of the access control decision request is not in line with the specified structure |

# Table 10.2.x.2-2: Parameters of content in the decision request message

| Parameter | Description | Mandatory/ Optional | Usage in access control mechanism |
| --- | --- | --- | --- |
| To | URI of target resource | M | Selection of access control policies associated with the target resource and selection of access control rules in an access control policy |
| From | Identifier representing the originator of the request | M | Evaluated against accessControlOriginators in access control rules |
| Operation | Requested operation | M | Evaluated against accessControlOperations in access control rules |
| rq_time | Time stamp when the request message was received at the hosting CSE. Obtained by the hosting CSE's system time clock. | O | Validated against accessControlTimeWindow parameter in an access control rule |
| rq_loc | Location information about the originator of the request. Obtained over the Mcn reference point. | O | Validated against accessControlLocationRegion parameter in an access control rule |
| rq_ip | IP source address associated with the IP packets that carry the request message. Obtained over the Mcn reference point. | O | Validated against accessControlIpAddress parameter in an access control rule |
| Role-IDs | List of role identifiers | O | Used in role based access control |
| Token-IDs | List of token identifiers | O | Used for retrieve tokens |
| Tokens | List of tokens | O | Used in token based access control |
| adviceIncluded | which indicates if the advice information can be included in the response | O | This parameter is used to request that the PDP returns a set of permitted attribute names and/or a set of child resource types |

# Table 10.2.x.2-3: Parameters of content in the decision response message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| decision | Result of access control policy evaluation | M |
| statusCode | A code represents what error occurred during evaluation of the decision request | O |
| statusMessage | A free-form description of the status code | O |
| PermittedAttributeNames | List of permitted attribute names | O |
| permittedChildResourceTypes | List of permitted child resources types | O |

#### 10.2.x.3  Update <policyDecisionPoint>

The Update operation shall not apply to <policyDecisionPoint> resource.

#### 10.2.x.4  Delete <policyDecisionPoint>

This procedure shall be used for deleting a <policyDecisionPoint> resource.

Table 10.2.x.4-1: <policyDecisionPoint> DELETE

| <policyDecisionPoint> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### 10.2.y  <policyRetrievalPoint> Resource Procedures

#### 10.2.y.1  Create <policyRetrievalPoint>

This procedure shall be used for creating a <policyRetrievalPoint> resource.

Table 10.2.y.1-1: <policyRetrievalPoint> CREATE

| <policyRetrievalPoint> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | According to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.y.2  Retrieve <policyRetrievalPoint>

This procedure is used to trigger a PRP process that is bound to a <policyRetrievalPoint> virtual resource.

Originator: The Originator should request to obtain access control policies by using RETRIEVE operation on a <policyRetrievalPoint> virtual resource from the Receiver.

Receiver: The Receiver should check if the Originator has RETRIEVE permission on the <policyRetrievalPoint> virtual resource. Upon successful validation, the Receiver should retrieve all applicable access control policies. If there is no process bound to the <policyRetrievalPoint> virtual resource, the Receiver should respond with an error.

Table 10.2.y.2-1: <policyRetrievalPoint> RETRIEVE

| <policyRetrievalPoint > RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 with the following additions: From: Identifier of the AE or the CSE that initiates the Request To: The address of the <policyRetrievalPoint> virtual resource Content: The representation of the policy request. The parameters contained in it are listed in table 10.2.y.2-2 |
| Processing at Originator before sending Request | The Originator should create a policy request according to a decision request. The Originator should request to obtain policies by using the RETRIEVE operation on a <policyRetrievalPoint> virtual resource. The policy request should be included in the Content parameter of the Request message. |
| Processing at Receiver | The Receiver should perform the following operations: Check if the Originator has RETRIEVE permission on the <policyRetrievalPoint> virtual resource Check the validity of the provided parameters Check if the <policyRetrievalPoint> virtual resource is bound to a PRP process. Upon successful validation, passing the policy request to the PRP process. The PRP process retrieves all applicable access control policies according to the policy request. The Receiver should create a policy response using the retrieved access control policies and respond to the Originator. The policy response should be included in the Content parameter of the Response message. |
| Information in Response message | According to clause 10.1.2 with the following additions: Content: The representation of the policy response. The parameters contained in it are listed in table 10.2.y.2-3 |
| Processing at Originator after receiving Response | The Originator should evaluate the decision request using the retrieved the access control policies. |
| Exceptions | According to clause 10.1.2 with the following: There is no PRP process bound to the <policyRetrievalPoint> virtual resource The provided content of the access control policy request is not in line with the specified structure |

# Table 7.y.3.2-2: Parameters of content in the policy request message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| To | URI of target resource | M |
| From | Identifier representing the originator of the request | M |

# Table 7.y.3.2-3: Parameters of content in the policy response message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| Policy Combining Algorithm | Specifying what algorithm shall be used for arriving at an authorization decision given the individual results of evaluation of a set of policies. | M |
| Policies | A set of policies that shall be used to evaluate the access control decision request | M |

#### 10.2.z.3  Update <policyRetrievalPoint>

The Update operation shall not apply to <policyRetrievalPoint> resource.

#### 10.2.y.4  Delete <policyRetrievalPoint>

This procedure shall be used for deleting a <policyRetrievalPoint> resource.

Table 10.2.y.4-1: <policyRetrievalPoint> DELETE

| <policyRetrievalPoint> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### 10.2.z  <policyInformationPoint> Resource Procedures

#### 10.2.z.1  Create <policyInformationPoint>

This procedure shall be used for creating a <policyInformationPoint> resource.

Table 10.2.z.1-1: <policyInformationPoint> CREATE

| <policyInformationPoint> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | According to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.z.2  Retrieve <policyInformationPoint>

This procedure is used to trigger a PIP process that is bound to a <policyInformationPoint> virtual resource.

Originator: The Originator should request to obtain access control attributes by using RETRIEVE operation on a <policyInformationPoint> virtual resource from the Receiver.

Receiver: The Receiver should check if the Originator has RETRIEVE permission on the <policyInformationPoint> virtual resource. Upon successful validation, the Receiver should obtain the requested attributes. If there is no process bound to the <policyInformationPoint> virtual resource, the Receiver should respond with an error.

Table 10.2.z.2-1: <policyInformationPoint> RETRIEVE

| <policyInformationPoint > RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 with the following additions: From: Identifier of the AE or the CSE that initiates the Request To: The address of the <policyInformationPoint> virtual resource Content: The representation of the attribute request. The parameters contained in it are listed in table 10.2.z.2-2 |
| Processing at Originator before sending Request | The Originator should create an attribute request according to an access request. The Originator should request to obtain an attributes by using the RETRIEVE operation on a <policyInformationPoint> virtual resource. The attribute request shall be included in the Content parameter of the Request message. |
| Processing at Receiver | The Receiver should perform the following operations: Check if the Originator has RETRIEVE permission on the <policyInformationPoint> virtual resource Check the validity of the provided parameters Check if the <policyInformationPoint> virtual resource is bound to a PIP process. Upon successful validation, passing the attribute request to the PIP process. The PIP process obtains the requested access control attributes according to the access control attribute request. The Receiver should create an attribute response using the obtained attributes and respond to the Originator. The response should be included in the Content parameter of the Response message. |
| Information in Response message | According to clause 10.1.2 with the following additions: Content: The representation of the attribute response. The parameters contained in it are listed in table 10.2.z.2-3 |
| Processing at Originator after receiving Response | The Originator should evaluate the access control decision request using the retrieved the access control policies and access control attributes |
| Exceptions | According to clause 10.1.2 with the following: There is no PIP process bound to the <policyInformationPoint> virtual resource The provided content of the attribute request is not in line with the specified structure |

# Table 10.2.z.2-2: Parameters of content in the attribute request message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| From | Identifier representing the originator of the request | M |
| Role ID or Token ID | Identifier of a role or token | M |

# Table 10.2.z.2-3: Parameters of content in the attribute response message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| Role or token resource attriburtes | Attributes of a role or token resource | M |

#### 10.2.z.3  Update <policyInformationPoint>

The Update operation shall not apply to <policyInformationPoint> resource.

#### 10.2.z.4  Delete <policyInformationPoint>

This procedure shall be used for deleting a <policyInformationPoint> resource.

Table 10.2.z.4-1: <policyInformationPoint> DELETE

| <policyInformationPoint> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

### -----------------------End of change 2 ---------------------------------------------