| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 21 |
| Source:* | Datang, China Unicom, CATR |
| Date:* | 2016-01-18 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Seongyoon Kim, seongyoon@lge.com Peng Wang, China Unicom, wangpeng@chinaunicom.cn Song Luo, CATR, luosong@catr.cn |
| Reason for Change/s:* | New defined resource types and procedures for supporting distributed authorization system |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.5.0 |
| Clauses/Sub Clauses* | 9.6.m Resource Type policyDecisionPoint 9.6.n Resource Type policyRetrievalPoint 9.6.o Resource Type policyInformationPoint 10.2.x <policyDecisionPoint> Resource Procedures 10.2.y <policyRetrievalPoint> Resource Procedures 10.2.z <policyInformationPoint> Resource Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The following figure shows how the proposed virtual resource types are used in distributed authorization scenario.

## ----------------------- Start of change 1 -----------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. The <CSEBase> resource shall be the root for all resources that are residing in the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource

Figure 9.6.3-1 does not show the child announce resource types defined in table 9.6.3-2.

Editor’s Note: Annex E should be updated to include provisioning of the notification deletion policy.

The <CSEBase> resource shall contain the child resources specified in table 9.6.3-1.

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resources of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See clause 9.6.4 |
| [variable] | <node> | 0..n | See clause 9.6.18 |
| [variable] | <AE> | 0..n | See clause 9.6.5 |
| [variable] | <container> | 0..n | See clause 9.6.6 |
| [variable] | <group> | 0..n | See clause 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <mgmtCmd> | 0..n | See clause 9.6.16 |
| [variable] | <locationPolicy> | 0..n | See clause 9.6.10 |
| [variable] | <statsConfig> | 0..n | See clause 9.6.23 |
| [variable] | <statsCollect> | 0..n | See clause 9.6.25 |
| [variable] | <request> | 0..n | See clause 9.6.12 |
| [variable] | <delivery> | 0..n | See clause 9.6.11 |
| [variable] | <schedule> | 0..1 | This resource defines the reachability schedule information of the entity. The absence of this resource implies the entity is always reachable. See clause 9.6.9 |
| [variable] | <m2mServiceSubscriptionProfile> | 0..n | See clause 9.6.19 |
| [variable] | <serviceSubscribedAppRule> | 0..n | See clause 9.6.29 |
| [variable] | < notificationTargetPolicy > | 0..n | See clause 9.6.32 |
| accessControlDecision | <accessControlDevicion> | 1 | See clause 9.6.X |

Table 9.6.3-2: Child announced resources of <CSEBase> resource

| Child Announced Resources of <CSEBase> | Child Announced Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | Refer Table 9.6.26.1-1 Announced Resource Types | 0..n |  |

The child announced resources of <CSEBase> resource defined in table 9.6.3-2 should be created when an Originator CSE (i.e. original resource Hosting CSE) and a Hosting CSE (i.e. announced resource Hosting CSE) have no registration relationship (e.g. the Originator CSE has not created <remoteCSE> resource on the Hosting CSE).

The <CSEBase> resource shall contain the attributes specified in table 9.6.3-3.

Table 9.6.3-3: Attributes of <CSEBase> resource

| Attributes of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 . |
| resourceID | 1 | RO | See clause 9.6.1.3 . |
| resourceName | 1 | RO | See clause 9.6.1.3 . |
| creationTime | 1 | RO | See clause 9.6.1.3 . |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 . |
| accessControlPolicyIDs | 0..1 (L) | RO | See clause 9.6.1.3 . |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 . |
| cseType | 0..1 | RO | Indicates the type of CSE represented by the created resource. Mandatory for an IN-CSE, hence multiplicity (1). Its presence is subject to SP configuration in case of an ASN-CSE or a MN-CSE. |
| CSE-ID | 1 | RO | The CSE identifier in SP-relative CSE-ID format (clause 7.2). |
| supportedResourceType | 1 (L) | RO | List of the resource types which are supported in the CSE. This attribute contains subset of resource types listed in clause 9.2. This also includes the supported optional attributes for each supported resource type. |
| pointOfAccess | 1 (L) | RO | Represents the list of physical addresses to be used by remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is exposed to its Registree. |
| nodeLink | 0..1 | RO | The resourceID of a <node> resource that represents the node specific information. |
| notificationCongestionPolicy | 0..1 | RO | This attribute applies to CSEs generating subscription notifications. It specifies the rule which is applied when the storage of notifications for each subscriber (an AE or CSE) reaches the maximum storage limit for notifications for that subscriber. E.g. Delete stored notifications of lower notificationStoragePriority to make space for new notifications of higher notificationStoragePriority, or delete stored notifications of older creationTime to make space for new notifications when all notifications are of the same notificationStoragePriority. |
| accessControlDecisionPoint | 0..1 | RO | Indicates the resource ID of <accessControlDecision> where access control decision is made. If it is specified and when Hosting CSE receives a request, the procedure specified in clause 10.2.X.1 shall be performed in the replacement of access control decision made by Hosting CSE. This is appiled to all the resources in Hosting CSE. |
| NOTE: All the attributes of this resource type can be changed by an offline configuration mechanism, but not over the reference points (all attributes are "RO"). |

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

### 9.6.X	Resource Type accessControlDecision

The <accessControlDecision> resource is a virtual resource because it does not have a representation. It is the child resource of a <CSEBase> resource. When a request addresses the <accessControlDecision> resource, the Hosting CSE shall make a access control decision and provide result of the decision as the response of the request.

The <accessControlDecision> resource inherits access control policies that apply to the parent <CSEBase> resource.

## ----------------------- End of change 2 -----------------------

## ----------------------- Start of change 3 -----------------------

### 10.2.X	<accessControlDecision> Resource Procedures

#### 10.2.X.1	Introduction

Only Notify operation shall be allowed for the <accessControlDecision>.

#### 10.2.X.1	Notify <accessControlDecision>

This procedure is used to request access control decision to <accessControlDecision> Hosting CSE and a CSE can be an Originator.

Table 10.2.X.1-1: <accessControlDecision> NOTIFY

| <accessControlDecision> NOTIFY |
| --- |
| Associated Reference Point | Mcc |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: the parameters specified in table 10.2.X.1-2 |
| Processing at Originator before sending Request | According to clause 10.1.5 |
| Processing at Receiver | According to clause 10.1.5 for Step 003: Receiver shall make access control decision based on the information provided in the request. |
| Information in Response message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: the parameters specified in table 10.2.X.1-3 |
| Processing at Originator after receiving Response | According to clause 10.1.5 |
| Exceptions | According to clause 10.1.5 |

# Table 10.2.X.1-2: Parameters of content in Notify request

| Parameter | Description | Mandatory/ Optional | Usage in access control mechanism |
| --- | --- | --- | --- |
| to | URI of target resource | M | Selection of access control policies associated with the target resource and selection of access control rules in an access control policy |
| from | Identifier representing the originator of the request | M | Evaluated against accessControlOriginators in access control rules |
| operation | Requested operation | M | Evaluated against accessControlOperations in access control rules |
| rq_time | Time stamp when the request message was received at the hosting CSE. Obtained by the hosting CSE's system time clock. | O | Validated against accessControlTimeWindow parameter in an access control rule |
| rq_loc | Location information about the originator of the request. Obtained over the Mcn reference point. | O | Validated against accessControlLocationRegion parameter in an access control rule |
| rq_ip | IP source address associated with the IP packets that carry the request message. Obtained over the Mcn reference point. | O | Validated against accessControlIpAddress parameter in an access control rule |
| role-IDs | List of role identifiers | O | Used in role based access control |
| token-IDs | List of token identifiers | O | Used for retrieve tokens |
| tokens | List of tokens | O | Used in token based access control |

# Table 10.2.X.1-3: Parameters of content in Notify response

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| statusCode | A code represents what error occurred during evaluation of the decision request (e.g., granted, access denied, ACP doesn’t exist) | M |

## ----------------------- End of change 3 -----------------------