| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#21 |
| Source:* | LG Electronics |
| Date:* | 2016-01-21 |
| Contact:* | SeungMyeong JEONG, seungmyeong.jeong@lge.com |
| Reason for Change/s:* | AllJoyn IPE registration is not retricted to MN-CSE but allowed for all CSE types |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0018: oneM2M and AllJoyn Interworking MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0021 |
| Clauses/Sub Clauses* | 5.1, 5.2 and 6.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

An IPE can be deployed on any type of M2M Node and be registered with any type of CSEs(ASN/MN/IN-CSE) without any architectural restriction. This is reflected in LWM2M and OIC interworking specifications. This CR proposes to fix the limitation for AllJoyn IPE registration to MN-CSE only.

Also interworking over Mcc’ reference point is covered following the other interworking specs.

### -----------------------Start of change 1-------------------------------------------

# 5	Architecture Model

## 5.1	Reference model

The architecture model followed in the present document is based on the architecture model in Annex F of TS-0001 [1] that describes how interworking between oneM2M CSEs and non-oneM2M systems using specialized Interworking  Proxy application Entities (IPE). The present document descibes the AllJoyn IPE that supports the following reference model:

Figure 5.1-1 AllJoyn interworking reference model

This reference model describes how the oneM2M AEs can interwork with AllJoyn  applications. By the IPE, AllJoyn services are exposed as oneM2M resources and stored in a CSE. AEs access the exposed AllJoyn service resources by the oneM2M APIs.

Note that this figure does not exclude the interworking scenario via Mcc’ reference point.

Editor’s Note: interworking over Mcc’ reference point is FFS.

## 5.2	Composition of the IPE

The AllJoyn IPE consists of AE and AllJoyn application. To provide the interworking functions to other oneM2M entities, the IPE registers to a CSE and communicate with other AllJoyn applications using AllJoyn protocols. The IPE registration is mandatory in oneM2M systems which is not defined in AllJoyn system. AllJoyn discovery and session establishment are needed for the IPE to communicate with other AllJoyn applications.

Figure 5.2-1	Composition of the AllJoyn IPE

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 6.2	AllJoyn IPE registration

To start oneM2M-AllJoyn interworking, the IPE shall perform AE registration procedure to a CSE specified in [1]. When the IPE creates an <AE> resource, the resource shall include the label attribute set as “IPE:AllJoyn” value.

After the registration, the IPE may perform AllJoyn service discovery.

To stop using the interworking function, IPE shall perform AE de-registration procedure.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

MN-CSE

AllJoyn protocol

IPE

Mca

IN-AE / ADN-AE

Mca

IN-CSE

Mcc

AllJoyn Producer Application

AllJoyn Application

Mcc

ASN-CSE

ADN-AE

ASN-AE

Mca

Mca

AllJoyn Application

CSE

AllJoyn Protocol

AllJoyn IPE

Mca

AE

Mca

ASN/MN/IN

CSE

Mcc/Mcc’

MN/IN