²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP21.3 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-02-23 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | LWM2M Provisioning is addressed |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0014 V0.9/0.10 |
| Clauses/Sub Clauses* | 6.x cluases and sub-clause |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 -------------------------------------------------

## 6.1	Introduction

The LWM2M IPE participation in the LWM2M Protocol as described in clause 5 does so in the role of a LWM2M Server to which LWM2M Applications (LWM2M Clients) interact. As a LWM2M Server, the IPE provides the following Architecture Aspects based on the LWM2M Protocol Aspects described in Annex A.2:

- LWM2M Client Provisioning (Bootstrap)

- LWM2M Device and Endpoint Lifecycle (Client Registration)

- LWM2M Object Discovery (Client Registration, Device Management and Service Enablement)

- LWM2M Object Transport and Interworking (Device Management and Service Enablement)

- LWM2M Object Subscription and Notification (Information Reporting)

- LWM2M Object Security

- LWM2M Interworking Proxy Entity Administration

### -----------------------End of change 1 --------------------------------------------------

## 6.2	LWM2M Client Provisioning (Bootstrap)

The current LWM2M Interworking Specification considers LWM2M Clients and LWM2M Servers functionality of the IPE,  have been both provisioned with the proper LWM2M credential materials in accordance to the LWM2M specification (Bootstrap Process) in order to securely communicate together.

## Additionaly, a LWM2M Client connected to a LWM2M Interworking Proxy Equipment, has been bootstrapped also with the LWM2M Access Control Policy information associated to the Object Instances contained in that LWM2M Client. This information will be referenced in the clause 6.7  related to LWM2M Object Security of this document.  The Server IPE of the current LWM2M Interworking Specification having no Bootstrap Server capability, this LWM2M Client provisioning operations shall be part of an out-of-bound process.

## 6.3	LWM2M Device and Endpoint Lifecycle

### ---------------------- Start of change 2 --------------------------------------------------

## 6.7	LWM2M Object Security

### 6.7.1	Introduction

OMA-LWM2M and oneM2M Access Control Policies shall collaborate in order to assure the Interworked resources are accessible according to the oneM2M Authorisation Procedure specified in clause 11.3.4 (M2M Authorization Procedure) of oneM2M TS-0001 [2] and clause 7 (Authorization) of oneM2M TS-0003 [5].

### 6.7.2. 	LWM2M Interworking Access Control Policy

The oneM2M Access Control Policy mechanisms specified in clause 7 of oneM2M TS-0003 [5], shall be used to check and validate the parameters of a request message against the ACPs (<accessControlPolicy> resources) which have been assigned to the accessed resource.

In order to assure a proper LWM2M Interworking with oneM2M, the IPE shall setup the hosting CSE by:

- providing a mandatory set of <accessControlPolicy> (ACPs) resources.

- assigning a proper set of ACPs to the accessControlPolicyIDs attribute of each <container> resource allocated during the CSE registration phase (clause 6.3 LWM2M Object Discovery) .

The process for provisioning the IPE in order to perform such a setup is mentioned in next clause of the present document.

Placed in such a usual oneM2M configuration, Access Control Policy mechanisms specified in clause 7 of oneM2M TS-0003 [5] are fully applicable in this LWM2M Interworking context.

### 6.7.3.  IPE and Object Security provisioning

### In order to provide oneM2M information specified in the previous sub-clause (set of <accessControlPolicy> (ACPs) resources, assignement of accessControlPolicyIDs), the IPE shall be supplied by information such as :

### a list of oneM2M originators and their associated Access Control Rights for the IPE

### a list of oneM2M originators likely to contact the LWM2M Clients with the associated set of authorized operations

### In combining such an information with the Access Control Policy specified in a given LWM2M Client (see section 6.2 LWM2M Client Provisioning) the Inteworking Proxy Equipement shall be able – with or without external computing help (implementation dependant decision) – to provide the oneM2M Access Control Policy material for properly registering LWM2M Object representation in the Hosting CSE as required in the previous sub-clause.

-----------------------End of change 2 --------------------------------------------------