| CHANGE REQUEST |
| --- |
| Meeting:* | <ARC 22> |
| Source:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Date:* | 2016-03-07- |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Provide a feature of the configuration of device communication patterns as one of 3GPP Rel-13 IWK features. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 v0.2.0 |
| Clauses/Sub Clauses* | 8.x4 (new), 1, 5.3, 2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add new section 8.x4 of TR-0024 3GPP Rel13 IWK (WI-0037) for Configuration of Device Communication Patterns feature. The contents are summarized as below.

- General concept for Configuration of Device Communication Pattern feature

- What are the Communication Pattern parameters

- General procedure for Configuration of Device Communication Patterns

- Relationshp between resources (existing and new)

There is no impact to the oneM2M Release1.

Note):

Number of discussions for this topics have been done at ARC20.1, ARC20.2 and e-mails by another contributions ARC-2015-2290(-R01,R02,R03). This contribution is resolving comments on these discussions.

R03: To be corrected TR-0024 based on the agreed CRs of TS-0001 and some editorial correction of TR-0024.

R04/R05: To be fixed TR-0024 based on the e-mail comments at ARC 21.1 conference for shynchronization aspects and others.

R06: To be fixed TR-0024 based on the e-mail comments at ARC 21.2.

R07/R08: To be fixed TR-0024 based on the e-mail comments after ARC21.2.

- Modify the procedure and its description (8.4.3)

- Modify the announced resources and attributes, and add attributes “announceTo”, “announcedAttribute”, “provideToNSE”(new) (8.4.4)

R09: To be fixed unclarified portion of R08 for  TR-0024.

R10: To be fixed for TR-0024 based on ARC21.3 and e-mail discussions.

R11: To be optimized with new template of TR-0024 section 8, and agreed CRs of TS-0001.

R12: To be corrected as agreed CRs of TS-0001.

R13: To be adapted to new agreed template in ARC-2016-0168R05-3GPP_Rel13_IWK_BDT_TR-0024.

### -----------------------Start of change 1----(new section)---------------------------------------

### 8.x  Configuration of Traffic Patterns

#### 8.x.1  Description

M2M devices that have predicable communication behaviour – e.g. in the form of repeating Traffic Patterns – can profit in terms of reduction of signalling, energy saving, fewer sleep/awake transitions, etc., when their Traffic Patterns are communicated to the underlying network.

For example, 3GPP devices could use new 3GPP power savings features such as eDRX (extended discontinuous reception) and PSM (Power Saving Mode) on LTE devices.

Also the underlying network can benefit from being informed about a device’s Traffic Patterns by the oneM2M System.

For example, if the IN-CSE knows the device’s Traffic Patterns and transmits them to an underlying 3GPP network, then this information can be used by a 3GPP network to set the device’s “Maximum Response Time” (3GPP Term) to tune the UE’s DRX and PSM parameters.

Thus the network will benefit because the UE will have fewer sleep/wake transitions and unnecessary signalling in the network can be avoided.  Also, if the IN-CSE knows when the device is awake then data can be sent to the device exactly at the time when the device is listening, thus requiring the network to buffer less data for unavailable devices.

The purpose of the Configuration of Traffic Patterns feature is to provide a means to the oneM2M System  to inform the Underlying Network on parameters that can be used for optimizing the processing at the Underlying Network for a specific Field Domain Node. The feature includes the following functionalities:

- An Application Entity (AE) or a Common Service Entity (CSE) shall be able to provide information on the communication behavior of a Field Domain Node (ASN or MN) to the underlying network.

- To that purpose the AE or CSE shall be able to set Traffic Patterns of a particular Field Domain Node via the Mca or Mcc reference point of a IN-CSE,

  - The Field Domain Node is addressed using the (NodeID, AE-IDs) of the Node

- The IN-CSE shall in turn use the Mcn interface towards the Underlying Network to provide information on Traffic Patterns of a the Field Domain Node.

  - The IN-CSE uses the M2M-Ext-ID to identify the Node towards the Underlying Network.

#### 8.x.2	3GPP Release-13 MTC Procedure

oneM2M uses the 3GPP Release-13 MTC feature for Configuration of Device Communication Patterns in the Underlying Network by using the oneM2M Traffic Patterns resources to provide the corresponding 3GPP information. 
To that purpose the IN-CSE translates the oneM2M Traffic Patterns (TP) resource into a 3GPP Device Communication Pattern (CP) parameters.

A signalling sequence for provisioning of CP parameters is described in the sub-clause 5.10.2 of 3GPP TS 23.682 [i.5]. Following figure 8.x4.2-1 provides the signalling sequence derived from the 3GPP specification with oneM2M terminologies mapping.

Figure 8.x4.2-1:  Signalling sequence for provisioning of CP Parameters

3GPP TS 23.682 [i.5] makes assumptions for SCS/AS and SCEF of step 1 and step 2 as below.

==== Begin citation from 3GPP TS 23.682 =====

1.	The SCS/AS sends an Update Request (External Identifier or MSISDN, SCS/AS Identifier, SCS/AS Reference ID(s), CP parameter set(s), validity time(s), SCS/AS Reference ID(s) for Deletion) message to the SCEF.

NOTE 1:	The SCS/AS uses this procedure to add, change or delete some or all of the CP parameter sets of the UE, e.g. if the AS is aware that the UE has started or stopped moving for a significant time period, especially if the AS is instructing the UE to do so, then the SCS/AS provides the corresponding CP parameter set(s) and its validity time to the SCEF. The interface between SCEF and SCS/AS is outside the scope of 3GPP and the messages in the Figure are exemplary.

2.	The SCEF checks if the SCS/AS is authorised to send CP requests. The SCEF filters and the selects the CP parameter sets(s) for add/modify/delete based on operator policy or configuration.

NOTE 2:	If there are several CP parameter sets active for one UE, then the SCEF assures that the different CP parameter sets are not overlapping, e.g. based on the Scheduled communication time and/or Communication duration time parameters.

EXAMPLE 1:	For example, one CP parameter set may indicate that the UE is scheduled to communicate at 04:00 every day for 30 seconds, and another CP parameter set may indicate that the UE is scheduled to communicate at 23:30 every day for 45 seconds. These would be non-overlapping CP parameter sets.

EXAMPLE 2:	As a second example, if one CP parameter set indicated that the UE is scheduled to communicate at 04:00 every day for 30 seconds and another CP parameter set indicated that the UE is scheduled to communicate at 04:00 every day for 90 seconds, the two CP parameter sets would be overlapping.

In this release, to avoid receiving CP parameter sets from multiple SCEFs that might be overlapping, the HSS shall accept CP parameter sets from only a single SCEF for a given UE.

==== End citation from 3GPP TS 23.682 =====

3GPP TS 23.682 [i.5] defines the request message of step 3 as below.

==== Begin citation from 3GPP TS 23.682 =====

The SCEF sends Update CP Parameter Request (External Identifier or MSISDN, SCEF Reference ID(s), SCEF Address, CP parameter set(s), validity time(s), SCEF Reference ID(s) for Deletion) messages to the HSS for delivering the selected CP parameter set(s) per UE. There may be multiple CP parameter sets included in this message where each CP parameter set for addition or modification has been determined to be non-overlapping with other CP parameter sets either included in the message or already provisioned for a given UE. The SCEF derives the SCEF Reference (IDs) for CP parameter sets to be sent to the HSS based on the SCS/AS Reference ID(s) from the SCS/AS.

NOTE 3:	A request for deletion of a CP parameter set from the SCS/AS may result in a request for modification of the non-overlapping CP parameter set by the SCEF.

==== End citation from 3GPP TS 23.682 =====

Example: In the  case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the request. The S6t uses one of Diameter Application protocols defined by 3GPP. The request on the S6t reference point for the configuration of the CP parameter sets (a CIR command) must include a User-Identifier AVP (either an External Identifeir or a MSISDN of the UE), may include one or more AESE-Communication-Pattern AVP. An AESE-Communication-Pattern AVP must include a SCEF-ID AVP (represent the ID of the IN-CSE or M2M-SP-ID), may include a SCEF-Reference-ID AVP (assigned by the IN-CSE or M2M-SP to identify the configuration of CP parameter sets uniquely) , may include one or more Communication-Pattern-Set AVP. A Communication-Pattern-Set AVP may include AVPs for Periodic-Communication-Indicator, Communication-Duration-Time, Periodic-Time, one or more Scheduled-Communication-Time, Stationary-Indication, and Validity-Time.

3GPP TS 23.682 [i.5] defines the response message of step 5 as below.

==== Begin citation from 3GPP TS 23.682 =====

The HSS sends Update CP Parameter Response (SCEF Reference ID, Cause) message to the SCEF. The cause value indicates successful subscription update or the reason of failed subscription update.

==== End citation from 3GPP TS 23.682 =====

Example); In the  case that  the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the response. The response on the S6t reference point for the configuration of the CP parameter sets (a CIA command) must include either Result-Code AVP or Experimental-Result AVP, may include a User-Identifier AVP if successful case, may include one or more AESE-Communication-Pattern-Config-Status AVP. An AESE-Communication-Pattern-Config-Status AVP must include the SCEF-Reference-ID AVP (same value in the request), may include the SCEF-ID (same value in the request) and an AESE-Error-Report AVP. Refer to the 3GPP TS29.336 for the detailed protocol description.

The actual parameters for the request and response messages in above steps 3 and 5 are defined by 3GPP TS 29.336 [i.10] section 7 and 8 for S6t reference point.

#### 8.x.3  3GPP Parameters

A set of Traffic pattern (TP) parameters can be associated with a Traffic Pattern of one or multiple field domain nodes and are defined in the table below.

A Field Domain Node can be associated with one or multiple Traffic Patterns. At any time only a single Traffic Pattern can be associated with a Field Domain Node.

The IN-CSE shall assure that different Traffic Patterns for a Node are not overlapping at any point in time.

A combination of the following TP parameters can be set for a Traffic Pattern

Table 8.x4.3-1: Traffic Pattern parameters

| TP parameter | Description |
| --- | --- |
| TP Periodic communication indicator | Identifies whether the Node communicates periodically or not, e.g. only on demand. |
| TP Communication duration time | Duration interval time of periodic communication [may be used together with TP periodic communication indicator] Example: 5 minutes |
| TP Time period | Interval Time of periodic communication [may be used together with TP periodic communication indicator] Example: every hour |
| TP Scheduled communication time | Time zone and Day of the week when the Node is available for communication Example: Time: 13:00-20:00, Day: Monday |
| TP Stationary indication | Identifies whether the Node is stationary or mobile |
| TP Data size indication | indicates the expected data size for the pattern |
| TP Validity time | The time after which a TP becomes invalid once it had been set |

8.x4.4  Solution(s)

#### 8.x4.4.1 Solution18.x.4.1.1  Proposed resource types and attributes

This clause provides information of new resource types and new attributes including relationship with existing resource types and attributes.

Proposed new resource types are as below.

- Resource Type <trafficCharacteristics>

  - Note: It is child resource of existing Resource Type <AE> or <node>.

- Resource Type <trafficPattern>

  - Note: It is child resource of new Resource Type <trafficCharacteristics>.

Detailed information of new resource types are described in subclauses below.

8.x.4.1.1.1 Resource Type <trafficCharacteristics>

The <trafficCharacteristics> resource represents the characteristic information (e.g. communication pattern, mobility pattern, etc..) of a field domain node. This information may be detected or scheduled by application level processing. This resource type is used to share information with other entities such as the underlying network entity (server NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node.

Figure 8.x4.4.1.1-1: Structure of <trafficCharacteristics> resource

The <trafficCharacteristics> resource shall contain the child resources specified in table 8.x4.4.1.1-1.

Table 8.x4.4.1.1-1: Child resources of <trafficCharacteristics> resource

| Child Resources of <trafficCharacteristics> | Child Resource Type | Multiplicity | Description | <trafficCharacteristicsAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  | <subscription> |
| [variable] | <trafficPattern> | 0..n | See clause 8.x4.4.1.1.2. A source AE can create multiple number of <trafficPattern> resources for a single target AE of field domain node. In this case the source AE assures that different communication patterns are not overlapping at any point in time. | <trafficPatternAnnc> |

The <trafficCharacteristics> resource shall contain the attributes specified in table 8.x4.4.1.1-2.

Table 8.x4.4.1.1-2: Attributes of <trafficCharacteristics> resource

| Attributes of <deviceCharacteristics> | Multiplicity | RW/ RO/ WO | Description | <trafficCharacteristicsAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of TS-0001. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of TS-0001. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| creator | 1 | WO | The AE-ID of the entity which created the resource. | OA |

8.x.4.1.1.2 Resource Type <trafficPattern>

The <trafficPattern> resource represents the communication pattern and the mobility pattern of a field domain node to be shared with other entities such as the underlying network entity (NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node by using this information.

Figure 8.x4.4.1.1.2-1: Structure of <trafficPattern> resource

The <trafficPattern> resource shall contain the child resources specified in table 8.x4.4.1.1.2-1.

Table 8.x4.4.1.1.2-1: Child resources of <trafficPattern> resource

| Child Resources of <trafficPattern> | Child Resource Type | Multiplicity | Description | <trafficPatternAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  | <subscription> |
| [variable] | <schedule> | 0..1 | It provides the mask for the day of week, the starting time and end time for communication. If it is not provided this shall be interpreted as ‘anytime’ at the NSE. | <scheduleAnnc> |

The <trafficPattern> resource shall contain the attributes specified in table 8.x4.4.1.1.2-2.

Table 8.x4.4.1.1.2-2: Attributes of <trafficPattern> resource

| Attributes of <trafficPattern> | Multiplicity | RW/ RO/ WO | Description | <trafficPatternAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of TS-0001. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of TS-0001. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| provideToNSE | 0..1 | RW | It indicates as ‘TRUE’ or ‘FALSE’ whether the traffic pattern shall be provided to a NSE | OA |
| periodicIndicator | 0..1 | RW | It indicates as ‘Periodical’ or ‘On demand’. | OA |
| periodicDurationTime | 0..1 | RW | It provides the time in seconds of the duration of the periodic communication. | OA |
| periodicIntervalTime | 0..1 | RW | It provides the time in seconds of the interval for periodic communication. | OA |
| stationaryIndication | 0..1 | RW | It indicates as ‘Stationary (Stopping)’ or ‘Mobile (Moving)’. | OA |
| dataSizeIndicator | 0..1 | RW | It indicates the expected data size for the pattern | OA |
| validityTime | 0..1 | RW | It contains the point of time when the informed <trafficPattern> information to the NSE becoming invalid and shall be deleted at the NSE. | OA |

#### 8.x4.4.1.2  Proposed Flow

This clause describes the procedure for resource management of Traffic Patterns to a set of field nodes.Figure 8.x4.4.1.2-1 below depicts a general procedure for configuration of Traffic Patterns.

The procedure needs to be harmonized with the Figure 8.x4.2-1 of present document.

Figure 8.x4.4.1.2-1  General procedure for configuration of Traffic Patterns

Step-1: Provide information on the behavior of a field domain AE or field domain Node

An AE (IN-AE or an AE of the Field Domain Node that reports its communication behaviour) provides the hosting CSE (i.e. ASN/MN-CSE) of the field domain AE/Node with information on the communication behavior of the AE/Node (i.e. TP parameter sets)  by creating, updating or deleting its Traffic Patterns (TP).

The AE may provide TP parameter sets for a group of field domain nodes .

The request shall include

- the originator AE-ID of the requesting AE,

- a target identifier: i.e. the <trafficCharacteristics> child resource of a <node> resource or an <AE> resource of the field domain node or a group identifier of multiple field domain AEs/nodes for which the Traffic Patterns is provided, and

- a set of TP parameters  as indicated in table 8.x4.3-1.

The request may include multiple of TP parameter set(s) and validity time(s).

If the hosting CSE has received a request from an AE to create, update or delete Traffic Patterns it shall check if the request from the AE is valid (Note-1).

- Note-1: Apart from checking access rights of the AE the validation of the request from the AE could include:
 - Consistency with  <schedule> resources supported by an M2M SP in various M2M entities (MN-CSE, ASN)  hosting this AE/Node
 - If there are several TP parameter sets active for one Field Domain Node, then the original resource hosting CSE assures that the different TP parameter sets are not overlapping.

Step-2: Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

If the hosting CSE recognizes an announcement procedure is needed, it shall announce the Traffic Patterns received from the AE to the IN-CSE that has an interface to the NSE contained in the “AnnounceTo” attribute of the Traffic Patterns resources based on the existing announcement procedures.

Step-3: Select the server NSE to request for the configuration of the TP parameter sets

If the IN-CSE receives an announced Traffic Patterns and the IN-CSE recognizes the configuration of the Traffic Patterns  at the NSE is needed by checking “provideToNSE” attribute, the IN-CSE shall perform subsequent steps.

For the configuration of the TP parameter sets for a specific field domain node, the IN-CSE selects the NSE by using the identifier of the Field Domain Node (i.e. the M2M-Ext-ID) by which the Node can be identified in the NSE.

Note: The correct server NSE can be found by following of a chain of links of multiple resources in the IN-CSE, e.g. the nodeLink in the AEAnnc resource of a target AE of field domain node linking to the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE. (See clauses 7.1.8 and 7.1.9 in TS-0001[i.9])

Step-4: Request for the configuration of the TP parameter sets

For each field domain node received in the AE request the IN-CSE sends a request to provide TP parameter sets for the field domain node to the NSE, using the appropriate Mcn protocol. The request includes an identifier of the filed domain node and one or more TP parameter set(s) as defined at clause 8.x4.3.

Note: If the Underlying Network is 3GPP-compliant, see clause 8.x4.2 for more details.

Step-5: Response for the configuration of the TP parameter sets

The IN-CSE receives the response for the configuration of the TP parameter sets from the NSE. The response includes the result of the request.

Note: If the Underlying Network is 3GPP-compliant, see clause 8.x4.2 for more details.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 1	Scope

The present document is a study of interworking between oneM2M Architecture and 3GPP Rel-13 architecture for Service Capability Exposure as defined in the release 13 version of TS 23.682. The key objective and value is analyzed and described. The document also investigates the potential solution in oneM2M by evaluating the existing technical solutions.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 5.3	3GPP architecture for Service Capability Exposure

The 3GPP architecture for the Service Capability Exposure Function (SCEF) is defined in 3GPP TS 23.682 [i.5]. The specification includes two different architectures. One is for the “MTC Device triggering” feature and was specified in 3GPP release 11. The other one is for 3GPP Service exposure with 3rd party service providers features newly provided in Release 13 which is the focus of the present document. Refer to the following figure 5.3-1, taken from the release 13 version of 3GPP TS 23.682 [i.5].

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]	oneM2M TS-0002: " Requirements".

[i.3]	3GPP TS 22.101 Service aspects; Service principles (Release 13).

[i.4]	3GPP TS 22.115 Service aspects; Charging and billing (Release 13).

[i.5]	3GPP TS 23.682 Architecture enhancements to facilitate communications with packet data networks and applications (Release 13).

[i.6]	OMA API Inventory (http://technical.openmobilealliance.org/Technical/technical-information/oma-api-program)

[i.7]	OMA Service Exposure Framework (http://member.openmobilealliance.org/ftp/Public_documents/ARCH/ServiceExposure)

[i.8]	OMA Exposing Network Capabilities to M2M (http://member.openmobilealliance.org/ftp/Public_documents/ARCH/ENCap-M2M)

[i.9]	oneM2M TS-0001: " Functional Architecture ".

[i.10]	3GPP TS 29.336: Home Subscriber Server (HSS) diameter interfaces for interworking with packet data networks and applications (Release 13)

### -----------------------End of Changes to References  -------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Mca

Infrastructure Domain

Field Domain

1. provide information on the behavior of a field domain AE or field domain Node

2. Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

- Request for providing 
the TP parameter sets

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE

Any Domain