²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP22 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-02-23 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | LWM2M Provisioning is addressed |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0014 V0.9/0.10 |
| Clauses/Sub Clauses* | 6.x clauses and sub-clause + editorial (R03 /R04) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 -------------------------------------------------

## 6.1	Introduction

The LWM2M IPE participation in the LWM2M Protocol as described in clause 5 does so in the role of a LWM2M Server to which LWM2M Applications (LWM2M Clients) interact. As a LWM2M Server, the IPE provides the following Architecture Aspects based on the LWM2M Protocol Aspects described in Annex A.2:

- LWM2M Client Provisioning (Bootstrap)

- LWM2M Device and Endpoint Lifecycle (Client Registration)

- LWM2M Object Discovery (Client Registration, Device Management and Service Enablement)

- LWM2M Object Transport and Interworking (Device Management and Service Enablement)

- LWM2M Object Subscription and Notification (Information Reporting)

- LWM2M Object Security

- LWM2M Interworking Proxy Entity Administration

### -----------------------End of change 1 --------------------------------------------------

## 6.2	LWM2M Client Provisioning (Bootstrap)

This present document makes assumptions that the LWM2M Clients and LWM2M Servers functionality of the IPE have been provisioned with the proper LWM2M credential materials in accordance to the LWM2M specification (A.5.3.1. Bootstrap) in order to securely communicate between the LWM2M Client and LWM2M Server.

## Additionaly, a LWM2M Client connected to a LWM2M IPE, should be provisioned with the LWM2M Access Control Policy information associated to the Object Instances contained in the LWM2M Client as described in clause 6.7 LWM2M Object Security. Additionally, in current release of this present document, the LWM2M Server role of the LWM2M IPE does not contain the LWM2M Bootstrap Server capability, consequently the LWM2M Client provisioning operations shall be part of an out-of-band process.

## 6.3	LWM2M Device and Endpoint Lifecycle

### ---------------------- Start of change 2 --------------------------------------------------

## 6.7	LWM2M Object Security

### 6.7.1	Introduction

OMA-LWM2M and oneM2M Access Control Policies shall collaborate in order to assure the interworked resources are accessible according to the oneM2M Authorisation Procedure specified in clause 11.3.4 (M2M Authorization Procedure) of oneM2M TS-0001 [2] and clause 7 (Authorization) of oneM2M TS-0003 [5].

### 6.7.2. 	LWM2M Interworking Access Control Policy

The oneM2M Access Control Policy mechanisms specified in clause 7 of oneM2M TS-0003 [5], shall be used to check and validate the parameters of a request message against the ACPs (<accessControlPolicy> resources) which have been assigned to the accessed resource.

In order to assure a proper LWM2M Interworking with oneM2M, the IPE shall setup the hosting CSE by:

- providing a mandatory set of <accessControlPolicy> (ACPs) resources

- assigning a proper set of ACPs to the accessControlPolicyIDs attribute of each <container> resource allocated during the CSE registration phase (clause 6.3 LWM2M Object Discovery)

The process for provisioning the IPE in order to perform such a setup is described in clause 6.7.3  “IPE and Object Security provisioning” of the present document.

In addition, the Access Control Policy mechanisms specified in clause 7 of oneM2M TS-0003 [5] are fully applicable in this LWM2M interworking context.

### 6.7.3.  IPE and Object Security provisioning

### In order to provide oneM2M information specified in the clause 6.7.2 (set of <accessControlPolicy> (ACPs) resources, assignement of accessControlPolicyIDs), the LWM2M IPE shall be supplied by information such as:

### a list of oneM2M originators and their associated Access Control Rules  likely to be exercised on the Hosting CSE resources

### a list of oneM2M originators likely to contact the LWM2M Clients with the associated set of authorized operations

### In combining such an information with the Access Control Policy specified in a given LWM2M Client (clause  6.2 LWM2M Client Provisioning) the LWM2M IPE shall be able  to provide to the Hosting CSE, the oneM2M Access Control Policy materials  needed for properly registering LWM2M Objects representation. In the current release of this Specification, this procedure of how the Access Control Policy materials are provided is implementation specific.

-----------------------End of change 2 --------------------------------------------------