| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | ZTE |
| Date:* | 2016-03-04 |
| Contact:* | Wu Hao, ZTE, wu.hao18@zte.com.cn Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Reason for Change/s:* | Add description for section 8 |
| CR against: Release* | Rel-0.2 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.2.0 |
| Clauses/Sub Clauses* | 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add description for section 8.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.x1	Support for Group Message Delivery procedure

Figure 8.3.x1-1 shows a generic procedure to support group message delivery between oneM2M and 3GPP network.

Figure 8.3.x1-1: General group message delivery procedure between oneM2M and 3GPP network

Step-1: Group Message Request

The AE sends the Group Message Request message to the IN-CSE with start time.

Step-2: Authorization

The IN-CSE checks that the AE is authorised to send a group message request with NSE, which is specified in 3GPP TS 23.682[i.14].

Step-3: Allocate TMGI Request

If no TMGI is allocated before, the IN-CSE shall send an Allocate TMGI Request message to request the NSE to allocate one or more TMGIs, which is specified in 3GPP TS 23.682[i.14].

Step-4: Allocate TMGI Response.

If Step-3 is performed, the NSE shall send an Allocate TMGI Response message to the IN-CSE indicating the list of allocated TMGIs, and an expiration time for those TMGIs, which is specified in 3GPP TS 23.682.

Step-5: Activate MBMS Bearer Request.

The IN-CSE sends an Activate MBMS Bearer Request message to the NSE, which is specified in 3GPP TS 23.682[i.14].

Step-6: Activate MBMS Bearer Request.

The NSE sends an Activate MBMS Bearer Response to the IN-CSE.

Step-7: Activate MBMS Bearer Request.

The IN-CSE sends a Group Message Confirm message to the AE to indicate whether the Request has been accepted for delivery to the group.

Step-8: Application level interaction.

Application level interactions may be applied for the devices of specific group to retrieve the related MBMS service information, e.g. TMGI, start time.

Step-9: Group message delivery.

At or after the requested start time, but before the expiration time, the AE transfers the content to be delivered to the group via the IN-CSE by using MBMS provided by 3GPP network. In response to the received content, the ASN/MN-CSE may immediate or later communication with the AE.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?