| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | ZTE |
| Date:* | 2016-03-04 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn Wu Hao, ZTE, wu.hao18@zte.com.cn Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Reason for Change/s:* | Add description for section 8 |
| CR against: Release* | Rel-0.2 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.2.0 |
| Clauses/Sub Clauses* | 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add description for section 8.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.x4	Support for Network Issue Report

Figure 8.3.x4-1 shows a generic procedure to network issue report service between oneM2M and 3GPP network.

Figure 8.3.x4-1: General procedure to support network issue report between oneM2M and 3GPP network

Step-1: Network Status Request

When the AE needs to retrieve NSI (Network Status Indication), the AE sends a Network Status Request (Geographical area, Duration, Threshold) message to the IN-CSE. Duration indicates the time for which a continuous reporting is requested. The absence of Duration indicates a one-time reporting. Threshold indicates a range at which the AE wishes to be informed of the network status. Multiple Threshold values may be included.

Step-2: Authorization

The IN-CSE authorizes the AE request.

Step-3: Aggregated Congestion Request

The IN-CSE sends an Aggregated Congestion Request (Location Area, Duration, Threshold) message to the NSE. Duration indicates the time for which a continuous reporting is requested. The absence of Duration indicates a one-time reporting. The IN-CSE, based on operator policies, may chose a different Threshold value than the one indicated by the AE in step 1.

Step-4: Aggregated Congestion Report.

The NSE sends an Aggregated Congestion Report to the IN-CSE including depending on the operator configuration and current RCAF knowledge, the congestion status for every cell or eNodeB belonging to the Location Area requested by the IN-CSE.

Step-5: Derive NSI.

The IN-CSE derives the NSI (Network Status Indication) for the requested Geographical Area by combining the received reports.

Step-6: Network Status Report.

The IN-CSE sends a Network Status Report message including NSI to the AE.

Step-7a: Detect end of duration.

The IN-CSE detects that the requested Duration for an ongoing continuous reporting of network status is over.

Step-7b: Cancel Network Status Request.

When the AE needs to terminate an ongoing continuous reporting of network status, the AE sends a Cancel Network Status Request message to the IN-CSE.

Step-8b: Authorization

The IN-CSE authorizes the AE request.

Step-9b: Cancel Network Status Response.

If the AE requested to terminate an ongoing continuous reporting of network status in step 7b, the IN-CSE sends a Cancel Network Status Response message to the AE.

Step-10: Cancel Aggregated Congestion Request.

The IN-CSE sends a Cancel Aggregated Congestion Request message to the NSE.

Step-11: Cancel Aggregated Congestion Response.

The NSE removes the related instructions and stops monitoring the set of cells or eNodeBs belonging to the Location Area for a change in the congestion status. Afterwards, a Cancel Aggregated Congestion Response is sent to the IN-CSE.

Step-12: Remove State.

The IN-CSE removes all state information related to this continuous reporting.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?