| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | ZTE |
| Date:* | 2016-03-04 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn Wu Hao, ZTE, wu.hao18@zte.com.cn Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Reason for Change/s:* | Add description for section 8 |
| CR against: Release* | Rel-0.2 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.2.0 |
| Clauses/Sub Clauses* | 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add description for section 8.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.x5	Support for resource management of background data transfer

Figure 8.3.x5-1 shows a generic procedure to resource management of background data transfer between oneM2M and 3GPP network.

Figure 8.3.x5-1: General procedure to support resource management of background data transfer between oneM2M and 3GPP network

Step-1: Background data transfer Request.

The AE sends a Background data transfer request (Volume per UE, Number of UEs, Desired time window) message to the IN-CSE. The Volume per UE describes the volume of data the AE expects to be transferred per device. Number of UEs describes the expected amount of devices participating in the data transfer. Desired time window describes the time interval during which the AE wants to realize the data transfer. Optionally, the AE can provide a geographic area information.

Step-2: Authorization.

The IN-CSE authorizes the AE request.

Step-3: PCC procedure.

The IN-CSE selects any of the available PCRFs and triggers the Negotiation for future background data transfer procedure with the NSE. The IN-CSE forwards the parameters provided by the AE. The NSE responds to the IN-CSE with the possible transfer policies and a reference ID, which is specified in TS 23.682.

Step-4: Background data transfer Response.

The IN-CSE forwards the transfer policies to the AE by sending a Background data transfer response (Possible transfer policies) message.

Step-5: Background data transfer Request.

If more than one transfer policy was received, the AE shall select one of them and send another Background data transfer request (Selected transfer policy) message to inform the IN-CSE about the selected transfer policy.

Step-6: Background data transfer Response.

The IN-CSE confirms the transfer policy selection to the AE by sending a Background data transfer response message.

Step-7: PCC procedure.

The IN-CSE continues the Negotiation for future background data transfer procedure with the NSE, which is specified in TS 23.682.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?