| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | ZTE |
| Date:* | 2016-03-04 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn Wu Hao, ZTE, wu.hao18@zte.com.cn Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Reason for Change/s:* | Add description for section 8 |
| CR against: Release* | Rel-0.2 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.2.0 |
| Clauses/Sub Clauses* | 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add description for section 8.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.x6	Support for change the chargeable party at session set-up or during the session procedure

8.3.x6.1	Support for change the chargeable party at session set-up

Figure 8.3.X6.1-1 shows a generic procedure to change the chargeable party at session set-up between oneM2M and 3GPP network.

Figure 8.3.x6.1-1: General procedure to support change the chargeable party at session set-up between oneM2M and 3GPP network

Step-1: Set chargeable party Request.

When setting up the connection, the AE may request to become the chargeable party for the session to be set up by sending a Set chargeable party request message (Description of the application flows, sponsor information, Sponsoring Status) to the IN-CSE, including optionally a usage threshold. The Sponsoring Status indicates whether sponsoring is started or stopped, i.e. whether the 3rd party service provider is the chargeable party or not.

Step-2: Authorization.

The IN-CSE authorizes the AE request to sponsor the application traffic and stores the sponsor information.

Step-3: PCRF initiated IP-CAN session modification.

The IN-CSE interacts with the NSE by triggering a PCRF initiated IP-CAN Session Modification as described in TS 23.682 and provides IP filter information, sponsored data connectivity information, and Sponsoring Status (if received from the AE) to the NSE.

Step-4: Set chargeable party Response.

The IN-CSE sends a Set chargeable party response (Result) message to the AE. Result indicates whether the request is granted or not.

8.3.x6.2	Support for change the chargeable party during the session

Figure 8.3.x6.2-1 shows a generic procedure to change the chargeable party during the session between oneM2M and 3GPP network.

Figure 8.3.x6.2-1: General procedure to support change the chargeable party during session between oneM2M and 3GPP network

Step-1: Change chargeable party Request.

For the ongoing AS session, the AE may send a Change chargeable party request message (Reference ID, Sponsoring Status) to the IN-CSE, including optionally a usage threshold. The Sponsoring Status indicates whether sponsoring is enabled or disabled, i.e. whether the 3rd party service provider is the chargeable party or not.

Step-2: Authorization.

The IN-CSE authorizes the AE request of changing the chargeable party.

Step-3: PCRF initiated IP-CAN session modification.

The IN-CSE interacts with the NSE by triggering a PCRF initiated IP-CAN Session Modification as described in TS 23.682 and provides IP filter information, sponsored data connectivity information, and Sponsoring Status (if received from the AE) to the NSE.

Step-4: Change chargeable party Response.

The IN-CSE sends a Change chargeable party response (Reference ID, Result) message to the AE. Result indicates whether the request is granted or not.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?