| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu |
| Date:* | 2016-03-14 |
| Contact:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu |
| Reason for Change/s:* | Generic Interworking will make use of two specializations of the <flexContainer> resource type. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0025 – Generic Interworking MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.6.0 |
| Clauses/Sub Clauses* | 9.6.1.2.2, 9.6.35 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

<Provide an introduction containing the problem(s) being solved, and a summary list of proposals.  Discuss any risk of breaking backwards compatibility with last published version of the impacted TS.>

### -----------------------Start of change 1-------------------------------------------

##### 9.6.1.2.2	Specializations of <flexContainer>

Editor’s note: Standardized specializations of <flexContainer> resources shall be listed in this section, e.g. those required for standardized interworking procedures.

9.6.1.2.2.x	Specializations of <flexContainer> for Generic Interworking

Generic Interworking (specified in TS-0012 [6]) provides interworking with many types of non- oneM2M Area Networks and their devices. It supports the interworking variant “ full mapping of the semantic of the non-oneM2M data model to Mca” as indicated in Annex F.2. 
For Generic Interworking the non-oneM2M data model of the non- oneM2M Area Network needs to be described in the form of a oneM2M compliant ontology which is derived from the oneM2M Base Ontology (specified in TS-0012 [6]) and that may be available in a formal description language (e.g. OWL).

Note 1: While in general the semantic information contained in the ontology can be made available (in semanticDescriptor child-resources of the utilized resources) the mechanisms used for Generic Interworking as described in [6] for data exchange with an AE do not rely on the existence of semanticDescriptors. This allows e.g. very simple devices to exchange their data in “raw” form (e.g. as byte-fields that need to be interpreted by the communicating entity as integer numbers or text strings).

Note 2: Generic Interworking is aiming at a maximum of flexibility regarding the types of interworked Area Networks / Devices (e.g. RESTful or RPC based) while at the same time requiring a minimum of specialized resource types. Generic Interworking can make use of <container> / <contentInstance> resource types and/or <flexContainer> resource types for communication with the Generic Interworking IPE.

Table 9.6.1.2.2.x-1 lists specializations of the <flexContainer> resource type for Generic Interworking in which the containerDefinition attribute provides further definition of the resource.

Table 9.6.1.2.2.x-1 <flexContainer> Specializations for Generic Interworking

| Resource specialization | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| genericInterworkingService | This resource type is used to link to a set of Input- and OutputDatapoints and OperationInstances which are oneM2M resources, modelling communication channels to/from a Service of the interworked Device | genericInterworkingService, genericInterworkingOperationInstance, semanticDescriptor, subscription | AE, container, flexContainer, genericInterworkingService, | 9 in [6] |
| genericInterworkingOperationInstance | AllJoyn service framework wrapper | semanticDescriptor, subscription | genericInterworkingService, | 9 in [6] |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.35 	Resource Type flexContainer

The <flexContainer> resource type is a customizable container for data instances. It is a template for the definition of flexible specializations of data containers. Like a <container> resource, specializations of this <flexContainer> resource type are used to share information with other entities and potentially to track the data. While the <container> resources includes data to be made accessible to oneM2M entities inside <contentInstance> children, a specialization of the <flexContainer> resource includes associated content directly inside the <flexContainer> by means of one or more [customAttribute] attribute(s).  The attribute name and attribute data type of [customAttribute] attributes are defined explicitly for each specialization of <flexContainer>, i.e. the specific set of attribute name and type are defined in a corresponding XSD-file.

Example usage of <flexContainer>: As a specialization of <flexContainer> that includes two [customAttribute] attributes, named "temperature"(xs:float type) and "humidity"(xs:positiveInteger type) can be specified in some TS. The actual data types of [customAttribute] will be described both in the specification document or XSD file which are referred by the value of containerDefinition attribute.

Figure 9.6.35-1: Structure of <flexContainer> resource

The <flexContainer> resource shall contain the child resource specified in table 9.6.35-1.

Table 9.6.35-1: Child resources of <flexContainer> resource

| Child Resources of <flexContainer> | Child Resource Type | Multiplicity | Description | <flexContainerAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <flexContainer> | 0..n | <flexContainer> resource can include any of its specializations as child resource | <flexContainer> <flexContainerAnnc> |

The <flexContainer> resource shall contain the attributes specified in table 9.6.35-2.

Table 9.6.35-2: Attributes of <flexContainer> resource

| Attributes of <flexContainer> | Multiplicity | RW/ RO/ WO | Description | <flexContainerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 | NA |
| parentID | 1 | RO | See clause 9.6.1.3 | NA |
| expirationTime | 0..1 (NOTE1) | RW | See clause 9.6.1.3 | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 | MA |
| creationTime | 0..1 (NOTE 1) | RO | See clause 9.6.1.3 | NA |
| lastModifiedTime | 0..1 (NOTE 1) | RO | See clause 9.6.1.3 | NA |
| stateTag | 1 | RO | See clause 9.6.1.3 | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 | NA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| containerDefinition | 1 | WO | This contains a reference (URN) to the definition which shall be used by the CSE to statically validate the syntax of the <flexContainer> resource (see NOTE 2). This URN shall refer to one of the following: AllJoyn Interworking Generic Interworking A list of possible URNs is provided in 9.6.1.2.2 Other URN may be specified. | MA |
| creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. | NA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the present <flexContainer> resource | OA |
| [customAttribute] | 0..n | RW | Specialization-specific attribute(s). Name and data type defined in each specialization of <flexContainer> resource. | OA |
| NOTE 1: When an instance of <flexContainer> is a child of a <flexContainer> resource, these attributes can be optional. Their presence is determined by the respective definition referred to by the containerDefinition attribute NOTE 2: The reference is a URN and not URL: the CSE does not retrieve the definition of the <flexContainer> dynamically. |

### -----------------------End of change 2---------------------------------------------