| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | LG Electronics |
| Date:* | 2016-03-07 |
| Contact:* | SeungMyeong JEONG, seungmyeong.jeong@lge.com |
| Reason for Change/s:* |  |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0018 oneM2M and AllJoyn Interworking MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0021 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clause 7 interworking procedures describes:

- how does the IPE initially creates resources for oneM2M-AllJoyn interworking

- how does the IPE interact with other oneM2M enities for consuming/injecting services from/to AllJoyn services

### -----------------------Start of change 1-------------------------------------------

# 7	Interworking Procedures

## 7.1	Introduction

The interworking procedures describes the fololowing:

- how does the IPE initially create necessary resources for oneM2M-AllJoyn interworking (clause 7.2)

- how does the IPE perform interworking between oneM2M system and AllJoyn networks depending on the service exposure direction(clause 7.3)

## 7.2	IPE initial setup

IPE initial setup consists of resource creation procedures. An <AE> resource, AllJoyn service resources and <subscription> resources are created by the IPE.

For the interworking, firstly the IPE shall perform IPE registration (see clause 6.3).

If the IPE is set to advertisement-based or pre-configured discovery mode (see clasue 6.4), the AE in the IPE shall expose/create corresponding resources(see clause 6.2) once the AllJoyn Application in the IPE completes AllJoyn service discovery and session establishement with AllJon Producer Applications referring its AllJoyn service objects.

If the IPE is set to on-demand discovery mode (see clasue 6.4), the IPE shall perform the same procedure above (i.e. advertisement-based or pre-configured discovery mode) when it receives a Notify request for on-demand discovery (see clause 10.2.6.2 [1]) by its Registrar CSE.

The following AllJoyn service resources shall only be created by the AllJoyn IPE:

Table 7.2-1: Resources created by IPE only

| Service Resource | Resource Type | Attributes |
| --- | --- | --- |
| service objects, service frameworks | flexContainer | containerDefinition = wrapper |
| interface | flexContainer | containerDefinition = allJoynInterface |
| method | flexContainer | containerDefinition = allJoynMethod |
| property | flexContainer | containerDefinition = allJoynProperty |
| signal | container | labels = allJoynSignal |

However, [allJoynMethodCall] resources can be created by other oneM2M entities.

After the creation of AllJoyn service resources, the IPE should create <subscription> resources to monitor AllJoyn service method call, property change, signal generation by other oneM2M entities manipulating the service resources. Signal generation subscription shall be created only if the signal <container> resource is the great-grand child resource of [allJoynApp] resource with direction attribute set to “oneM2mToAllJoyn”.

When the IPE creates <subscription> resources, targeted subscribed-to resources and their children <subscription> resources shall have the following attributes:

Table 7.2-2: Subscription for method call

| Subscribed-to resource | <subscription> resource |
| --- | --- |
| resourceType | containerDefinition | eventType of eventNotificationCriteria |
| <flexContainer> | [allJoynMethod] | Creation of a direct child of the subscribed-to resource |

Table 7.2-3: Subscription for property change

| Subscribed-to resource | <subscription> resource |
| --- | --- |
| resourceType | containerDefinition | eventType of eventNotificationCriteria |
| <flexContainer> | [allJoynProperty] | Creation of a direct child of the subscribed-to resource |

Table 7.2-4: Subscription for signal generation

| Subscribed-to resource | <subscription> resource |
| --- | --- |
| resourceType | labels | eventType of eventNotificationCriteria |
| <container> | AllJoyn:Signal | Creation of a direct child of the subscribed-to resource |

## 7.3	IPE interworking

When the AllJoyn service resources are created by the IPE, the other oneM2M entities can manipulates those resources.

Since an AllJoyn service is produced/consumed by an AllJoyn interface member access (i.e., method, property, signal), the IPE delivers method call, property change and signal generation from/to oneM2M and AllJoyn systems.

For an AllJoyn service that is consumed by oneM2M entities(i.e., direction attribute of [allJoynApp] resource is “allJoynToOneM2m”), the IPE performs the following:

- When an [allJoynMethodCall] resource is created, the IPE shall interpret the resource into the AllJoyn method call message and send the message to the corresponding AllJoyn Producer Application. The IPE should update callStatus and output attribute of the [allJoynMethodCall] resource, if applicable.

- When the requestedValue attribute of a [allJoynProperty] resource is updated, the IPE shall interpret the property value into the AllJoyn property set message and send the message to the corresponding AllJoyn Producer Application. The IPE should update requestedValue attribute of the [allJoynProperty] resource, if applicable.

- When the IPE receives an AllJoyn signal message, the IPE shall interpret the message into the corresponding <contentInstance> resource and create it as a child of the signal <container> resource.

For an AllJoyn service that is consumed by AllJoyn Consumer Applications on AllJoyn devices(i.e., direction attribute of [allJoynApp] resource is “oneM2mToAllJoyn”), the IPE shall perform the following:

- When the AllJoyn Producer Application on the IPE receives AllJoyn method call message, it shall interpret the message into an [allJoynMethodCall] resource and create it as the child resource of the corresponding [allJoynMethod] resource.

- When the AllJoyn Producer Application on the IPE receives AllJoyn property set message, it shall interpret the message into the requestedValue attribute of the [allJoynProperty] resource and update it.

- When a new <contentInstance> resource as a child of a signal <container> resource, the IPE shall interpret the resource into the AllJoyn signal message and send the message to the corresponding AllJoyn Consumer Application(s).

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?