| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | InterDigital |
| Date:* | 2016-3-2 |
| Contact:* | Dale Seed, InterDigital - Dale.Seed@InterDigital.com Chitra Vaidyanathan, InterDigital - Chitra.Vaidyanathan@InterDigital.com |
| Reason for Change/s:* | Add optional values and operators to eventNotificationCriteria |
| CR against: Release* | Rel2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS001 Functional Architecture Specification V2.6.0 |
| Clauses/Sub Clauses* | Section 9.6.8 Table 9.6.8-3: eventNotificationCriteria Conditions |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

TS001 v2.6.0, section 9.6.8 describes the <subscription> resource and its attributes. One of the attributes of <subscription> is eventNotificationCriteria which contains conditions that indicate when a notification shall be generated.

One of the defined “conditions” of eventNOtificationCriteria is attribute. The current definition of this condition requires that on any update to any of the attributes specified in the attribute list, a notification shall be generated.

This contribution proposes a new attributeValueConditions eventNOtificationCriteria.  This new attribute is defined as a list of conditions based on the value of one or more attributes of a subscribed-to-resource.  The conditions in this list are used to qualify the generation of a notification when one or more attributes of a subscribed-to-resource are updated.

The above changes will enable more flexible and powerful subscription / notification functionality.   This is useful for subscriptions to resource types such as <flexContainer>, <mgmtObj>, <container>, etc.  The following is a <flexContainer> example, showing the benefits of this proposed enhancement.

For example, a <flexContainer> is defined for a smart parking garage.  The garage keeps track of the number of available spaces via a <flexContainer> resource having a custom attribute named availSpaces.  A subscription is created to the <flexContainer> resource to generate a notification when the number of available space is less than a value 50.  This is accomplished by configuring the eventNOtificationCriteria of the subscription with an eventType condition of ‘A - Update to attributes of the subscribed-to resource’ and configuring the attributeValueConditions condition elements name to ‘availSpaces’, operation to ‘LT’ and value to ‘50’.   Thereafter, as updates are made to the <flexContainer> the CSE monitors the value of the availSpaces custom attribute to detect if the value drops below 50.  If/when this occurs, the CSE generates a notification.

## ----------------------- Start of change 1 -----------------------

Table 9.6.8-3 describes the eventNotificationCriteria conditions.

Table 9.6.8-3: eventNotificationCriteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| stateTagSmaller | 0..1 | The stateTag attribute of the resource is smaller than the specified value. |
| stateTagBigger | 0..1 | The stateTag attribute of the resource is bigger than the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| sizeAbove | 0..1 | The contentSize attribute of the <contentInstance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <contentInstance> resource is smaller than the specified value. |
| eventType | 0..n | The type of event. Possible event type values are: Update to attributes of the subscribed-to resource Deletion of the subscribed-to resource , Creation of a direct child of the subscribed-to resource , Deletion of a direct child of the subscribed-to resource The other conditions in eventNotificationCriteria conditions apply to the selected eventType. For example, if eventType is "Creation of a direct child of the subscribed-to resource" then other eventNotificationCriteria conditions is applied to the direct child resources of the subscribed-to resource. If this condition is not specified, the default value is "Update to attributes of the subscribed-to resource" |
| operationMonitor | 0..n | The operations accessing the subscribed-to resource matches with the specified value. It allows monitoring which operation is attempted to the subscribed-to resource regardless of whether the operation is performed. This feature is useful when to find malicious AEs. Possible string arguments are: create, retrieve, update, delete. |
| attribute | 0..n | A list of attributes names of a subscribed-to-resource. This list is only applicable when eventType has a value of “Update to attributes of the subscribed-to resource”. If this list is present, then it is used to specify a subset of a subscribed-to-resource’s attributes for which updates shall result in a notification pending any applicable attributeValueConditions if present. If ANY attribute specified on this list is updated, then a notification shall be generated pending any applicable attributeValueConditions if present. If an attribute that is not specified in this list is updated, then a notification shall not be generated. If this list is not presented, then the default attribute list is the full set of a subscribed-to-resource’s attributes. If ANY attribute of a subscribed-to-resouce is updated, then a notification shall be generated pending any applicable attributeValueConditions if present. |
| attributeValueConditions | 0..n | A list of conditions based on the value of one or more attributes of a subscribed-to-resource. The value-based conditions in this list shall be used to qualify the generation of a notification when one or more attributes of a subscribed-to-resource are updated. The conditions shall be based on the syntax defined in Annex L. This list is only applicable when eventType has a value of “Update to attributes of the subscribed-to resource”. This list may be used independently or in conjunction with the attribute eventNotificationCrtieria. If used in conjunction, then only updates to attributes present in the attribute eventNotificationCrtieria shall be applicable for triggering the evaluation of this list. If this list is present, an update to an applicable attribute of a subscribed-to-resouce shall trigger the evaluation of this list to determine if any of the specified conditions are pertaining to at least one of the updated attributes. If so, and the applicable conditions in the list evaluate to TRUE then a notification shall be generated. The following is an example. batteryStatus EQ NORMAL AND batteryLevel GE 50 If either the value of the batteryStatus or batteryLevel attributes is updated, and following the update the value of batteryStatus equals “NORMAL” and the value of batteryLevel is greater than or equal to a value of 50, than a notification shall be generated. |

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

# Annex L (Normative):
Syntax for attributeValueConditions

## L.1	Introduction

The present Annex specifies the syntax for attributeValueConditions condition tag of the eventNotificationCriteria attribute of a <subscription> resource (see clause 9.6.8).

## L.2	attributeValueConditions syntax

For each attribute of a subscribed-to-resource that is included in an attributeValueConditions list, the name of the attribute, a comparison operator and a comparison value shall be specified.   If more than one attribute is included in the list than combination operator (i.e. AND or OR) shall also be specified for each additional attribute.   The combination operator shall be used to determine whether to AND or OR the results of an individual attribute condition with the results of any prior and applicable attribute conditions preceding it in the list.  The combined results shall determine whether or not an update shall result in a notification or not.

The following is a list of supported attributeValueConditions comparison operators and applicable types of comparison values.

Table L.2-1: attributeValueConditions comparison operators and value types

| Comparison Operators | Applicable Comparison Value Types | Usage |
| --- | --- | --- |
| EQ (Equals) | String or number | Used to determine if attribute equals a specified value |
| NE (Not Equals) | String or number | Used to determine if attribute does not equal a specified value |
| GT (Greater Than) | Number only | Used to determine if attribute is greater than a specified value |
| LT (Less Than) | Number only | Used to determine if attribute is less than a specified value |
| GE (Greater or Equals) | Number only | Used to determine if attribute is greater than or equal to a specified value |
| LE (Less or Equals) | Number only | Used to determine if attribute is less than or equal to a specified value |
| MATCH | String only | Used to determine if attribute contains a given value |

The supported types of combination operators include.

Table L.2-2: attributeValueConditions combination operators

| Combination Operator | Condition | Applicability |
| --- | --- | --- |
| AND | Concatenation of query which evaluated as AND combination logic. | Query-string |
| OR | Concatenation of query-string which evaluated as OR combination logic. | Query-string |

The following are somes examples of attributeValueConditions lists.

Table L.2-3: attributeValueConditions examples

| Combination Operator | Description |
| --- | --- |
| batteryLevel LT 10 | Generate an notification if the batteryLevel value is updated to a value that is less than 10. |
| batteryStatus EQ NORMAL AND batteryLevel GE 50 | Generate a notification when either batteryStatus or batteryLevel is updated, and the value of batteryStatus is equal to NORMAL and the value of batteryLevel is greater than or equal to a 50. |

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?