| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | InterDigital |
| Date:* | 2016-03-04 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com ) |
| Reason for Change/s:* | Introducing functionality for re-targeting RETRIEVE requests to AEs by enhancing the <container> resource. |
| CR against: Release* | Release-3 |
| CR against: WI* | Active WI-0025 (Generic Interworking) MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V2.6.0 |
| Clauses/Sub Clauses* | 9.6.6, 9.6.27, 9.6.2.3, 10.2.22.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Background:

At TP21, an initial version of this contribution was presented.  Overall, the idea was well received and it was requested to consider adding the capability to allow a CSE to selectively re-target RETRIEVE requests to an AE (e.g. based on the freshness of <contentInstance> resources in a <container> and the required freshness specified by the originator of a request).  This contribution provides the added capability for this.

Motivation:

Today many existing technologies such as OIC, LWM2M, ZigBee Smart Energy 2.0, etc. are RESTful in nature and are based on the premise that the device applications themselves host their own local resources which can be directly targeted by CRUD requests.

oneM2M Release 1 however requires AEs to mirror any resources they locally host into CSE hosted resources (e.g. <container> resources).   Once mirrored, AEs must use communication models such as subscription / notification or polling to synchronize the mirrored resources hosted on the CSE with their locally hosted AE resources. This mirroring and synchronization can introduce extra complexity and overhead on AEs (especially those hosted on resource constrained IoT/M2M devices) which is a concern and limitation in the eyes of potential application developers evaluating whether or not to adopt and use oneM2M for their next deployments.  Similar comments also apply to IPEs as well.

Proposal:

Provide an alternative to mirroring of AE hosted resources by introducing the capability to allow a CSE to re-target RETRIEVE requests directly to resources hosted by AEs.  Rather than unconditionally re-targeting RETRIEVE requests to an AE, enable a CSE to selectively re-target certain RETRIEVE requests.  For example, re-target a <contentInstance> retrieve request to an AE for a specified <container> if / when a hosting CSE does not have a <contentInstance> available or does not have one that is fresh enough (i.e. creationTime is newer than a specified time or expirationTime is earlier than a specified time).

Solution:

Introduce RETRIEVE re-targeting functionality to existing oneM2M <container> resources.

Example:

An AE is hosted on a device implementing a temperature sensor resource.  The complete URI to this temperature sensor resource is:

coap:\\172.25.0.50:6000\sensors\temperature

To interface this temperature sensor to a oneM2M CSE, a small temperature sensor AE is built that supports the following functionality:

- The temperature sensor AE registers the temperature sensor to the CSE by creating an <AE> resource and configures it’s pointOfAccess attribute with the value coap:\\172.25.0.50:6000

- The temperature sensor AE creates a <container> resource as a child of the <AE> and configures the retargetPointOfContact with a value of sensors\temperature

- A RETRIEVE request to the coap:\\172.25.0.50:6000\sensors\temperature URI will result in the temperature sensor AE returning a temperature sensor reading formatted as a <contentInstance> resource representation having the current temperature value of the sensor (e.g. 78 F) embedded within the content attribute of <contentInstance> representation along with any other applicable metadata such as a contentInfo attribute.

Sometime later, a temperature monitor AE attempts to retrieve a temperature sensor reading. The temperature monitor AE performs a RETRIEVE to the <container> resource’s <latest> virtual child resource.   In this request, the temperature monitor AE also includes a createdAfter filterCriteria request parameter.  This parameter specifies a required freshness (i.e. <contentInstance> must have been created no earlier than a specified time and date).  The Hosting CSE detects that a <contentInstance> is available in the targeted <container> however it is older than the time and date specified in the createdAfter filterCriteria request parameter.  As a result, the Hosting CSE then re-targets the RETRIEVE request to the temperature sensor AE by forming a RETRIEVE to the temperature sensor URI.

RETRIEVE coap:\\172.25.0.50:6000\sensors\temperature

The Hosting CSE in turn, blocks the original request waiting for a response for the re-targeted request.  The temperature sensor AE receives the request, processes it, and returns a temperature reading (e.g. 80 F) to the CSE.  The response contains content embedded within a resource representation formatted as a oneM2M <contentInstance>.  Upon receiving the response to the retargeted request, the Hosting CSE returns the response to the temperature monitor AE that originated the request in the form of a <contentInstance> RETRIEVE response.  The Hosting CSE also also creates a corresponding <contentInstance> child resource in the targeted <container>.

A corresponding call flow for this example is shown below.

### -----------------------Start of change 1-------------------------------------------

### 9.6.6	Resource Type container

The <container> resource represents a container for data instances. It is used to share information with other entities and potentially to track the data. A <container> resource has no associated content. It has only attributes and child resources.

Figure 9.6.6-1: Structure of <container> resource

The <container> resource shall contain the child resources specified in table 9.6.6-1.

Table 9.6.6-1: Child resources of <container> resource

| Child Resources of <container> | Child Resource Type | Multiplicity | Description | <containerAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| semanticDescriptor | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <contentInstance> | 0..n | See clause 9.6.7 | <contentInstance>, <contentInstanceAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| latest | <latest> | 1 | See clause 9.6.27 | None |
| oldest | <oldest> | 1 | See clause 9.6.28 | None |

The <container> resource shall contain the attributes specified in table 9.6.6-2.

Table 9.6.6-2: Attribute of <container> resource

| Attributes of <container> | Multiplicity | RW/ RO/ WO | Description | <containerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 . | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 . | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 . | NA |
| parentID | 1 | RO | See clause 9.6.1.3 . | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 . | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 . If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1 . | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 . | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 . | NA |
| stateTag | 1 | RO | See clause 9.6.1.3 . | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 . | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 . | NA |
| creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. | NA |
| maxNrOfInstances | 0..1 | RW | Maximum number of direct child <contentInstance> resources in the <container> resource. | OA |
| maxByteSize | 0..1 | RW | Maximum size in bytes of data(i.e., content attribute of a <contentInstance> resource) that is allocated for the <container> resource for all direct child <contentInstance> resources in the <container> resource. | OA |
| maxInstanceAge | 0..1 | RW | Maximum age of a direct child <contentInstance> resource in the <container> resource. The value is expressed in seconds. | OA |
| currentNrOfInstances | 1 | RO | Current number of direct child <contentInstance> resource in the <container> resource. It is limited by the maxNrOfInstances. | OA |
| currentByteSize | 1 | RO | Current size in bytes of data(i.e., content attribute of a <contentInstance> resource) stored in all direct child <contentInstance> resources of a <container> resource. This is the summation of contentSize attribute values of the <contentInstance> resources. It is limited by themaxByteSize. | OA |
| locationID | 0..1 | RW | An ID of the resource where the attributes/policies that define how location information are obtained and managed. This attribute is defined only when the <container> resource is used for containing location information. | OA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the child <contentInstance> resources of the present <container> resource (see note). | OA |
| retargetPointOfContact | 0..1 | RW | A point of contact that the Hosting CSE shall use when re-targeting <contentInstance> requests to an AE. This attribute shall be configured with a oneM2M compliant Resource-ID of an <AE> resource (e.g. AE01) along with an appended path of an AE resource to target (e.g. (e.g. sensor/temp). For example, AE01/sensor/temp Once configured, the value stored in this attribute shall remain private and only be accessible to the Hosting CSE and the creator of the <container> resource. | NA |
| NOTE: The access to this URI is out of scope of oneM2M. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.27	Resource Type latest

The <latest> resource is a virtual resource because it does not have a representation. It is the child resource of a <container> resource.

When a RETRIEVE request addresses the <latest> resource, the Hosting CSE shall first attempt to service the request using the latest <contentInstance> available.  If a <contentInstance> is not available or does not meet a specified filterCriteria (e.g. creationTime of the latest <contentInstance> available is older than required or expirationTime of the latest <contentInstance> available is earlier than required), then the Hosting CSE shall attempt to re-target the request if applicable.

The <latest> resource inherits access control policies that apply to the parent <container> resource.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

Removed in R02 version of contribution

### -----------------------End of change 3 -------------------------------------------

### -----------------------Start of change 4 -------------------------------------------

#### 10.2.22.1	Retrieve <latest>

This procedure shall apply to the latest <contentInstance> resource among all existing <contentInstance> resources in the parent <container> resource. If there is no <contentInstance> resource in the parent, then the Hosting CSE shall attempt to re-target the request.

Below is the detailed procedure for re-targeting of a RETRIEVE request to <latest>.

Originator sends a RETRIEVE request to a <latest> resource. Request may optionally include one or more filterCriteria conditions such as createdAfter or expirationAfter.  See clause 8.1.2 for the information to be included in the Request message.

Hosting CSE shall perform processing to determine whether to process request using locally hosted <contentInstance> or re-target the request to be processed.  When a RETRIEVE request addresses the <latest> resource, the Hosting CSE shall first attempt to service the request using the latest <contentInstance> available.  If a <contentInstance> is not available or does not meet the specified filterCriteria (e.g. creationTime of the latest <contentInstance> available is older than required or expirationTime is earlier than expected), then the Hosting CSE shall attempt to re-target the request if the retargetPointOfContact is configured.  If re-targeting is performed, the Hosting CSE shall send the request to the retargetPointOfContact and receive corresponding response back from Receiver.  Hosting CSE shall re-target response back to the Originator.

Receiver The Receiver performs local processing to verify the existence of requested resource.  After successful verification, the Receiver shall return a <contentInstance> representation, otherwise an error indication shall be returned.

Figure 10.1.2-1: Procedure for Retargeting a RETRIEVE <latest>

Step 001: The Originator shall send RETRIEVE request targeting a <latest> resource.  Originator shall send mandatory parameters and may send optional parameters in Request message for RETRIEVE operation as specified in clause 8.1.2.

Step 002: The Hosting CSE shall first attempt to service the request using the latest <contentInstance> available, and based on the same procedures defined in clause 10.2.19.3 for a <contentInstance> RETRIEVE.  If a <contentInstance> is not available or does not meet the specified filterCriteria, then the Hosting CSE shall attempt to re-target the RETRIEVE request if the retargetPointOfContact attribute is configured in the parent <container>.

Step 003: The Hosting CSE shall send a re-targeted RETRIEVE request to the retargetPointOfContact.

Step 004: The Receiver processes the RETRIEVE request

Step 005: The Receiver shall respond to Hosting CSE with a response formatted as a <contentInstance> with mandatory parameters and may send optional parameters in the response message for RETRIEVE operation as specified in clause 8.1.3.

Step 006: The Hosting CSE shall process the received re-targeted RETRIEVE response.   If the response includes a properly formatted <contentInstance>, the Hosting CSE shall create a <contentInstance> and store the response information.

Step 007: The Hosting CSE shall respond to Originator with a response formatted as a <contentInstance> with mandatory parameters and may send optional parameters in Response message for RETRIEVE operation as specified in clause 8.1.3.

General Exceptions:

- The targeted resource/attribute in To parameter does not exist. The Hosting CSE or Receiver responds with an error.

- The Originator does not have RETRIEVE privileges to retrieve information stored in the resource on the Hosting CSE or privileges for request to be re-targeted to retrieve information stored in the resource on the Receiver. The Hosting CSE responds with an error.

### -----------------------End of change 4 -------------------------------------------