| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 22 |
| Source:* | Catalina Mladin , InterDigital Communications |
| Date:* | 2015-03-06 |
| Contact:* | Catalina.Mladin@InterDigital.com |
| Reason for Change/s:* | Provide context for group messaging features for 3GPP Rel-13 IWK. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 v0.2.0 |
| Clauses/Sub Clauses* | New clause 8.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add new section 8.3 of TR-0024 3GPP Rel13 IWK (WI-0037) for the Group Messaging feature.

R01 has template updates

### -----------------------Start of change 1-------------------------------------------

### 8.x  Support for Group Messaging

### 8.x.1 Description

M2M deployments lends themselves to the use of group operations in many ways, from coordinated management to signalling reduction and resource utilization optimizations.  For example, in many M2M deployments it is desirable to charge devices as a group, send messages to a group, trigger groups of devices, and monitor devices as a group.

The Group Messaging feature is intended to efficiently distribute the same content to the members of a group. 3GPP has considered several solutions for implementation, including the use of cell broadcast, MBMS and via PDN connections. The 3GPP Release 13 procedure makes se of MBMS for group message delivery and may be re-used for general group message delivery purposes (not limited to MTC devices). The group message delivery using MBMS has limited applicability and does not support all the scenarios, e.g. UEs not supporting MBMS, UEs located in areas where MBMS is not deployed. The feature involves the use of MBMS entities such as BM-SC (Broadcast Multicast Service Centre) to allocate a TMGI (Temporary Mobile Group Identity) for a specific MBMS user service.

### 8.x.2	3GPP Release-13 MTC procedure

oneM2M uses the 3GPP Release-13 MTC feature for Group Messaging, which involves message delivery using MBMS. For that purpose the IN-CSE uses the oneM2M group management feature to define a 3GPP-external group. It also uses communications over the mcn interface to authorize the originator of a group messaging procedure and for allocation of an external temporary group identifier, which is then used in group message delivery within the Underlying Networks.

A signalling sequence for Group Message delivery is described in the sub-clause 5.5 of 3GPP TS 23.682 [i.5]. Figure 8.3.5-1 provides the signalling sequence derived from the 3GPP specification with oneM2M terminologies mapping. (TS 23.682 [i.14] fig 5.5.1-1 )

Figure 8.x.5.-1 Group message delivery using MBMS

3GPP TS 23.682 [i.5] describes group message delivery using MBMS as follows

NOTE 1:	Steps 1-5 can be skipped if a valid TMGI allocation already exists or if the MBMS bearer activation is performed without TMGI pre-allocation.

NOTE 2:	The interactions between the SCEF and the SCS/AS (in steps 1, 4, 6, 11 and 13) are outside the scope of 3GPP and are shown for informative purposes only.

1.	If there is no assigned TMGI for an External Group Id, the SCS/AS sends the Allocate TMGI Request (External Group ID, SCS Identifier) message to the SCEF. The SCS/AS may determine the IP address(es)/port(s) of the SCEF by performing a DNS query using the External Group Identifier or using a locally configured SCEF identifier/address. The SCEF checks that the SCS/AS is authorized to request TMGI allocation.

2.	The SCEF determines whether the SCS/AS is authorized to request TMGI allocation.

NOTE 3:	The authorization of TMGI allocation for the group and acquisition of the BM-SC routing information are not specified in this release of the specification.

3.	The SCEF initiates TMGI allocation by the BM-SC (see TMGI Allocation Procedure specified in TS 23.468 [30]).

4.	The SCEF sends the received TMGI and expiration time information to the SCS/AS.

NOTE  4:	The SCEF may cache the serving BM-SC Identity information and mapping between External Group ID and TMGI.

5.	Application level interactions may be applied for the devices of specific group to retrieve the related MBMS service information, e.g. TMGI, start time. Application level interactions between the UE and the SCS/AS are out of scope of this specification.

6.	The SCS/AS sends the Group Message Request (External Group Identifier, SCS Identifier, location/area information, RAT(s) information, TMGI, start time) message to the SCEF. The location/area information indicated by the SCS/AS may be the geographic area information.

7.	The SCEF checks that the SCS/AS is authorised to send a group message request. If this check fails the SCEF sends a Group Message Confirm message with a cause value indicating the reason for the failure condition and the flow stops at this step. In this case, the SCS/AS may subsequently release the TMGI allocated at step 3 by requesting an explicit de-allocation, or may rely on the expiration timer.

NOTE 5:	Authorization of Group Message delivery using MBMS towards a specific group is not specified in this release of the specification.

8.	The SCEF sends an Activate MBMS Bearer Request (MBMS broadcast area, TMGI, QoS, start time) message to the BM-SC (see TS 23.468 [30]).

NOTE 6:	The SCEF maps between location/area information provided by the SCS/AS and the MBMS broadcast area for the distribution of the content to the group based on configuration in the operator domain. The SCEF needs to be aware that the selected MBMS broadcast area may result in broadcast of the content over an area larger than the area that may be indicated by SCS/AS.

9.	BM-SC performs the Session Start procedure (see MBMS Session Start procedure specified in TS 23.246 [29]).

10.	The BM-SC sends an Activate MBMS Bearer Response to the SCEF (see TS 23.468 [30]).

11.	The SCEF sends a Group Message Confirm (TMGI (optional), SCEF IP addresses/port) message to the SCS/AS to indicate whether the Request has been accepted for delivery to the group.

12.	Application level interactions may be applied for the devices of specific group to retrieve the related MBMS service information, e.g. TMGI, start time. Application level interactions between the UE and the SCS/AS are out of scope of this specification.

13.	At or after the requested start time, but before the expiration time, the SCS/AS transfers the content to be delivered to the group to the SCEF using the IP address and port received at step 11. SCEF delivers the contents to BM-SC via MB2-U, using the IP address and port received at step 9. The BM-SC transfers the corresponding content to UEs. To avoid that potential responses to the broadcast message by high numbers of devices are sent at almost the same time, the SCS/AS makes sure the UEs are provided with a response time window if it expects the UEs to respond to the delivered content.

NOTE 7:	Subsequent to this step, it is up to the SCS/AS if the MBMS bearers will be kept active and allocated and for how long. The mechanisms defined in TS 23.468 [30] can be used by the SCEF to release the MBMS resources.

14.	In response to the received content, the UE may initiate immediate or later communication with the SCS/AS.

NOTE 8:	The UE application ensures distribution of any responses within the response time window.

### 8.x.2  Parameters

This section provides information regarding the parameters necessary to accomplish the group messaging feature..

### 8.x.4  Proposed resource types and attributes

This section provides information of new resource types and new attributes including relationship with existing resource types and attributes.

### 8.x.3  Proposed flow

This section describes the general procedure for group message delivery using MBMS .

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?