| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#22 |
| Source:* | NEC |
| Date:* | 2016-03-14 |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Norio Uchida, NEC (TTC), n-uchida@cq.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Correction of Node-TP general procedure |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v2.7.0 |
| Clauses/Sub Clauses* | 8.3.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: ARC-2016-0015R02 : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is to correct the general procedure of Configuration Node Traffic Pattern based on the ARC21.1 through the ARC21.3 conferences, and e-mail discussions.

### -----------------------Start of change 1-------------------------------------------

#### 8.      8.3.5.3  	General procedure for Configuration of Traffic Patterns

Figure 8.3.5.3-1 below depicts a general procedure for configuration of Traffic Patterns.

Figure 8.3.5.3-1  General procedure for configuration of Traffic Patterns

Step-1: Provide information on the behavior of a field domain AE or field domain Node

An AE (IN-AE or an AE of the Field Domain Node that reports its communication behaviour) provides the hosting CSE (i.e. ASN/MN-CSE) of the field domain AE/Node with information on the communication behaviorof the AE/Node (i.e. TP parameter sets) by creating, updating or deleting its Traffic Patterns (TP).

The AE may provide TP parameter sets for a group of field domain nodes .

The request shall include

- the originator AE-ID of the requesting AE,

- a target identifier: i.e. the <trafficCharacteristics> child resource of a <node> resource or an <AE> resource of the field domain node or a group identifier of multiple field domain AEs/Nodes for which the Traffic Patterns is provided, and

- a set of TP parameters  as indicated in table 8.3.5.2-1.

The request may include multiple of TP parameter set(s) and validity time(s).

If the hosting CSE has received a request from an AE to create, update or delete Traffic Patterns it shall check if the request from the AE is valid (Note-1).

Note-1: Apart from checking access rights of the AE the validation of the request from the AE could include:
 - Consistency with <schedule> resources supported by an M2M SP in various M2M entities (MN-CSE, ASN)  hosting this AE/Node
 - If there are several TP parameter sets active for one Field Domain Node, then the original resource hosting CSE needs to ensure that the different TP parameter sets are not overlapping.

Step-2: Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

If the hosting CSE recognizes an announcement procedure is needed, it shall announce the Traffic Patterns received from the AE to the IN-CSE that has an interface to the NSE contained in the “AnnounceTo” attribute of the Traffic Patterns resources based on the existing announcement procedures.

Step-3: Select the server NSE to request for the configuration of the TP parameter sets

If the IN-CSE receives announced Traffic Patterns and the IN-CSE recognizes that the configuration of the Traffic Patterns at the NSE is needed by checking the “provideToNSE” attribute, the IN-CSE shall perform the subsequent steps.
For the configuration of the TP parameter sets for a specific field domain node, the IN-CSE selects the NSE by using the identifier of the Field Domain Node (i.e. the M2M-Ext-ID) by which the Node can be identified in the NSE.

Note: The correct server NSE can be found by following of a chain of links of multiple resources in the IN-CSE, e.g. the nodeLink in the AEAnnc resource of a target AE of field domain node linking to the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE. (See sections 7.1.8 and 7.1.9)

Step-4: Request for the configuration of the TP parameter sets

For each field domain node received in the AE request the IN-CSE sends a request to provide TP parameter sets for the field domain node to the NSE, using the appropriate Mcn protocol. The request includes an identifier of the filed domain node and one or more TP parameter set(s) as defined at clause 8.3.5.2.

Note: If the Underlying Network is 3GPP-compliant, see Annex B for more details.

Step-5: Response for the configuration of the TP parameter sets

The IN-CSE receives the response for the configuration of the TP parameter sets from the NSE. The response includes the result of the request.

Note: If the Underlying Network is 3GPP-compliant, see Annex B for more details.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M TS-0002: " Requirements".

[i.2]	TR-069: "CPE WAN Management Protocol Issue": 1 Amendment 5, November 2013, Broadband Forum.

[i.3]	OMA-DM: "OMA Device Management Protocol", Version 1.3, Open Mobile Alliance.

[i.4]	LWM2M: "OMA LightweightM2M", Version 1.0, Open Mobile Alliance.

[i.5]	OMA-TS-MLP-V3-4-20130226-C: "Mobile Location Protocol", Version 3.4.

[i.6]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: "RESTful Network API for Terminal Location", Version 1.0.

[i.7]	IETF RFC 1035: "Domain names - Implementation and specification".

[i.8]	IETF RFC 3588: "Diameter Base Protocol".

[i.9]	IETF RFC 3596: "DNS Extensions to Support IP Version 6".

[i.10]	IETF RFC 3986: "Uniform Resource Identifier (URI): General Syntax".

[i.11]	IETF RFC 4006: "Diameter Credit-Control Application".

[i.12]	IETF RFC 6895: "Domain Name System (DNS) IANA Considerations".

[i.13]	GSMA-IR.67: "DNS/ENU Guidelines for Service Providers & GRX/IPX Providers".

[i.14]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications (Release 13)".

[i.15]	ETSI TS 132 240: "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Telecommunication management; Charging management; Charging architecture and principles (3GPP TS 32.240)".

[i.16]	ETSI TS 132 299: "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Telecommunication management; Charging management; Diameter charging applications (3GPP TS 32.299)".

[i.17]	3GPP2 .S0068: "Network Enhancements for Machine to Machine (M2M)".

[i.18]	JNI 6.0 API Specification: "Java Native Interface 6.0 Specification".

[i.19]	3GPP TS 23.401: "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access".

[i.20]	3GPP TS 23.402: "Architecture enhancements for non-3GPP accesses".

[i.21]	3GPP TS 23.060: "General Packet Radio Service (GPRS); Service description; Stage 2".

[i.22]	3GPP TS 22.368: "Service requirements for Machine Type Communications (MTC); Stage 1".

[i.23]	3GPP TS 23.003: "Numbering, addressing and identification".

[i.24]	Recommendation ITU-T X.660 | ISO/IEC 9834-1: "Information technology - Procedures for the operation of object identifier registration authorities: General procedures and top arcs of the international object identifier tree".

[i.25]	oneM2M TR-0008: "Analysis of Security Solutions for oneM2M System".

[i.26]	IETF RFC 4122: "A Universally Unique IDentifier (UUID) URN Namespace".

[i.27]	oneM2M Drafting Rules.

NOTE:	Available at http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc.

[i.28]	oneM2M TR-0007: "Study of Abstraction and Semantics Enablement".

[i.29]	3GPP TS 22.101: Service aspects; Service principles (Release 13).

[i.30]	3GPP TS 22.115: Service aspects; Charging and billing (Release 13).

[i.31]	3GPP TS 29.336: Home Subscriber Server (HSS) diameter interfaces for interworking with packet data networks and applications (Release 13).

### -----------------------End of Changes to References  -------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Mca

Infrastructure Domain

Field Domain

1. provide information on the behavior of a field domain node

2. Announce the Traffic Patterns to the contact of NSE

- Request for providing 
the TP parameter sets

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE

Any Domain

Mca

Infrastructure Domain

Field Domain

1. provide information on the behavior of a field domain AE or field domain Node

2. Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

- Request for providing 
the TP parameter sets

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE

Any Domain