²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP22.1 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-02-23 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | Capability to ease & to harmonize the way of identifying the Interworking Technology targeted by both <AE> resources and Content Sharing Resources (OIC targeted technology) |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0024 V0.3 |
| Clauses/Sub Clauses* | Clause 6. |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 -------------------------------------------------

### 6.2.2	OIC Device Representation

#### 6.2.2.1	Introduction

OIC Device provides the management and control functions for any M2M application. As such, the CSE that hosts the M2M Applications shall represent the OIC Device as a <AE> resource (OIC Device <AE> resource).  The OIC physical Device that hosts the logical OIC Device shall be represented as a <node> resource.

The properties carried by OIC Device (i.e. device type) shall be translated into the labels attribute of the <AE> Resource as separate entries with the following format:

- OIC-DT: Device Type (e.g. oic.d.light)

#### 6.2.2.2	OIC Device Identification

OIC Devices are identified by their “di” property as described in OIC Core Specification [3]. The “di” property is used as the AE-ID of the associated <AE> resource that represents the OIC Device.

In most deployment scenarios, OIC physical Devices host one (1) OIC Device. In this scenario the OIC physical Device’s <node> resource’s M2M-Node-ID should be the same as the “di” property. Also the deviceIdentifier attribute of <serviceSubscribedNode> resource should be same as the “di” property. When a OIC physical Device host’s more than one (>1) OIC Device, the determination of the <node> resource’s M2M-Node-ID is implementation specific. In all deployment scenarios, the <AE> resource is linked with the <node> resource as described in TS-001 [2].

As the OIC Device is represented as an <AE>  resource and a OIC Resource is represented as a Content Sharing Resource in the M2M Service Layer, a reference shall be made between the <AE> resource that represents the OIC Device and the Content Sharing Resources which represents the list of OIC Resources available in that OIC Server.

In order to identify interworked entities hosted in a CSE for the OIC technology described in this present document, the  <AE> resource that represents the OIC Device and the Content Sharing Resources which represent the OIC Resources, shall have a Iwked_Technology labels attribute set to OIC.

In addition the <AE> resource uses the Hierarchical and Non-Hierarchical mechanisms for Resource Addressing as defined in clause 9.3.1 of TS-001 [2] where the resourceName attribute of the <AE> shall be same as “di” property.

### ----------------------- End of change 1 -------------------------------------------------

### ----------------------- Start of change 2 -------------------------------------------------

## 6.3	OIC Resource Discovery

### 6.3.1	Introduction

OIC Server provides the information of supported OIC Resources to an OIC Client. The OIC IPE uses its OIC Client function to synchronize which OIC Resources are supported by the OIC Device and what is stored in the hosting CSE for the M2M Application representing the OIC Device. This clause specifies how discovered OIC Resources are translated to discoverable Content Sharing Resources along with the associated linkages to other resources.

### 6.3.2	OIC Resource Representation

#### 6.3.2.1	Introduction

OIC Server provides the list of supported OIC Resources, where information of each resource is specified in a oic-link format as specified in OIC Core specification [3]. The oic-link format contains information like the resource type, uri and interface.

Optionally other information can be carried by that list as the capability for all the OIC Resources in the OIC Server:

- a specific Content-Format (e.g. OIC JSON/ OIC CBOR Content-Format)

- time to live

For discovery of OIC Resources by M2M Applications, the properties carried by OIC Resources list (i.e. technology, resource type, uri, interface, optional content format, time to live) shall be translated into the labels attribute of the Content Sharing Resource as separate entries with the following format:

- Iwked-Technology:OIC

- Iwked-Entity-Type: Resource Type

- Iwked-Entity-ID: Resource URI (href)

- OIC-IF: Resource Interfaces

- Iwked-Content-Type: Supported Content Format (OIC default supported ContentFormat is CBOR. Others could be JSON, XML)

- OIC-TTL: time to live

For each OIC Resource discovered there will be a separate Content Sharing resource represented.

### -----------------------End of change 2 --------------------------------------------------