| CHANGE REQUEST |
| --- |
| Meeting:* | <ARC 23> |
| Source:* | ZTE |
| Date:* | 2016-05-06 |
| Contact:* | Qiuting Li, li.qiuting@zte.com.cn Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | Provide a solution for background transfer 3GPP Rel-13 IWK feature |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Ite number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 v0.3.0 |
| Clauses/Sub Clauses* | new |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add a new solution to clause 8.4.4 of TR-0024 3GPP Rel13 IWK (WI-0037) for the Background Data Transfer feature.

R01

Editorial correct.

R02

Editorial correct for Figure8.4.4.x.1-1and 8.4.4.x.2-1

### -----------------------Start of change 1-------------------------------------------

### 8.4.4 Solution(s)

#### 8.4.4.X SolutionX

##### 8.4.4.X.1 Proposed resource types and attributes

This clause provides information of new resource types and new attributes including relationship with existing resource types and attributes.

Proposed new resource types are as below.

- Resource Type <backgroundDataTransfer>

  - Note: It is child resource of existing Resource Type <AE> or <node>.

Detailed information of new resource types are described in subclause below.

###### 8.4.4.X.1.1 Resource Type <backgroundDataTransfer>

The <backgroundDataTransfer> resource represents the characteristics information (e.g. desired communication window, traffic policy, etc.) of a request for background data transfer and corresponding Underlying Network traffic policy. This information may be scheduled at application level processing. This resource type is used to share and negotiate information with other entities such as the underlying network entity (server NSE) which may optimize the background data transfer in the Underlying Network for AE/CSE.

Figure 8.4.4.x.1-1: Structure of <backgroundDataTransfer> resource

The <backgroundDataTransfer> resource  contains the child resources specified in table 8.4.4.x.1-1.

Table 8.4.4.x.1-1: Child resources of <backgroundDataTransfer> resource

| Child Resources of < <backgroundDataTransfer > | Child Resource Type | Multiplicity | Description | <backgroundDataTransfer > Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of TS-0001. | <subscription> |

The <backgroundDataTransfer> resource contains the attributes specified in table 8.4.4.x.1-2.

Table 8.4.4.x.1-2: Attributes of <backgroundDataTransfer> resource

| Attributes of <deviceCharacteristics> | Multiplicity | RW/ RO/ WO | Description | <backgroundDataTransferAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of TS-0001. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of TS-0001. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of TS-0001. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 of TS-0001. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of TS-0001. | NA |
| creator | 1 | WO | The AE-ID of the entity which created the resource. This can also be the CSE-ID of the IN-CSE if the IN-CSE created the resource. | OA |
| requestRefID | 1 | WO | A reference ID that is passed from the requester to IN-CSE and to the NSE in each request. The reference ID will be included in each response to associate it with the original request. | OA |
| volumePerNode | 1 | RW | Expected data volume for the background data transfer | OA |
| numberOfNodes | 1 | RW | Desired number of nodes for the background data transfer | OA |
| desiredTimeWindow | 1 | RW | Desired time window for the background data transfer | OA |
| possibleTrafficPolicies | 1(L) | RW | List of possible applicable transfer policies. Each policy may include a recommended time window, a charging rate and an aggregated maximum bitrate | OA |
| selectedTrafficPolicy | 1 | RW | If multiple polices are received from the Underlying Network, this attribute provides the one selected policy from the list of possible traffic policies. The policy may include a recommended time window, a charging rate and an aggregated maximum bitrate | OA |
| referenceID | 1 | RW | A reference ID that is offerd by the underlying network identies the traffic policy | OA |

##### 8.4.4.x.2 Proposed Flow

This clause describes the procedure for resource management of background data transfer to a set of field nodes based on AE’s request.

Figure8.4.4.x.2  below depicts a general procedure for configuration of traffic policy for background data transfer based on AE’s expection. The procedure needs to be harmonized with the Figure8.4.2-1and Figure8.4.2-2 of present document.

Figure 8.4.4.x.2-1: General Procedure for configuration of Background Data Transfer

Step-1 Request background data transfer configuration

An IN-AE requests IN-CSE negotiate with NSE in the Underlying Network to configure background data transfer by creating, updating or deleting a Background Data Transfer resource.

The request shall include:

the originator AE-ID of the requesting AE,

a target identifier: i.e. the <backgroundDataTransfer> child resource of a <node> resource or an <AE> resource of requesting AE.

a set of Background Data Transfer Parameters as indicated in table8.4.4.x.1-2.

If the IN-CSE has received a request from an IN-AE to create, update or delete Background Data Transfer  it shall check if the request from the IN-AE is valid

Step-2 Select NSE and Request background data transfer

The IN-CSE sends a request providing Background Data Transfer parameters to the selected NSE for negotiating background data transfer. The request shall include an identifier of the requestor, the volume of data expected to be transferred per node, the expected amount of nodes, the desired time window and optionally, network area information.

Note: The IN-CSE shall select any of available NSE before negotiation procedure, this is out of scope of this document.

Step-3 Traffic policy decision for Background data transfer

The Underlying Network shall determine one or more applicable transfer policies based on requesting Background Data Transfer parameters.

Step-4 Response for transfer policies

The NSE shall respond to the IN-CSE with one or more applicable transfer policies and a reference ID.

Each transfer policy shall include a recommended time window for the data transfer,and may provide  a maximum aggregated bitrate and the charging rate applicable for the given time window.

Step-5 Response for transfer policies provided by the Underlying Network

The IN-CSE update background Data Transfer resource based on NSE response, and return a response to originator AE with the applicable transfer policies and the referenceID from the Underlying Network.

Step-6 (optional) Inform selected transfer policy for background data transfer

If more than one transfer policy was received from the Underlying Network, the Originator AE needs to select one of them. It then updates the Background Data Transfer resource with the selected transfer policy.

Step-7 (optional) Response for the selected transfer policy

Once the IN-CSE received the selected transfer policy, it shall return a response to originator AE.

Step-8 Confirm the transfer policy

The IN-CSE shall inform confirmation for the transfer policy to the Underlying Network. If there was only one transfer offered in step-4, the IN-CSE shall respond a confirmation which means the transfer policy is known by originator AE. If more than one transfer policies was offered in step-4 and the originator AE selected one of them, the IN-CSE shall forward the selected transfer policy with the reference ID to the NSE as a confirmation.

Step-9 Store the confirmed transfer policy

The Underlying Network stores the new transfer policy and the reference ID based on the confirmation.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?