| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 23 |
| Source:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Norio Uchida, NEC (TTC), n-uchida@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Date:* | 2016-05-16 |
| Contact:* | Tetsuo Inoue, NEC (TTC), t-inoue@fp.jp.nec.com Norio Uchida, NEC (TTC), n-uchida@fp.jp.nec.com Ataru Kobayashi, NEC (TTC), a-kobayashi@df.jp.nec.com Joerg Swetina, NEC Europe Ltd. (ETSI), JoergSwetina@neclab.eu |
| Reason for Change/s:* | Correction of Traffic Pattern section: 1.) In the flow it is not sufficiently clear that an IN-AE may modify the communication patterns of a field domain node on behalf of that node. 2.) The text on consistency check, that was part of Note 1, had been wrongly formatted and could be misunderstood as normative text (outside of the Note). 3.) Corrected formatting of heading for Step 2. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI-0037 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v2.9.0 |
| Clauses/Sub Clauses* | 8.3.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR corrects the clause on Traffic Pattern:

- In the flow it is not sufficiently clear that an IN-AE may modify the communication patterns of a field domain node on behalf of that node.

- The text on consistency check, that was part of Note 1, had been wrongly formatted and could be misunderstood as normative text (outside of the Note).

- Corrected formatting of heading for Step 2.

### -----------------------Start of change 1-------------------------------------------

### 8.3.5	Configuration of Traffic Patterns

#### 8.3.5.1	Purpose of Configuration of Traffic Patterns

M2M devices that have predicable communication behaviour – e.g. in the form of repeating Traffic Patterns – can profit in terms of reduction of signalling, energy saving, fewer sleep/wake transitions, etc., when their Traffic Patterns are communicated to the underlying network.

For example, 3GPP devices could use new 3GPP power savings features such as eDRX (extended discontinuous reception) and PSM (Power Saving Mode) on LTE devices.

Also the underlying network can benefit from being informed about a device’s Traffic Patterns by the oneM2M System.

For example, if the IN-CSE knows the device’s Traffic Patterns and transmits them to an underlying 3GPP network, then this information can be used by a 3GPP network to set the device’s “Maximum Response Time” (3GPP Term) to tune the UE’s DRX and PSM parameters.

Thus the network will benefit because the UE will have fewer sleep/wake transitions and unnecessary signalling in the network can be avoided. Also, if the IN-CSE knows when the device is awake then data can be sent to the device exactly at the time when the device is listening, thus requiring the network to buffer less data for unavailable devices.

The purpose of the Configuration of Traffic Patterns feature is to provide a means to the oneM2M System  to inform the Underlying Network on parameters that can be used for optimizing the processing at the Underlying Network for a specific Field Domain Node. The feature includes the following functionalities:

An Application Entity (AE) or a Common Service Entity (CSE) shall be able to provide information on the communication behavior of a Field Domain Node (ASN or MN) to the underlying network.

To that purpose the AE or CSE shall be able to set Traffic Patterns of a particular Field Domain Node via the Mca or Mcc reference point of a IN-CSE:

The Field Domain Node is addressed using the (NodeID, AE-IDs) of the Node.

The IN-CSE shall in turn use the Mcn interface towards the Underlying Network to provide information on Traffic Patterns of a the Field Domain Node:

The IN-CSE uses the M2M-Ext-ID to identify the Node towards the Underlying Network.

#### 8.3.5.2	Traffic pattern parameters

Traffic pattern (TP) parameters can be associated with one or multiple field domain nodes and are defined in table 8.3.5.2-1.

A Field Domain Node can be associated with one or multiple sets of TP parameters. At any time only a single set of TP parameters can be associated with a Field Domain Node.

The IN-CSE shall assure that different TP parameter sets for a Node are not overlapping at any point in time.

A combination of the following parameters can be set.

Table 8.3.5.2-1: Traffic parameter set

| TP parameter set | Description |
| --- | --- |
| TP Periodic communication indicator | Identifies whether the Node communicates periodically or not, e.g. only on demand. |
| TP Communication duration time | Duration interval time of periodic communication [may be used together with TP Periodic communication indicator]. Example: 5 minutes. |
| TP Time period | Interval Time of periodic communication [may be used together with TP Periodic communication indicator]. Example: every hour. |
| TP Scheduled communication time | Time zone and Day of the week when the Node is available for communication. Example: Time: 13:00-20:00, Day: Monday. |
| TP Stationary indication | Identifies whether the Node is stationary or mobile. |
| TP Data size indication | indicates the expected data size for the pattern. |
| TP Validity time | The time after which aTP parameter becomes invalid once it had been set. |

#### 8.3.5.3	General procedure for Configuration of Traffic Patterns

Figure 8.3.5.3-1 depicts a general procedure for configuration of Traffic Patterns.

Figure 8.3.5.3-1: General procedure for configuration of Traffic Patterns

Step-1: An AE provides information on the communication behavior of a field domain Node to the IN-CSE that hosts the <node> resource of the field domain Node.

If the IN-CSE hosts the <node> resource of the field domain Node an AE (IN-AE or an AE of the Field Domain Node that reports its communication behaviour) provides that hosting CSE with information on the communication behavior of the Node. 
This is done by creating, updating or deleting the Node's Traffic Patterns (TP) which are contained in the trafficPatterns of the Node's trafficCharacteristics child-resource.

The AE may provide TP parameter sets for a group of field domain nodes.

The request shall include:

the originator AE-ID of the requesting AE;

a target identifier: i.e. the <trafficCharacteristics> child resource of the <node> resource of the field domain node or a group identifier of multiple field domain AEs/Nodes for which the Traffic Patterns is provided; and

a set of TP parameters as indicated in table 8.3.5.2-1.

The request may include multiple of TP parameter set(s) and validity time(s).

If the hosting CSE has received a request from an AE to create, update or delete Traffic Patterns, it shall check if the request from the AE is valid (note 1).

NOTE 1: Apart from checking access rights of the AE the validation of the request from the AE could include:
 - Consistency with other <schedule> resources supported of this Node (e.g. as contained in the Node's cmdhNwAccessRule).
 - If several TP parameter sets exist for one Field Domain Node, then ensure that the schedules of the different TP parameter sets are not overlapping.

Step-2: Select the server NSE for handling the TP parameter sets

If the IN-CSE receives a request to Create / Update / Delete Traffic Patterns and the IN-CSE recognizes that the handling (i.e. creation, update or deletion) of the Traffic Patterns at the NSE is needed by checking the “provideToNSE” attribute, the IN-CSE shall perform the subsequent steps.

For a specific field domain node the IN-CSE selects the NSE by using the identifier of the Field Domain Node (i.e. the M2M-Ext-ID) by which the Node can be identified in the NSE.

NOTE 2:	The correct server NSE can be found by following of a chain of links of multiple resources in the IN-CSE, e.g. the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE (see clauses 7.1.8 and 7.1.9).

Step-3: Request for the handling of the TP parameter sets

For each field domain node received in the AE request the IN-CSE sends a request to handling (i.e. creation, update or deletion) TP parameter sets for the field domain node to the NSE, using the appropriate Mcn protocol. The Mcn can correspond to one of standard interfaces specified by an external organization, for example, OMA RESTful Network API for Communication Patterns V1.0 [i.32]. The request includes an identifier of the filed domain node and one or more TP parameter set(s) as defined at clause 8.3.5.2.

NOTE 3:	If the Underlying Network is 3GPP-compliant, see Annex B for more details.

Step-4: Response for the configuration of the TP parameter sets

The IN-CSE receives the response for the configuration of the TP parameter sets from the NSE. The IN-CSE performs no further action upon the received response.

NOTE 4:	If the Underlying Network is 3GPP-compliant, see Annex B for more details.

### -----------------------End of change 1---------------------------------------------

# Text boxes

Infrastructure Domain

1. Create / Update / Delete Traffic Caharacteristics and related Traffic Patterns  of a field domain Node at the IN-CSE

3. Request to provide / delete 
Traffic Pattern parameter sets

4. Response

2. Select the NSE for handling the Traffic Pattern parameter sets

Mca

Mcn

IN-CSE

NSE

AE

Any Domain

Mca

Infrastructure Domain

Field Domain

1. provide information on the behavior of a field domain AE or field domain Node

2. Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

- Request for providing 
the TP parameter sets

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE

Any Domain