| CHANGE REQUEST |
| --- |
| Meeting:* | TP24 |
| Source:* | InterDigital |
| Date:* | 2016-07-11 |
| Contact:* | Dale Seed (dale.seed@interdital.com) Bob Flynn (bob.flynn@interdigital.com) Bhargavi Nagaraja Rao (BhargaviNagarajaRao.Chanakesapura@InterDigital.com ) |
| Reason for Change/s:* | Description of DISCOVERY as an operation |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V1.13.3 |
| Clauses/Sub Clauses* | 10.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add an entry to the Basic Procedures described in Section 10.1 to describe the  “Discovery” operation.

Currently DISCOVERY is described in terms of a modification of a RETRIEVE request. However there are specific permissions granting privilege to perform DISCOVERY as an operation.

This shall be useful in cases where operation types are to be specified for certain attributes like operationMonitor during <subscription> create or eventOperation type for <eventConfig> resource creation.

Currently, the spec has no provision to configure an event for discover operation as it qualifies under the RETRIEVE operation itself. But for use case scenarios where a discover operation triggers an event or statistic collection is required for only discover operations, there should be a way to add this information during the <eventConfig> create.

The same scenario applies for subscription where operationMonitor in eventNotification criteria can be discover operation.

With the proposed change, the scenarios detailed above can be achieved.

## ----------------------- Start of change 1 -----------------------

### 10.1.6	DISCOVERY

The DISCOVERY operation shall be used for discovering of resources residing on a CSE that match the provided Filter Criteria parameters.

Originator: The Originator requests to discover resources by specifying  the conditions in the filter criteria to limit the scope of the discovery results using the DISCOVERY method. See clause 10.2.6 for the information on the Discovery procedure

Receiver: The Receiver performs local processing to verify the existence of requested resource and checks privileges for discovering the information related to the resource. After successful verification, the Receiver shall return the requested information, otherwise an error indication shall be returned. Receiver operation is specified in clause 10.2.6.2

Figure 10.1.6-1: Procedure for Discovering Information

Step 001: The Originator shall send mandatory parameters and may send optional parameters in Request message for DISCOVERY operation as specified in clause 10.2.6.2.

Step 002: The Receiver shall verify the existence  (including Filter Criteria checking, if it is given) of the target resource and check if the Originator has appropriate privileges to discover the requested information.

Step 003: The Receiver shall respond with  mandatory parameters and may send optional parameters in Response message for DISCOVERY operation  as specified in clause 10.2.6.2.

General Exceptions:

- The targeted resource/attribute in To parameter does not exist. The Receiver responds with an error.

- The Originator does not have privileges to discover information stored in the resource on the Receiver. The Receiver responds with an error.

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?