| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#25 |
| Source:* | InterDigital, AT&T |
| Date:* | 2016-10-17 |
| Contact:* | Catalina Mladin, Catalina.Mladin@InterDigital.com Michael Starsinic, Michael.Starsinic@InterDigital.com James Hu, James.Hu@att.com |
| Reason for Change/s:* | Introduce descriptions for CIoT IP and non-IP data delivery |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <WI-0058> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 |
| Clauses/Sub Clauses* | 5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The goal of this contribution is to lay a foundation in TS-0026 so that work on Non-IP data delivery and 3GPP Interworking in general can proceed quickly.

This proposal populates Section 5 and 6.1 of TS-0026.

Section 5 is divided into 3 subsections.

- Section 5.1 introduces, at a high level, the interfaces that are offered by 3GPP for interworking.

- Section 5.2 shows, at a high level, how oneM2M functional entities tie into the interfaces that are exposed by 3GPP.

- Section 5.3 lists all of the CIoT features that are relevant to oneM2M.  It is intended that this TS will eventually have sections that correspond to each of the listed features.  The sections that describe each feature will detail how oneM2M can use the feature.

Section 6.1 describes the Control Plane Data Delivery features that 3GPP added in Rel-13.  There are sub-sections that describe each of the 3 Control Plane Data Delivery methods; Non-IP via the SCEF, Non-IP via the P-GW, and IP via the P-GW.  Each subsection highlights important points that should be considered when attempting to use the feature in a oneM2M system.

Although other standards bodies (i.e. OMA) may develop the API’s that are used to acces the NIDD feature.  oneM2M still needs to develop a stage 3 binding of the Mca and Mcc reference points to non-IP.  In order to delveop this bdining to NIDD, several key open issues need to be addressed. The notes included identify these issues, highlighting stage 2 issues (e.g. use of PoA)  and stage 3 issues (e.g. support for NIDD data via oneM2M protocol).  How the Mca and Mcc reference are bound to the Non-IP is left FFS.

Open Issues:  The Notes that are listed in this CR and the features and services that are listed in section 5.3 are items that need to be addressed in this TS.

R01 shows consensus from online and offline discussions on section 5.

R02 retains consensus on section 5 Section 6 content will be submitted as contribution to TR-0024

### -----------------------Start of change 1-------------------------------------------

# 5	oneM2M Architecture for 3GPP cellular IoT interworking with oneM2M

## 5.1	 Introduction

This document introduces a baseline architecture for supporting 3GPP interworking and 3GPP CIoT features such as IP and non-IP data Control Plane Data Delivery. It describes how the oneM2M system may leverage the IoT related features and services that 3GPP added in releases 10 through 13.  Features and services may be accessed by an ADN-AE, MN-CSE, or an ASN-CSE that is hosted on a UE, an IN-CSE that is able to access services that are exposed by a mobile network operator.

Figure 5.1-1 shows, at a high level, how 3GPP interfaces with external entities.  A more detailed picture can be found in 3GPP TS 23.682.

The Service Capability Server (SCS) is a 3GPP term that refers to an entity which connects to the 3GPP network to communicate with UEs used for MTC and the MTC-IWF and/or SCEF.  The SCS offers services to MTC Applications that are hosted on the UE or in an Application Server (AS).

In addition to connecting to the 3GPP though the SGi (IP based data plane) interface, the SCS connects to the 3GPP network via the MTC Interworking Function (MTC-IWF) and/or the Service Capability Exposure Function (SCEF).  Both the MTC-IWF and SCEF are described 3GPP TS 23.682 [2].

The MTC-IWF offers a single service to the SCS; device triggering via SMS.  This service is accessed via the Tsp Reference point which is a Diameter based interface.

The SCEF offers multiple services to the SCS.  These services are accessed via an API exposed by the SCEF.  The API is not defined by 3GPP.  The API maybe defined by other standardization bodies or it may be customized by the SCEF operator.  OMA has standardized APIs that may be used to access some of the exposed services, e.g. Communication Patterns [3].

The SCEF and MTC-IWF may be co-located.  In this type of deployment, the Tsp interface would not be exposed to the SCS; SMS device triggering functionality would be exposed to the SCS by the SCEF via API.

MTC Applications on the UE interact with the 3GPP network via 3 different interfaces.  MTC Applications may use the 3GPP network to send IP packets to and from the SCS and/or other MTC Applications.  SMS device triggers may be received by MTC Applications that are hosted in the UE.  Also, NAS messaging may be used to send and receive non-IP data, send and receive IP data, configure power savings mode, configure extended idle mode DRX, configure low priority indicators, etc.

Figure 5.1-1: 3GPP IoT Related Interfaces

## 5.2	Functional mapping between 3GPP and oneM2M

Figure 5.2-1 is an updated version of Figure 5.1-1.  This figure has been updated to show, at a high level, how oneM2M functional entities may access the features and services that are exposed by 3GPP.  The oneM2M entities are shaded in grey.

The “MTC Applications” that are hosted on the UE correspond to oneM2M entities which may be ADN-AE, MN-CSE, or ASN-CSE, or the UE may host a noDN. The SCS may be an IN-CSE, and the “MTC-Applications” or ASs that are hosted in an external network may be an IN-AE.

The “3GPP Trust Domain” box in Figure 5.1-1 and Figure 5.2-1 captures the functional entities that MUST be part of the 3GPP trust domain. Although Figure 5.1-1 and Figure 5.2-1 show that the IN-CSE and IN-AE are outside of the 3GPP Trust Domain, it should be noted that the IN-CSE can be part of the operator trust domain.

Figure 5.2-1: oneM2M Interfaces to the 3GPP Network

Several implementation options for the placement of the oneM2M (IN) CSE relative to the SCEF and the 3GPP network are envisioned. In all implementations, the SCEF always resides within 3GPP domain.

In some options the IN-CSE and the SCEF are deployed by a mobile network provider and are both part of the operator’s trust domain.

In other options the SCEF is part of the 3GPP trust domain and the IN-CSE is not part of the operator’s trust domain.

In all options, services within the IN-CSE may access the services that are exposed by the SCEF via the API.

## 5.3	Cellular IoT Features and Services

The SCEF exposes the following services to the IN-CSE.  This document describes how the IN-CSE may access each service.

  - Configuring Communication Patterns, see section 6.6.

  - Configuring Session QoS, see section 6.9.

  - Configuring Session Sponsorship, see section 6.11.

  - Background Data Transfer, see section 6.10.

  - Monitoring, see section 6.4.

  - High Latency Communication – Extended S-GW and SCEF Buffering, see section 6.3.

  - High Latency Communication – Configuring PSM and eDRX, see section 6.3.

  - Mobile Core Network Issue Reports, see section 6.8.

  - SMS Based Device Triggering, see section 6.5.

  - Group Messaging (via MBMS), see section 6.7.

  - Non-IP Data Delivery, see section 6.1.1.

A UE hosted ADN-AE, MN-CSE, or ASN-CSE may access the following features that may be exposed by the 3GPP modem.  This document describes how the UE hosted ADN-AE, MN-CSE, or ASN-CSE may access each service.

- SMS Based Device Triggering, see section 6.5.

- Group Messaging (via MBMS), see section 6.7.

- Non-IP Data Delivery, see section 6.1.1.

- Configuring Low Access Priority Connections, see section TBD.

- High Latency Communication – Configuring PSM and eDRX, see section 6.3.

- User Plane CIoT Optimizations (Suspend / Resume), see section TBD.

### -----------------------End of change 1 ------------------------------------------

### ----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[2] 3GPP 23.682 Architecture enhancements to facilitate communications with packet data networks and applications; (Release 14)

[3] OMA-TS-REST-NetAPI-CommunicationPatterns-V1-0: '"RESTful Network API for Communication Patterns'", Version 1.0, Open Mobile Alliance.

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?