| CHANGE REQUEST |
| --- |
| Meeting:* | ARC25 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-10-08 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* |  |
| CR against: Release* | Three |
| CR against: WI* | Active WI-0050 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* |  |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Currently <locationPolicy> is the resource indicating how the location of a device is obtained and where the location information is stored.

<locationPolicy> resource can only be the child resource of <CSEBase>, which means devices with <CSEBase> could indicate how to obtain location information and where to store it.

For those devices like ADN or NoDN, there is no way to indicate the location policy.

However, in M2M, it’s frequently used to indicate the location of ADN or NoDN. Especially, ADN is the most widely used node type in oneM2M, it would be a problem if we cannot indicate the location policy of ADN.

There are some other requirements to indicate the location policy of NoDN in the area network. For example, location of a NoDN may be shared based, the source of the location maybe the Middle Node itself. The approximity of the location depends on the type of the area network. For example, bluetooth is 30 meters, wifi is 100 meters.

To solve this problem, there are two options:

Option 1: Add <locationPolicy> as child resource of <AE> resource and <node> resource and clearly indicate that the for IN, MN and ASN, the location policy is stored under the <CSEBase>. For ADN, location policy is stored under the <AE>. For NoDN, location policy is stored under the <node>. But this is an inconsistent behaviour without any particular reason.

Option 2: Add <locationPolicy> as child resource of just <node> resource and remove the others. In this case, no matter which kind of node it is, the location policy is always stored under <node> resource. The problem of this approach is backward compatibility.

### -----------------------Start of change 1-------------------------------------------

### To be filled after the decision on the options provided above.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?