| CHANGE REQUEST |
| --- |
| Meeting:* | ARC25 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-10-08 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | See introduction part of the CR |
| CR against: Release* | Three |
| CR against: WI* | Active WI-0034 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0020 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The proposed contribution provides a TCC solution that is widely used in RESTful architecture for distributed transaction.

### -----------------------Start of change 1-------------------------------------------

### 6.1.4	TCC (Try confirm cancel)

# Figure 6.1.4-1: TCC method

In the TCC method, the transaction is composed of three phases.

In the Try phase, the application tries to update resources distributed on different servers. In the update request, the application provides an expiration time. The server then checks if the server can perform the request. If the checking is successful, the server responds an successful response and goes into reserved state. Otherwise, the server rejects the request. In case the server hasn’t received any confirm request in the reserved state, the server goes back to Initial state after timeout.

In the Confirm phase, if application finds that all servers related to the distributed transaction has successfully went into reserved state, the application sends confirm message to all the servers. Upon receiving the confirm message, the server make change to the resource and goes into final state.

In the Cancel phase, if any of the server rejects in the try phase and the application determined to abandon the transaction, the application simply bypasses the confirm phase. If the server doesn’t receive any confirm message during the expiration time, the server cancels the transaction automatically.

The benefit of TCC method is that the server doesn’t need to wait for the abort message if anything happened in the transaction. But the server still need to keep a reserved state for the successful execution of a transaction.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?