| CHANGE REQUEST |
| --- |
| Meeting:* | ARC26 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-11-25 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | See introduction |
| CR against: Release* | Three |
| CR against: WI* | Active WI-0034 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0020 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution provides potential solution in oneM2M to support transaction.

### -----------------------Start of change 1-------------------------------------------

## 8.1	Transaction

### 8.1.1	<transaction> resource

An <transaction> resource could be child resouce of any resource. It indicates that the parent resource is apart of a transaction. According to the information in the <transaction> resource, the parent resource is changed.

The <transaction> resource shall contain the child resources specified in table 9.6.5-1.

Table 9.6.5-1: Child resources of <transaction> resource

| Child Resources of <transaction> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 [i.2]. |

The <transaction> resource shall contain the attributes specified in table 8.1.1-1.

Table 8.1.1-1: Attributes of <transaction> resource

| Attributes of <transaction> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3[i.2]. |
| resourceID | 1 | RO | See clause 9.6.1.3[i.2]. |
| resourceName | 1 | WO | See clause 9.6.1.3[i.2]. |
| parentID | 1 | RO | See clause 9.6.1.3[i.2]. |
| expirationTime | 1 | RW | See clause 9.6.1.3[i.2]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3[i.2]. |
| creationTime | 1 | RO | See clause 9.6.1.3[i.2]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3[i.2]. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3[i.2]. |
| state | 1 | RO | The current state of the transaction. It could be Initial state: if the Hosting CSE hasn’t determined that the transaction can be executed or not. Reserved state: if the Hosting CSE has finished the checking and guaranteed the transaction can be executed at the given execution time. Final state: if the Hosting CSE has successful executed the transaction. |
| executionTime | 1 | RW | The intended execution time of the transaction. The Hosting CSE executes the primitive contained in the <request> child resource at the time specified by the attribute. |
| primitive | 1 | WO | The attribute is a complex data type that carries the primitive that is operated on the parent resource of the <transaction> resource. The primitive attribute includes information about the operation, originator, primitiveContent. |

### 8.1.2 Transaction handling

The following diagram show the flow how a transaction is commited in using <transaction> resource in oneM2M. In a transaction, one AE and multiple CSEs are involved. The AE need to coordinate transaction among multiple CSEs. An AE need to send operation to resource hosted on multiple CSEs. The AE requires the multiple CSEs either excute the operation successfully or none of them execute the operation.

Figure 8.1.2-1: Transaction procedure

Step 1: AE creats <transaction> resource as child resource to multiple resources according to the requirement of the service. The <transaction> resource contains the execution time of the transaction as well as the primitive to be executed. The execution time of different CSEs is the same to guarantee the commit of transaction is cooridinated. The primitive further contains the originator’s identity, the operation and the content of the primitive to be executed. The <transaction> resources to be created on different CSEs could be different.

Step 2: At each CSE that has received the <transaction> creation request, the CSE checks if the <transaction> can be successfully executed. The content of the checking may include the access right, the format of the primitive is correct, the execution can be performed at the specified time and other necessary criterias that are critical to the success of the primitive.

Step 3 (Success): If the checking is successful, the CSE responds created to the AE and make the parent resource of <transaction> resource into reserved state. In the reserved state, the resource will refuse any other request that will potentially break the affect the success of execution of the primitive at the specified execution time.

Step 4 (Success): At the specified execution time, the CSEs will individually execute their corresponding primitive.

Step 3 (Failure): If the checking at any one of the CSE has failed, the CSE responds a failed response to the AE. On receiving the failed response, the AE determines that the transaction cannot be commited any more, thus send delete <transaction> to those CSEs which have successfully created the <transaction> resource to cancel the transaction.

Step 4 (Failure): The CSE which has successfully created the <transaction> deletes the transaction.

Optional additional steps:

Step 3 (Failure): On receiving the failed response, the AE may decide if the <transaction> could be created again at the failed CSE according to the service. The re-creation of <transaction> should be within the time of the given execution time.

### 8.1.3	<transaction> Resource Procedures

#### 8.1.3.1	Create <transaction>

Table 8.1.2.1-1: <transaction> CREATE

| <transaction> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3[i.2] apply with the specific details for: Content: The representation of the <transaction> resource described in clause 8.1.1 |
| Processing at Originator before sending Request | According to clause 10.1.1.1[i.2] The Originator is the AE that coordinates the transaction according to the requirement of from the services. |
| Processing at Receiver | According to clause 10.1.1.1[i.2] The Receiver checks if the primitive in the <transaction> resource could be successfule executed at the given executionTime in the <transaction> resource. On successful check, the receiver responds OK to the originator. Otherwise, the request is rejected. |
| Information in Response message | All parameters defined in table 8.1.3-1[i.2] apply with the specific details for: Content: Address of the created <transaction> resource, according to clause 10.1.1.1[i.2] |
| Processing at Originator after receiving Response | According to clause 10.1.1.1[i.2] |
| Exceptions | According to clause 10.1.1.1[i.2] |

#### 8.1.3.2	Update <transaction>

Table 8.1.2.2-1: <transaction> UPDATE

| <transaction> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3[i.2] apply with the specific details for: Content: attributes of the <transaction> resource as defined in clause 8.1.1 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3[i.2] |
| Processing at Receiver | According to clause 10.1.3[i.2] |
| Information in Response message | According to clause 10.1.3[i.2] |
| Processing at Originator after receiving Response | According to clause 10.1.3[i.2] |
| Exceptions | According to clause 10.1.3[i.2] |

#### 8.1.3.3	Retrieve <transaction>

Table 8.1.2.3-1: <transaction> RETRIEVE

| <transaction> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | According to clause 10.1.2.[i.2] |
| Processing at Originator before sending Request | According to clause 10.1.2. [i.2] |
| Processing at Receiver | According to clause 10.1.2. [i.2] |
| Information in Response message | According to clause 10.1.2. [i.2] |
| Processing at Originator after receiving Response | According to clause 10.1.2. [i.2] |
| Exceptions | According to clause 10.1.2. [i.2] |

#### 8.1.3.4	Delete <transaction>

Table 8.1.2.4-1: <transaction> DELETE

| <transaction> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3[i.2] apply. |
| Processing at Originator before sending Request | According to clause 10.1.4.[i.2] |
| Processing at Receiver | According to clause 10.1.4. [i.2] |
| Information in Response message | According to clause 10.1.4. [i.2] |
| Processing at Originator after receiving Response | According to clause 10.1.4. [i.2] |
| Exceptions | According to clause 10.1.4. [i.2] |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?