## Slide 1: Group multicast
Group Name: ARC
Source: Jiaxin Yin, Huawei Technologies Co., Ltd. yinjiaxin@huawei.com
Meeting Date: 2016-10-17
Agenda Item: TBD

## Slide 2: Background
oneM2M does not support the utilizing multicast capability from the underlying network if supported. The underlying network could be 3GPP network or binding protocols like CoAP etc.
The discussion is to kick off the question how to support multicast group by oneM2M?
The contribution is the presentation show for ARC-2016-0455-group_multicast

## Slide 3: Multicast Group case1
CSE
ASN1
ASN2
ASN3
ASN4
ASN5
Group create request
Check Multicast capability one by one
All the group member have no multicast capability, the same with before: not subgroup
One Group, no multicast group

## Slide 4: Subgroup management case2
CSE
ASN1
ASN2
ASN3
ASN4
ASN5
Group create request
Check Multicast capability one by one
All the group member have the same multicast capability: 3GPP MBMS, there is one subgroup.
One multicast Group: 3GPP MBMS group

## Slide 5: Subgroup management case3
CSE
ASN1
ASN2
ASN3
ASN4
ASN5
One multicast group：3GPP MBMS multicast group
Group create request
Check Multicast Capability one by one
Part of the group member have multicast capability：MBMS; others do not.

## Slide 6: Subgroup management case4
CSE
ASN1
ASN2
ASN3
ASN4
ASN5
Multicast group 1：3GPP MBMS multicast
Group create request
Check Multicast Capability one by one
Some of the group member have multicast capability：MBMS; Some have the IP multicast capability.
Multicast group 2：IP multicast

## Slide 7: Resource structure
Group
multicastGroup
CSEbase
parentGroup
The <multicastGroup> resource is for the multicast of the group members. The multicastGroup contains a subset of the group members that belongs to one network and same multicast capability segment.
The <ParentGroup> resource is to indicate that if the CSE is part of a multicast group.
multicastAddress
memberList
fanOutURI
multicastAddress
memberList
fanOutURI
multicastType
responseURI

## Slide 8: Group create procedure
AE
IN-CSE
ASN1
ASN2
ASN3
ASN5
ASN4
Create group
Determines that ASN1,2,3 belongs to the same multicast group
Create multicast
Try to add itself into the multicast group
success
success
Allocate multicastAddress and fanOutURI

## Slide 9: Group fanout procedure
Case B: multicastType = IP Multicast
AE
IN-CSE
SCEF
MulticastServer
ASN1
ASN3
ASN2
Address fanout Req
Check the multicast group type
Send fanout message to the multiCastAddress
Success Rsp
Success Rsp
Case A: multicastType = 3GPP MBMS
Group message delivery using MBMS defined TS23682
Multicast using using the mapping between fanOutURI and memberIDs
Aggregate the member responses

## Slide 10
Questions and comments